HARDWARE REQUIREMENTS SPECIFICATION
for
6U VPX Zynq MPSoC and AFE7906 based Digital receiver Module with 12Channel 3GSPS ADC I/P 5MHz to 12 GHz I/P IBW 600MHz
DP-VPX-0227
Version 0.02
Release date 29.12.2023

Document Reference : DP-VPX-0227-000-HRS-0V03

Prepared by

Data Patterns (India) Limited.,
Plot No.H9, 4th Main Road,
SIPCOT IT Park, Siruseri,
Chennai - 603103

Copyright (2024) by Data Patterns

All rights reserved. These materials are confidential and proprietary to Data Patterns and no part of these materials should be reproduced or published in any form by any means, electronic or mechanical, including photocopy, on any information storage or retrieval system, nor should the materials be disclosed to third parties without the explicit written authorization of Data Patterns.

NAMING CONVENTION
The following naming convention is followed while giving the document reference number.
<PRODUCT_ID>-<FG>-<DOC_NAME>-<VERSION>. Where,

PRODUCT_ID	:	Denotes the product ID. For example – DP-SPL-5656

FG	:	Denotes the finished good number. Where,
For document common for all FGs - 000
For document configurable for individual FGs – 300, 600 etc.

DOC_NAME	:	Denotes the short form or acronym of document name.
For example : “HRS” for Hardware Requirements Specification

VERSION	:	Denotes version of the document. For example “1V00”

For example, document reference number :
Common FG - DP-VPX-0227-000-HRS-1V00
Individual FG - DP-VPX-0227-663-HRS-1V00

HARDWARE REQUIREMENTS SPECIFICATION
FOR
6U VPX Zynq MPSoC and AFE7906 based Digital receiver Module with 12Channel 3GSPS ADC I/P 5MHz to 12 GHz I/P IBW 600MHz
DP-VPX-0227

Document Title	Hardware Requirements Specification for 6U VPX Zynq MPSoC and AFE7906 based Digital receiver Module with 12Channel 3GSPS ADC I/P 5MHz to 12 GHz I/P IBW 600MHz DP-VPX-0227
Document Reference	DP-VPX-0227-000-HRS-0V03
Version Number	0V03 (eg; 1V00)
Version Date	29.12.2023
Prepared By	Name : Rajeshmani G / Sign :
Document Review By	Name : Devaguru V / Sign :
Technical Review By	Name : Ramesh M / Sign :
Approved By	Name : DRB / Sign :

AMENDEMENTS TO THE DOCUMENT
S. No.	Ver. No.	Ver. Date	Changed by	Section (s) Changed	Description / of Change
1	0V01	28.12.2023	Rajeshmani G	-	Initial Version
2	0V02	29.12.2023	Rajeshmani G	All sections	Internal Review comments
3	0V03	15.04.2024	Rajeshmani G	4,4.3.2,4.3.3,5.2.1,8 and Annexure C	DRB review comments

# INTRODUCTION

DP-VPX-0227 is the standard 6U VPX module consists of Zynq MPSoC in combination with Quad core ARM processor signal processing and AFE7906 based Digital receiver Module with 9Channel 3GSPS ADC Input frequency from 1320MHz +/-360MHz and Input IBW of 600MHz.On board power generator & sequencing shall be done from +12V and +5V. The module shall be a conduction cooled type with Ruggedizer.

## Scope

This document will explain how the requirements will meet through the specifications. The targeted audience is HDD. The task for HDD department is as follow, HDD : Preparation and Verification of HRS with respect to the requirement.

## Acronyms and Abbreviations

The acronyms and abbreviations used in this document are listed in the below Table 1.1.

Table 1.1 : List of Acronyms and Abbreviations

HRS	Hardware Requirements Specification
BID	Board ID
ID	Identification
PID	Project/ Product ID
SID	System ID
HRS	Hardware Requirement Specification
SYRS	System Requirement Specification
DDR	Double Data Rate
EEPROM	Electrically Erasable Programmable Read Only Memory
PCIe	Peripheral Component Interconnect Express
SATA	Serial AT Attachment
USB	Universal Serial Bus
ADC	Analog to Digital Converter
SPI	Serial Peripheral Interface
PLL	Phase Locked Loop
RF	Radio Frequency
IF	Intermediate Frequency
UART	Universal Asynchronous Receiver Transmitter
PL	Programmable Logic
PS	Processing System

## Referenced Documents

This section gives the external and internal documents referred to prepare this manual.

### External Documents

Table 1.2 : External Documents

### Internal Documents

Table 1.3 : Internal Documents

[SyRS]	System Requirements Specification for DP-RDR-7474, Data Patterns (India) Pvt. Ltd., DP-RDR-7474-600-SYRS-0V03, dd.mm.yyyy.

# MODULE OVERVIEW

DP-VPX-0227 is an 6U VPX 9-10GHz 9Channel Digital Receiver with integrated RF Down converter module, Zynq Ultrascale Plus re-programmable (MPSoC) hardware in combination with Quad core ARM processor for signal processing.

The Processing section (PS) operates with 64-bit Quad Arm core which performs the system management functionality. This Section shall have on board 32 Bit + 8Bit ECC DDR4 dynamic memories, two 64MB QSPI NOR flash for boot configuration, an EEPROM memory of 4KB via I2C interface to store the DDR4 memory configuration details, an eMMC NAND flash of 16GB for application and user storage and a 16Mbit MRAM for storing critical information.It shall provide USB3.0 (USB 2.0 Backward Compatible) and 1000Base-T Ethernet for Communication and 2x RS422 (or) 2x RS232 UART port for debugging purpose.

The Programmable Logics(PL) Section shall have on board 4GB 32bit DDR4 dynamic memory and an 128MB QSPI NOR flash for user storage. It shall have two RS232 UART port for communication purpose.One x8 PCIe interface,x4 10G ethernet and x4RIO interface to P1 connector then One x4 PCIe interface,x4 RIO interface to P2 Connector.Also one x4 10G ethernet to P4 Connector.One I2C interface to P0 connector.It consists of multi board sync input group such as Trigger,SOB and Sysref for ADC channels Synchronization.

This module have AFE7906 chip to handle nine number of 960MHz to 1680MHz input RF signals with 3GSPS sampling rate with JESD204B standard and also shall have a XMC Connector to connect with 9 Channel 9-10GHz Receiver Down converter board, IF OUT as 1320MHz with 360MHz Instantaneous BW DDC Piggy Module. This module shall have low noise on board clock generation and distribution section to provide jitter free Sampling Clock to RFADC, FPGA JESD Cores and Piggy Modules. This section shall also have a option of choosing internal and external reference clock.

On board Power Generator & Sequencing section shall be used for generation of all the power supplies in the module from +12V & +5V. This module shall have VPX P0 Connector for Power Supply, VPX P1 & P2 Connector all communication links and debugging interfaces and x24LVTTL or x12 LVDS in P2 and P4 for Field IOs. This module shall have a temperature sensor for monitoring the FPGA temperature.
The module shall be of conduction cooled type with Ruggedizer and wedge lock arrangement and comply 1” slot width dimensions.

Onboard power supply generation such as +5V,+6V,+3.5V,-5V for down converter module DP-CRF-7910 by using external +12V supply.

## Features

 The main features of DP-VPX-0227 module is given below:

- Zynq Ultra-scale Plus MPSoC from Xilinx
- One 32 Bit+8 Bit ECC 4GB DDR4 Memory from PS & 4GB 32 Bit DDR4 Memory from PL
- Two 14 bit 3GSPS ADC 9 channels with JESD204B Interface.
- One XMC Connector for DDC Piggy module DP-CRF-7910.
- 1 x8 PCIe interface to P1
- 1 x4 PCIe interface to P2
- 2 x1 PCIe/SATA interface
- 1 x1 USB 3.0 interface (USB 2.0 Backward Compatible)
- 1 x 1G 1000 Base-T RGMII interface from PS.
- 1 x 1G Base-T PS SGMII/PL RGMII interface
- 2 x RS422 interface or 4 xRS232.
- 2 x4 RIO1 to support 10G Ethernet
- 2 x4 10Gig Ethernet from PL.
- 28 Single-Ended IO (LVTTL/LVCMOS) or 12 Differential IO (LVDS) to P2 and P4 connector.
- On board clock generator section with Internal & External Reference
- On board Power supply generator & sequencer
- 9 Channel 3GSPS ADC input receiver.

## Applications

- Digital Receiver for RF signals.
- Data Communications.
- Signal Processing.
# BLOCK DIAGRAM

Figure 3.1 : Block Diagram of <DP-VPX-0227>
# SPECIFICATIONS

Table 4.1 : Specifications

DP-VPX-0227-HRS-001	Type	6U VPX (VITA 67.3 standard Compliant)
DP-VPX-0227-HRS-002	Zynq Ultrascale+ MPSoC	Part: XCZU11EG-2FFVC1760I / Zynq Ultrascale+ MPSoC / Part reference:XCZU11EG-2FFVC1760I / Processing System / APU- 64-bit Quad core Arm Cortex™-A53 upto 1.5GHz / RPU- Dual-core Arm Cortex-R5 / Arm v7-R Architecture (32-bit) upto 600MHz / Graphics Processing Unit (GPU) / Programmable Logic / CLB LUTs : 298K / Distributed RAM size: 9.1Mb / Block RAM size : 21.1Mb / DSP Slices : 2928 / No of HPIO : 416 / No of HDIO : 96 / No of GTH Transceiver : 32 / No of GTY Transceiver : 16 / GTH Transceiver speed : 10Gbps / GTY Transceiver speed : 25Gbps
INPUT AND OUTPUT SPECIFICATIONS
DP-VPX-0227-HRS-003	RFADC Specifications	MFR Part:AFE7906 / Nos. of Channels: Narrow Band channels: 1Nos. Wide Band Channel: 8Nos. Resolution: 14Bits Sampling Clock: 1800MHz input frequency: 1400 ± 2.5MHz (NB) 1320 ± 180MHz (WB) Input power at connector : 6.5dBm(Typ) DSA: 25dB in step of 0.5dB SNR: 50dBFs @ -3dBFs SFDR: 70DBc @ -3dBFs (WB) 80DBc @ -3dBFs (NB) Digital interface: x8 JESD lanes SPI for configuration
DP-VPX-0227-HRS-004	IO Interfaces	TTL I/O Signals / 162Nos. of TTL control lines to XMC connector for DDC module Interface. / LVDS/TTL I/O Signals / 24Nos. Of TTL or 12 Pairs of LVDS terminated to VPX connector for Field interface.
DP-VPX-0227-HRS-005	Synchronization Interfaces	1No. SOB & TRP LVDS pair from VPX. / 1No. Of TRIG-IN & TRIG-OUT LVDS pair to/from VPX. / 1PPS interface M-LVDS signal from VPX.
CLOCK SPECIFICATIONS
DP-VPX-0227-HRS-006	Reference clock Inputs	25MHz M-LVDS clock Reference from VPX. / 25MHz from XO – Reference Clock for Digital Clock Generation, RFPLL and Ethernet clock / 40MHz from XO – PS reference clock / 32.768 KHz - RTC reference clock / 156.25MHz from XO – for 10G Ethernet / External 1800MHz Reference clock input from SMPM to AFE for sampling clock. / External SYSREF input from SMPM to LMK PLL for distribution. / External FPGA Reference clock from VPX. / External SYSREF output to from LMK to VPX.
DP-VPX-0227-HRS-007	RF Clock Generation	Separate PLL & Distribution Circuitry shall be used for the generation of all the RF section clock such as / AFE Sampling Clock : 1800MHz / Sysref Clock to FPGA & RFADC : Upto 10MHz / GTY-PL Bank reference clocks for JESD204B interface upto 500 MHz
DP-VPX-0227-HRS-008	Digital Clock Generation	A separate PLL shall be used for the generation of digital clocks such as, / 4Nos. of 125MHz Reference clock for GTH-RIO and PLDDR4 interface. / 3Nos of 100MHz Reference clock for GTR-USB, PCIE and GTH PCIE interface. / 2Nos of 156.25MHz Reference clock for GTH-10G Ethernet interface. / 24MHz Reference clock for USB interface. / 40MHz Reference clock for PS interface.
MEMORY
DP-VPX-0227-HRS-009	DDR4	4GB 32Bit DDR4 +8 Bit ECC Memory Interfaced to PS side. 4GB 32Bit DDR4 Memory Interfaced to PL side.
DP-VPX-0227-HRS-0010	EMMC	16GB eMMC Nand Flash Memory for user storage
DP-VPX-0227-HRS-0011	NOR FLASH	2 x 128MB Quad SPI NOR Flash
DP-VPX-0227-HRS-0012	EEPROM	256Kbit EEPROM for Module Information storage
DP-VPX-0227-HRS-0013	MRAM	4Mbit MRAM for critical Information recording
COMMUNICATION
DP-VPX-0227-HRS-0014	High Speed-PS Section	2 Nos of x1 PCIE / SATA / 1Nos of USB3.0 / 1Nos of SGMII
DP-VPX-0227-HRS-0015	High Speed-PL Section	1Nos of x4 PCIE using Hard IP core. / 1Nos of x8 PCIE using Hard IP core. / 2Nos of x4 10G Ethernet to support 10G-Base KR, 10G Interfaces. / 2Nos of x4 RIO to support Aurora, SFPDP interfaces.
DP-VPX-0227-HRS-0016	Test & Debug port	4x RS232 / 2x RS422 on VPX P4 connector for communication purpose / 2Nos of 1000-Base-T Ethernet
INTERFACE / CONNECTORS
DP-VPX-0227-HRS-0017	Temperature Sensor	On board temperature Sensor via I2C interface to measure MPSoC Temperature.
DP-VPX-0227-HRS-0018	XMC Connector	162 TTL control lines for DDC module / Power Supply: / +5V,1.7A / +6V,2.8A / +3.5V,2A / -5V.0.06A
DP-VPX-0227-HRS-0019	VPX Connector	VPX Connector P0 / VS1,VS2=12V, VS3=5V, 3.3V_AUX (optional) / One I2C link from PS / One I2C link from PL / JTAG Interface / 25MHz REF Clock / 1PPS
		VPX Connector P2 / 1 x4 RIO from GTH / 1Nos of x4 PCIE from GTH. / x8 LVDS or x16 LVTTL IO’s. / 4 LVTTL IO’s. / Multi board sync signal such as TRIG-IN, TRIG-OUT,SOB,TRP and Sysref OUT. / External FPGA reference clock.
		VPX Connector P2 / 1 x4 RIO from PL to support (Aurora/SFPDP) IP core. / 1Nos of x4 PCIE from GTH bank using hardcore IP. / x8 LVDS or x16 LVTTL IO’s. / 4 LVTTL IO’s. / Multi board sync group such as Trigger,SOB,TRP,Sysref IN and Sysref OUT.
		VPX Connector P3 / 5x Analog Input signal for Down conversion. / 1x External Sysref reference clock for Onboard PLL.
		VPX Connector P4 / 2 Nos of x1 PCIE / SATA from GTR. / 1Nos of USB3.0 from GTR. / 1Nos of SGMII from GTR. / 2Nos of 1000-Base-T Ethernet / x4 LVDS or x8 LVTTL IOs. / x2 RS422 or x4 RS232
		VPX Connector P6 / 4x Analog Input signal for Down conversion / 1x External Reference clock for ADC Sampling. / 1x External LO input to DDC piggy module.
DP-VPX-0227-HRS-0020	JTAG Header	JTAG header is used for FPGA programming
DP-VPX-0227-HRS-0021	I2C Header	ADM and SI5332 Digital PLL programming header.
DP-VPX-0227-HRS-0022	RF Connector	9x SMPM connectors for ADC analog inputs / 1x SMPM connector for External Clock Reference. / 1x SMPM connector for External Sysref Clock Reference.
SOFTWARE SUPPORT
DP-VPX-0224-HRS-0023	Device Drivers	Device drivers for all standard interfaces in PS section supported by BSP. / Device Drivers for all PL related peripheral Interfaces.
DP-VPX-0224-HRS-0024	OS	Petalinux
POWER REQUIREMENTS
DP-VPX-0227-HRS-0025	Voltag	VS1,VS2=12V, VS3=5V, 3.3V_AUX (optional)
DP-VPX-0227-HRS-0026	Current	10.5A@12V(Max)
DP-VPX-0227-HRS-0027	Power Dissipation	126W@12V (Max)
MECHANICAL
DP-VPX-0227-HRS-0028	Dimension (LxBxH) in mm	233.35mmx160mmx25.23mm
DP-VPX-0227-HRS-0029	Weight in gm	<1.3Kg
ENVIRONMENTAL
DP-VPX-0227-HRS-0030	Operating Temperature	-40ºC to +71ºC
DP-VPX-0227-HRS-0031	Storage Temperature	-55ºC to +90ºC
DP-VPX-0227-HRS-0032	Relative Humidity	95% RH
DP-VPX-0227-HRS-0033	Commercial / Rugged	Rugged
DP-VPX-0227-HRS-0034	Thermal Dissipation	Conduction Cooled

(If applicable, specification statements shall be elaborated)
Note :
(1) – USB 2.0 interface can be used as either Standalone USB2.0 interface or combined with USB3.0 interface.

## Specification Statement – Type
Requirement ID :DP-VPX-0227-HRS-001
This module shall be 6U VPX based module compliant with VITA 67.3 standard.

## Specification Statement – Zynq Ultrascale+ MPSoC
Requirement ID :DP-VPX-0227-HRS-002
This module shall have one Zynq Ultra-scale+ (MPSoC) FPGA with following specifications.
Section	Parameters	Specifications
PS Section	Application Processor Core	Quad-core ARM® Cortex™-A53 MPCore™ up to 1.5GHz
	Real-Time Processor Core	Dual-core ARM Cortex-R5 MPCore™ up to 600MHz
	Graphics Processing Unit	Mali™-400 MP2 up to 667MHz
	Dynamic Memory Interface	x32: DDR4 with x8 ECC
	Static Memory Interfaces	2x Quad-SPI
	High-Speed Connectivity	PCIe® Gen2 , USB3.0, SATA 3.1
	General Connectivity	1xUSB 2.0, 1x eMMC, 2x UART, 2x I2C, 1x SPI
	PS-GTR_6 Gbps	4
	PS IOs	214
PL Section	System Logic Cells (K)	653,100
	CLB Flip-Flops (K)	597,120
	CLB LUTs (K)	298,560
	Max. Distributed RAM (Mb)	9.1
	Total Block RAM (Mb)	21.1
	UltraRAM (Mb)	22.5
	Clock Management Tiles (CMTs)	8
	DSP Slices	2928
	GTH 12.5Gb/s Transceivers	32
	GTY 25Gb/s Transceivers	16
	HD IOs (1.2V- 3.3V)	96
	HP IOs (1V to 1.8V)	416

## Specification Statement – Input and Output Specifications
### RF ADC Specifications
Requirement ID :DP-VPX-0227-HRS-003
- This module shall have two ADCs called as (AFE1 and AFE2). AFE1 ADC shall have 5 channels and AFE2 ADC shall have 4 channels with differential analog input from RF Balun.
- Narrow Band channels: 1Nos and Wide Band Channel: 8Nos.
- RF input frequency:
  - 1400 ± 2.5MHz (Narrow Band)
  - 1320 ± 180MHz (Wide Band)
- ADC resolution: 14bit
- ADC input level : 6.5 dBm (Typ)
- Digital Step attenuation(DSA) settings 25dB in step of 0.5dB.
- ADC Sampling Clock: 1800MHz
- Digital Data Interface: JESD204B with a maximum data rate of upto 9 Gbps.
- 8 SerDes transmitters up to 29.5 Gbps(Chip capability)
- RF input frequency range 5 MHz - 12 GHz(Chip capability)
- x3 SPI per chip for configuration.
### IO Interfaces
Requirement ID :DP-VPX-0227-HRS-004
- This module shall have 162 Nos of TTL IO’s control lines for digital attenuator to XMC connector for DDC piggy module.
- 24Nos. Of TTL or 12 Pairs of LVDS terminated to VPX connector for Field interface.

### Synchronization Interfaces
Requirement ID :DP-VPX-0227-HRS-005
- 1No. SOB & TRP LVDS pair from VPX.
- 1No. Of TRIG-IN & TRIG-OUT LVDS pair to/from VPX.
- 1PPS interface M-LVDS signal from VPX.

## Specification Statement – Clock Requirements
### Reference Clock

Requirement ID :DP-VPX-0227-HRS-006

This module shall have the following clocks mentioned below in the Table 4.2 : On board Clock split up.
Table 4.2 : On board Clock split up
S.No	Clock	Clock receiving/distribution section
1	25MHz M-LVDS clock Reference from VPX or 25MHz TCXO	Reference Clock for Digital Clock Generation, RFPLL and Ethernet clock
2	40MHz TCXO	PS Reference Clock
3	32.768KHz Crystal	RTC Reference Clock
4	156.25MHz Clock	10G Ethernet Clock
5	External 1800MHz Clock input(Optional)	AFE1 and 2 sampling clock
6	External Sysref input(Optional)	LMK04828 PLL Sysref distribution
7	External FPGA Reference clock(Optional)	Reference clock input for FPGA
8	External Sysref output to VPX Connector (Optional)	Generated by internal PLL LMK04828

Note: Separate PLL External reference clock of 1800MHz is available from VPX coax connector to RF PLL for ADC sampling clock and SYSREF generation.

### Digital Clock Generation

Requirement ID :DP-VPX-0227-HRS-007

- This module shall have a Programmable PLL to generate the below Digital Clock as mentioned below,
  - 4Nos. of 125MHz Reference clock for GTH-RIO and PLDDR4 interface.
  - 3Nos of 100MHz Reference clock for GTR-USB, PCIE and GTH PCIE interface.
  - 2Nos of 156.25MHz Reference clock for GTH-10G Ethernet interface.
  - 24MHz Reference clock for USB interface.
  - 40MHz Reference clock for PS interface.
### RF Clock Generation

Requirement ID :DP-VPX-0227-HRS-008

- This module shall have a separate PLL & Distribution Circuitry shall be used for the generation of all the RF section clock such as,
- RFADC Sampling Clock : Upto 1.8 GHz
- GTY Bank reference clocks for PL Section JESD204B interface upto 216 MHz
- GTH Bank reference clocks upto 200MHz.
- SYSREF clock of upto 10 MHz for both RFADCs & FPGA JESD204B interface.
Input Reference Clocks	Generated Ouput Clocks
1) 25MHz from TCXO (or) 10MHz External Clock / 2) 100MHz from VCXO	RFADC Sampling Clock – 2 Nos	Upto 1.8GHz
	RFADC SYREF Clock – 2 Nos	Upto 10 MHz
	RFADC GTY Bank Reference Clock -4 Nos	216 MHz
	GTH Bank Reference Clock -1 Nos	200 MHz
	GTY Bank Sysref Clock – 3 Nos	10 MHz
	SYSREF Clock to FPGA – 2 Nos	Upto 10 MHz

## Specification Statement – Memory

### DDR4 memory

Requirement ID :DP-VPX-0227-HRS-009

- This Module shall have one 32 Bit (+8 Bit ECC) 4GB DDR4 SDRAM Controller with Data Rate of 2400 MT/s from PS Section.
- This Module shall have one 32 Bit 4GB DDR4 SDRAM Controller with Data Rate of 2400 MT/s from PL Section.

### Configuration Flash

Requirement ID :DP-VPX-0227-HRS-0011

This module shall have 128MB(dual parallel 64MB) Quad SPI NOR Flash memory for booting process.

### User Flash

Requirement ID :DP-VPX-0227-HRS-0010
- This module shall have 16GB eMMC NAND Flash memory which shall be used for storing Device tree, File system & User defined application.
- It shall also have 128MB Quad SPI NOR Flash memory for user storage.

### EEPROM

Requirement ID : DP-VPX-0227-HRS-0012
- This module shall have an EEPROM memory of 4Kb via I2C interface.
- DDR4 Serial Presence Detect EEPROM (4Kb) per controller to store the DDR4 memory configuration details (Data width, clock speed, data bit swap information etc.)

### MRAM

Requirement ID : DP-VPX-0227-HRS-0013

This module shall have an MRAM memory of 4Mb via SPI interface with PS section.
MRAM memory shall be used for critical data storage during power OFF.

## Specification Statement – Communication
### High Speed PS Section
Requirement ID :DP-VPX-0227-HRS-0014

- This module shall have one x4 GTR Transceiver link terminating at VPX P4 connector from the Processing Section of the FPGA which can be configured as below,
  - 2 x1 PCIe / SATA
  - 1 x1 USB2.0/ 1 x USB 3.0
  - 1 x 1G Ethernet (SGMII)

### PL Section

Requirement ID :DP-VPX-0227-HRS-0015

- This module PL section shall have high speed interface such as,
  - 1Nos of x4 PCIE using Hard IP core.
  - 1Nos of x8 PCIE using Hard IP core.
  - 2Nos of x4 10G Ethernet to support 10G-Base KR, 10G Interfaces.
  - 2Nos of x4 RIO to support Aurora, SFPDP interfaces.

### Test & Debug Port

Requirement ID :DP-VPX-0227-HRS-0016

- This module shall have 2x RS232 / 2x RS422 on VPX P4 connector for communication purpose/Test and Debugging purpose from PS section. (or) 2 x RS232 UART ports from PS & 2 x RS232 UART ports from PL.
- 2Nos of 1000-Base-T Ethernet for also testing and debugging purpose.

## Specification Statement – Interface / Connectors

### VPX Connector

Requirement ID :DP-VPX-0227-HRS-0019

- The module shall comply VITA 67.3 standard connecterisation for back plane interface
- The module shall have VPX Connector(P0, P1 P2,P3,P4 and P6) with following interfaces.
  - VPX P0 Connector :
    • VS1,VS2=12V, VS3=5V, 3.3V_AUX (optional)
    • One I2C link from PS
    • One I2C link from PL
    • JTAG Interface
    • 25MHz REF Clock
   • 1PPS
  - VPX P1 Connector :
   • 4x 10 GigE interface to support (10G-Base KR) IP Core.
   • 1 x4 RIO from PL to support (Aurora/SFPDP) IP core.
    • 1Nos of x8 PCIE from GTH bank.
  - VPX P2 Connector :
    • 1 x4 RIO from PL to support (Aurora/SFPDP) IP core.
    • 1Nos of x4 PCIE from GTH bank using hardcore IP.
    • x8 LVDS or x16 LVTTL IO’s.
    • 4 LVTTL IO’s.
    • Multi board sync group as Trigger,SOB,TRP,Sysref IN and Sysref OUT.
    • External FPGA reference clock.
  - VPX P3 Connector :
    • 5x Analog Input signal for Down conversion.
    • 1x External Sysref reference clock for Onboard PLL.
  - VPX P4 Connector :
    • 2 Nos of x1 PCIE / SATA
    • 1Nos of USB3.0
    • 1Nos of SGMII
    • 2Nos of 1000-Base-T
    • x4 LVDS or x8 LVTTL IOs.
    • x2 RS485 or x4 RS232
  - VPX P6 Connector :
    • 4x Analog Input signal for Down conversion
    • 1x External Reference clock for ADC Sampling.
    • 1x External LO input to DDC piggy module.
### Temperature Sensor

Requirement ID :DP-VPX-0227-HRS-0017

- This module shall have one temperature Sensor to measure FPGA Temperature.
- This temperature Sensor is connected via I2C link from PS Section of FPGA

### XMC Connector for DDC Piggy module

Requirement ID :DP-VPX-0227-HRS-0018

• 162 TTL control lines for DCA control of DDC module.
• DDC module Power Supply generation such as :
◦ +5V,1.7A
◦ +6V,2.8A
◦ +3.5V,2A
◦ -5V.0.06A

### JTAG Header

Requirement ID :DP-VPX-0227-HRS-0020
This module shall have 1x6 pin JTAG Header Straight connector for the FPGA programming.
### RF Connectors

Requirement ID :DP-VPX-0227-HRS-0022

- This module shall have 9 Nos of SMPM connector for ADC Analog input.
- This module shall have 1 Nos of External Clock reference input to PLL.
- This module shall have 1 Nos of External Sysref reference input.
### I2C Header

Requirement ID :DP-VPX-0227-HRS-0021

ADM and SI5332 Digital PLL programming header.

## Specification Statement – Software Support

### Device Drivers

Requirement ID :DP-VPX-0224-HRS-0023

- Device Drivers shall be developed for all standard interfaces in PS section supported by BSP.
- Device Drivers shall be developed for validating all PL related interfaces.
### OS

Requirement ID :DP-VPX-0224-HRS-0024

This module shall have Uboot support and shall operate on Linux 5.4 & above.

## Specification Statement – Power Requirements

### Voltage

Requirement ID :DP-VPX-0227-HRS-0025
- The main input to the module is VS1,VS2=12V, VS3=5V, 3.3V_AUX (optional) from the VPX P0 Connector.
- 3.3V_AUX supply shall be optional.
- Other required supplies for the module shall be generated from the above supplies which shall be monitored & sequenced by voltage monitor & sequencer.
### Current

Requirement ID :DP-VPX-0227-HRS-0026

The current requirement for the module shall be 10.5A@12V(Max).
### Power Dissipation

Requirement ID :DP-VPX-0227-HRS-0027

The power requirement for the module shall be 126W@12V (Max).

## Specification Statement – Mechanical

### Dimension (L x B x H) in mm with Ruggedizer & Piggy module

Requirement ID :DP-VPX-0227-HRS-0027

The mechanical dimension for the module shall be 233.35 mm x 160 mm x 25.4 mm.

## Specification Statement – Environmental

### Operating Temperature
Requirement ID :DP-VPX-0227-HRS-0028
The operating temperature of the module shall be -40°C to +71°C(Card edge).
### Storage Temperature
Requirement ID :DP-VPX-0227-HRS-0029
The storage temperature of the module shall be -55°C to +90°C.
### Commercial / Rugged
Requirement ID :DP-VPX-0227-HRS-0030
The module grade shall be rugged.
### Thermal Dissipation
Requirement ID :DP-VPX-0227-HRS-0031
The module thermal dissipation shall be of conduction cooled type.
# FPGA DESIGN REQUIREMENT
Requirement ID :DP-VPX-0227-HRS-002
## FPGA Description

This module shall have one Zynq Ultra-scale+ MPSoC "XCZU11EG-2FFVC1760I" from Xilinx shall be used for signal processing which includes following interfaces

## Functional Requirement

S.No	Function Name	Description	Reference if applicable
1	JESD204B Interface (PL)	Two x8 JESD204B receiver with FFT logic shall be implemented for RFADC digital SERDES output	DP-VPX-1013,DP-VPX-0206 & DP-VPX-1505 DP-CG-BTM-33932
2	DDR4 Interface (PL)	One 32 Bit DDR4 Controller logic shall be implemented.	DP-FAB-BTM-00243
3	10G Ethernet (PL)	10G Ethernet Logic shall be implemented & shall be Interfaced with X4 RIO1 and x4 RIO2 lines to the P1 and P2 Connector.	DP-SPL-0181
4	SPI Interface (PL)	Seven SPI logic shall be implemented for register Configurations of AFE7906 and PLL.	DP-VPX-1505 and DP-CG-BTM-33932
5	UART Interface (PL)	The UART Logic shall be implemented.	DP-VPX-1505
6	IO Interface (PL)	IO Loop back Validation logic to be implemented	DP-VPX-1013
7	Zynq Ultrascale+ MPSoc Processing System	One Zynq Ultrascale+ MPSoC processing system core shall be implemented for configuration of desired PS interfaces.	DP-VPX-0206
8	1000Base-T RGMII (PL)	One 1000Base-T RGMII logic shall be implemented.	DP-SPL-0196
9	IO Interface (PL)	x4 LVTTL and x12 LVDS outputs with walking 1’s and 0’s Test logic to be implemented.	DP-VPX-0206

### Functional Requirement Description
JESD204B Interface for RFADC:
Three JESD204B Receiver core logic shall be implemented for three RFADCs with following specifications
- Serial Lane Rate : 9 Gbps
- GTY Reference Clock : 216 MHz
- No of Lanes : 8
- FFT Logic shall be implemented for phase difference measurement
- RFADC Part Number: AFE7906
DDR4 Interface from PL Section:
One 16 Bit DDR4 Controller logic shall be implemented in HPIO Bank with following Specifications.
- Data Width : 32 Bit without ECC
- Address Width : 32 Bit
- Rank :1
- Memory Size : 4 GB
- Data transfer Rate : 2400MT/S
- SYSCLK Frequency : 125.05 MHz
- DDR4 Memory Part : MT40A1G16TB-062E IT:F
10G Ethernet Interface:
10G Ethernet Logic shall be implemented in PL Section for x4 RIO Lanes with following Specifications.
- Protocol : 10GBASE-KR
- Specification : IEEE 802.3-2012
- Serial Rate : 10.3125 Gbps
- GTH Reference Clock Frequency : 156.25MHz
SPI Interface:
Seven SPI Logic shall be implemented for various ADC and PLL as per following specifications
Sl. No	Device	No of Lines	I/O Voltage Level	Maximum SPI Bus Frequency (MHz)
1	RFADC1	3 wire SPIA	LVCMOS1V8	25
2		3 wire SPIB1	LVCMOS1V8	25
3		3 wire SPIB2	LVCMOS1V8	25
4	RFADC2	3 wire SPIA	LVCMOS1V8	25
5		3 wire SPIB1	LVCMOS1V8	25
6		3 wire SPIB2	LVCMOS1V8	25
7	RFPLL	3 wire	LVCMOS3V3	50

UART Interface:
- UART Logic shall be implemented in PL Section to validate two RS232 UART Ports
- The Baud Rate shall be 115200bps.
IO Interface :
Registers shall be assigned for all the field IOs based on Loopback validation option
IO Logic Level	Input/Output	No of IOs	Number of Register shall be assigned
LVDS IO	Output	13 Nos	3
	Input	5 Nos	1
LVTTL IO	Output	4 Nos	2

# DEVELOPMENT PLATFORM

S.No	Parameter	Requirement
1	Architecture	ARM Cortex-A53, Dual Core ARM Cortex-R5, ARM Mali-400 Based GPU
2	OS	Linux 4.1
3	BUS	NA

# FAT VALIDATION REQUIREMENT

Requirement ID	Requirement	Testing Plan	Software
DP-VPX-0227-HRS-002	Zynq Ultrascale+ MPSoC	FPGA Part shall be detected & programmed by JTAG Cable.	NA
DP-VPX-0227-HRS-003	RFADC Specifications	Analog input shall be given to the RFADC from the Signal Generator. The digitized value shall be logged by the application & analyzed by High Speed Data Converter tool.	Test application shall be developed for ADC Configuration and logging the ADC samples in a (.csv) file.
DP-VPX-0227-HRS-004	IO Interfaces	LVDS, LVTTL shall be validated by loopback test between input and output.	Test application shall be developed for configuration of registers.
DP-VPX-0227-HRS-007	RF Clock Generation	Lock status shall be read by FPGA through SPI configuration.	Test application shall be developed for configuration of registers.
DP-VPX-0227-HRS-008	Digital clock generation	Digital section clock generation should be validated through Oscilloscope using probe.	Clock builder pro software is used for configuration.
DP-VPX-0227-HRS-009	DDR4 Memory	DDR4 will be tested using file read, file write and full memory test	Test application shall be developed
DP-VPX-0227-HRS-0011	Configuration Flash	Uboot file shall be loaded and validated by booting process.	NA
DP-VPX-0227-HRS-0010	eMMC NAND Flash	EMMC NAND flash shall be validated by using file read, file write and full memory test.	Test application shall be developed
DP-VPX-0227-HRS-0013	MRAM	MRAM shall be validated by using file read, file write and full memory test.	Test application shall be developed
DP-VPX-0227-HRS-0014	PS Section / - PCIe 2.0	PCIe Enumeration shall be done from any other VPX standard board via DP-VPX-XXXX Backplane.	NA
	PS Section- SATA 2.0	SATA DOM shall be connected with this interface via DP-VPX-XXXX Backplane and validated by File Read, Write test	Test application shall be developed
	PS Section- USB 2.0	External USB Pen Drive shall be connected to this interface via DP-VPX-XXXX Backplane. Functionality of this USB Port shall be validated by File Read and Write Test.	Test application shall be developed
DP-VPX-0227-HRS-0015	PL Section- 10G Ethernet	Test Board shall be developed for Electrical to Optical Conversion. This Optical lines shall be validated by interfacing with Optical to Ethernet converter module and Functionality of the Ethernet over optical shall be performed by link establishment and band width verification.	Test application shall be developed
	PL Section RIO	RIO Loop back shall be done from any other VPX standard board via DP-VPX-XXXX Backplane.	Test application shall be developed
	PL Section PCIe	PCIe Enumeration shall be done from any other VPX standard board via DP-VPX-XXXX Backplane.	Test application shall be developed
DP-VPX-0227-HRS-0016	Test & Debug port	2 Nos of RS422 /RS232 ports functionality shall be tested by communicating with test PC using DP-SPL-4258, a RS422/RS232 to USB serial converter module.	Test application shall be developed
	PS Section- 1000Base -T	Ethernet Cable shall be connected from this interface to Test PC via DP-VPX-XXXX Backplane. Functionality of the Ethernet port shall be validate by pinging a known IP and File transfer Test.	Test application shall be developed
DP-VPX-0227-HRS-0017	Temperature Sensor	Measured Temperature value shall be read from the temperature sensor register & the test application shall display the temperature on the front panel.	Test application shall be developed for displaying the FPGA & board temperature.
DP-VPX-0227-HRS-0025	Voltage	All Voltages shall be measured by the Multi-meter, unsequenced voltages shall be monitored through voltage monitor section.	Software support to read back the voltage and ADC values from ADM1166 voltage monitor-sequencer.
DP-VPX-0227-HRS-0026	Current	Current shall be measured by the clamp meter for +12V & +5V.	NA
DP-VPX-0227-HRS-0027	Power Consumption	Power Consumption shall be determined by the measuring the current at +12V & +5V supply and then calculated for P=VI.	NA

# DEMO VALIDATION REQUIREMENT

Requirement ID	Requirement	Testing Plan	Software
NA	NA	NA	NA

# SOFTWARE / FPGA LIBRARY :

DP Part Number	Library Part Number	Library Description	Remarks
NA	NA	NA	NA

# ANNEXURES
# Annexure A : KC Implementation

Table A 1 : KC Implementation

Key Characteristics ID	KC Name/ Specification	Requirement/Section Ref
NA	NA	NA

# Annexure B : Requirement Traceability Matrix

Table B 1 : Requirement Traceability Matrix

S. / No.	Requirement / ID	Description	DP-RDR-7474-600-SyRS-0V03 / SyRS Requirement Specification ID/REF	CMB/ / CRQ ID/REF	HRS Section / No.
	DP-VPX-0227-HRS-001	Type	-	-	4.1
	DP-VPX-0227-HRS-002	Zynq Ultrascale+ MPSoC	4.6.1	-	4.2
	DP-VPX-0227-HRS-003	RFADC Specifications	DP-RDR-7474-SyRS-006-024	-	4.3.1
	DP-VPX-0227-HRS-004	IO Interfaces	4.6.1	-	4.3.2
	DP-VPX-0227-HRS-005	Synchronization Interfaces	4.6.1	-	4.3.3
	DP-VPX-0227-HRS-006	Reference clock Inputs	DP-RDR-7474-SyRS-001-006	-	4.4.1
	DP-VPX-0227-HRS-007	RF Clock Generation	DP-RDR-7474-SyRS-001-006	-	4.4.3
	DP-VPX-0227-HRS-008	Digital Clock Generation	DP-RDR-7474-SyRS-001-006	-	4.4.2
	DP-VPX-0227-HRS-009	DDR4	DP-RDR-7474-SyRS-006-025	-	4.5.1
	DP-VPX-0227-HRS-0010	EMMC		-	4.5.3
	DP-VPX-0227-HRS-0011	NOR FLASH		-	4.5.2
	DP-VPX-0227-HRS-0012	EEPROM		-	4.5.1
	DP-VPX-0227-HRS-0013	MRAM		-	4.5.5
	DP-VPX-0227-HRS-0014	High Speed-PS Section	DP-RDR-7474-SyRS-001-006	-	4.6.1
	DP-VPX-0227-HRS-0015	High Speed-PL Section	DP-RDR-7474-SyRS-006-022,DP-RDR-7474-SyRS-006-023	-	4.5.5
	DP-VPX-0227-HRS-0016	Test & Debug port	Derived Specification	-	4.6.3
	DP-VPX-0227-HRS-0017	Temperature Sensor	DP-RDR-7474-SyRS-006-021	-	4.7.2
	DP-VPX-0227-HRS-0018	XMC Connector	4.6.1	-	4.7.3
	DP-VPX-0227-HRS-0019	VPX Connector		-	4.7.1
	DP-VPX-0227-HRS-0020	JTAG Header		-	4.7.4
	DP-VPX-0227-HRS-0021	I2C Header			4.7.6
	DP-VPX-0227-HRS-0022	RF Connector		-	4.7.5
	DP-VPX-0224-HRS-0023	Device Drivers		-	4.8.1
	DP-VPX-0224-HRS-0024	OS		-	4.8.2
	DP-VPX-0227-HRS-0025	Voltage		-	4.9.1
	DP-VPX-0227-HRS-0026	Current		-	4.9.2
	DP-VPX-0227-HRS-0027	Power Dissipation		-	4.9.3
	DP-VPX-0227-HRS-0028	Dimension (LxBxH) in mm		-	4.10.1
	DP-VPX-0227-HRS-0029	Weight in gm		-	4.10.1
	DP-VPX-0227-HRS-0030	Operating Temperature		-	4.11.1
	DP-VPX-0227-HRS-0031	Storage Temperature		-	4.11.2
	DP-VPX-0227-HRS-0032	Relative Humidity		-	4.11.3
	DP-VPX-0227-HRS-0033	Commercial / Rugged		-	4.11.3
	DP-VPX-0227-HRS-0034	Thermal Dissipation		-	4.11.4

# Annexure C : FAT Validation Matrix

Table C 1 : FAT Validation Matrix

Requirement ID	Description	Verification Method					Note
		QUAL TEST	ATP	INTEGRATION	DEMO	INSPECTION	ANALYSIS
DP-VPX-0227-HRS-001	Type					Y
DP-VPX-0227-HRS-002	Zynq Ultrascale+ MPSoC		Y			Y
DP-VPX-0227-HRS-003	RFADC Specifications		Y
DP-VPX-0227-HRS-004	IO interfaces		Y	Y
DP-VPX-0227-HRS-005	Synchronization Interfaces			Y
DP-VPX-0227-HRS-006	Reference clock Inputs		Y
DP-VPX-0227-HRS-007	RF Clock Generation		Y
DP-VPX-0227-HRS-008	Digital Clock Generation		Y
DP-VPX-0227-HRS-009	DDR4		Y
DP-VPX-0227-HRS-0010	EMMC		Y
DP-VPX-0227-HRS-0011	NOR FLASH		Y
DP-VPX-0227-HRS-0012	EEPROM		Y
DP-VPX-0227-HRS-0013	MRAM		Y
DP-VPX-0227-HRS-0014	High Speed-PS Section		Y
DP-VPX-0227-HRS-0015	High Speed-PL Section		Y
DP-VPX-0227-HRS-0016	Test & Debug port		Y
DP-VPX-0227-HRS-0017	Temperature Sensor		Y
DP-VPX-0227-HRS-0018	XMC Connector		Y			Y
DP-VPX-0227-HRS-0019	VPX Connector		Y			Y
DP-VPX-0227-HRS-0020	JTAG Header		Y			Y
DP-VPX-0227-HRS-0021	I2C Header		Y
DP-VPX-0227-HRS-0022	RF Connector		Y			Y
DP-VPX-0224-HRS-0023	Device Drivers		Y
DP-VPX-0224-HRS-0024	OS		Y
DP-VPX-0227-HRS-0025	Voltage		Y
DP-VPX-0227-HRS-0026	Current		Y
DP-VPX-0227-HRS-0027	Power Dissipation		Y
DP-VPX-0227-HRS-0028	Dimension (LxBxH) in mm		Y
DP-VPX-0227-HRS-0029	Weight in gm		Y
DP-VPX-0227-HRS-0030	Operating Temperature	Y
DP-VPX-0227-HRS-0031	Storage Temperature	Y
DP-VPX-0227-HRS-0032	Relative Humidity	Y
DP-VPX-0227-HRS-0033	Commercial / Rugged	Y
DP-VPX-0227-HRS-0034	Thermal Dissipation	Y

QUAL TEST – If the requirement is complied with any qualification testing it comes under Qual Test. (Eg. Environment Specification).
FAT – If the requirement is complied with normal functional testing, it comes in ATP. (all the requirement which can be validated can comes under this category).
INTEGRATION – If the requirement is complied by integration testing, it comes in INTEGRATION (Unit level, System Level, External Interface level which requires external modules / system for compliance)
DEMO – If the requirement is complied with one time validation, it comes under DEMO. (The requirements which have to be qualified but not carried for the production testing)
INSPECTION –	If the requirement is complied with the physical inspection, it comes under INSPECION (Eg. Size of the module)
ANALYSIS – If the requirement is complied with the any analysis, design compliance it comes under ANALYSIS

# Annexure D : Test Setup

Test Equipments Required

This section shall be given with required test equipments, test cables (bought out), test cables (fabricated), test jig, test rig, external modules, JTAG, Emulators, software environment, programming file etc.
Table D 1 : Test Equipment To Be Used

S. No.	Equipments/ Tool	Manufacturer	Model Number
	Power Supply-12 V, 20A (Min)	TDK Lambda
	Power Supply-5 V, 3A (Min)	TDK Lambda
	6U VPX 67.3 VITA Standard Slot Back-plane with mechanical	Data Patterns	DP-VPX-XXXX
	ADM1166 sequencer cable	Analog Devices	USB-SDP-CABLEZ
	Test Board for 1000Base- T and USB 3.0	Data Patterns	DP-SPL-XXXX
	JTAG Cable	Xilinx	Digilent HS-2/HS-3
	Signal Generator (for RF/IF inputs)	Agilent	N5181A
	Digital Multi meter
	Test PC (1)
	USB to Rs232/422 Converter – 2 no / 1 No	Data Patterns	DP-SPL-4258-300
	Power Divider	Mini Circuits
	FAN
	Ethernet Cable -2 Nos
	Network Analyzer	Agilent
	Electronic Calibration Kit / Mechanical Calibration Kit	Agilent
	Open Frame Ruggedizer	Data Patterns	DP-RM-MFB-XXXXX
	Test Jig	Data Patterns	DP-FAB-JIG-XXXXX

- Test PC should have the following features :
    - RAM – 4GB or more
    - COM port
    - Operating System – Windows
    - Super Sequencer Evaluation Software
    - Vivado 2016.4 version
    - High Speed Data Converter Pro 4.20
    - Docklight
Table D 2 : Test Jig interface details

S. No.	Jig / Cable / Part No.	Jig / Cable / Connector Ref	Board / Equipment mating ref (if avail)
	DP-FAB-JIG-XXXXX, RF Interface	TBD	TBD
	DP-FAB-CSY-22656	TBD	TBD

Table D 3 : Programming file details

S. No.	Programming Files	Device	Development / (New / Existing)
1	DP-VPX-0227-000-PWRSEQ-XVYZ.txt	Power Sequencer ADM1166	New
2	DP-VPX-0227-Vx-01-UYYY-Rx-XXXXXXXX.mcs	FPGA	New

Test Setup