HARDWARE REQUIREMENTS SPECIFICATION
for
3U VPX SOSA Zynq Ultrascale+ MPSoC based 6 Channel 14-Bit 0.02 to 3GHZ I/P Digital Receiver Module
DP-VPX-0236
Version 1.00
Release date 02.06.2025

Document Reference : DP-VPX-0236-000-HRS-0V06

Prepared by

Data Patterns (India) Limited.,
Plot No.H9, 4th Main Road,
SIPCOT IT Park, Siruseri,
Chennai - 603103

Copyright (2025) by Data Patterns

All rights reserved. These materials are confidential and proprietary to Data Patterns and no part of these materials should be reproduced or published in any form by any means, electronic or mechanical, including photocopy, on any information storage or retrieval system, nor should the materials be disclosed to third parties without the explicit written authorization of Data Patterns.

NAMING CONVENTION
The following naming convention is followed while giving the document reference number.
<PRODUCT_ID>-<FG>-<DOC_NAME>-<VERSION>. Where,

PRODUCT_ID	:	Denotes the product ID. For example – DP-SPL-5656

FG	:	Denotes the finished good number. Where,
For document common for all FGs - 000
For document configurable for individual FGs – 300, 600 etc.

DOC_NAME	:	Denotes the short form or acronym of document name.
For example : “HRS” for Hardware Requirements Specification

VERSION	:	Denotes version of the document. For example “1V00”

For example, document reference number :
Common FG - DP-SPL-5656-000-HRS-1V00
Individual FG - DP-SPL-5656-300-HRS-1V00

HARDWARE REQUIREMENTS SPECIFICATION
FOR
3U VPX SOSA Zynq Ultrascale+ MPSoC based 6 Channel 14-Bit 0.02 to 3GHZ I/P Digital Receiver Module.
DP-VPX-0236

Document Title	Hardware Requirements Specification for 3U VPX SOSA Zynq Ultrascale+ MPSoC based 6 Channel 14-Bit 0.02 to 3GHZ I/P Digital Receiver Module DP-VPX-0236
Document Reference	DP-VPX-0236-000-HRS-0V06
Version Number	0V06 (eg; 1V00)
Version Date	02.06.2025
Prepared By	Name : Vigneshwari G / Sign :
Document Review By	Name : Devaguru V / Sign :
Technical Review By	Name : Ramesh M / Sign :
Approved By	Name : DRB / Sign :

AMENDEMENTS TO THE DOCUMENT
S. No.	Ver. No.	Ver. Date	Changed by	Section (s) Changed	Description / of Change
1	0V01	26.12.2024	Vigneshwari G	-	Initial Version
2	0V02	02.01.2025	Vigneshwari G	-	Specifications
3	0V03	09.04.2025	Vigneshwari G	Specification	Optical connector section
4	0V04	27.05.2025	Vigneshwari G	Test setup block diagram	New requirement
5	0V05	30.05.2025	Nithyasri A	Block Diagram	DRB Comment
6	0V06	02.06.2025	Vigneshwari G	All section	DRB Comments

# INTRODUCTION

DP-VPX-0236 shall be a 3U VPX AFE7906 based 6-Channel 3Gsps RF ADC Digital Receiver module . This module shall have Zynq Ultrascale Plus re-programmable (MPSoC) hardware in combination with Dual / Quad core ARM processor signal processing. On board power generator & sequencing section shall be used for generation of all the power supplies in the module from +12V,+5V & +3.3V. This module shall have VPX connector for power supply. This module shall be of conduction cooled type with Ruggedizer .

## Scope

This document will explain how the requirements will meet through the specifications. The targeted audience is HDD. The task for HDD department is as follow, HDD : Preparation and Verification of HRS with respect to the requirement.

## Acronyms and Abbreviations

The acronyms and abbreviations used in this document are listed in the below Table 1.

Table 1 : List of Acronyms and Abbreviations
<Arial 10, normal case bold>, <Add an enter after and before the caption with “Single” line spacing>

HRS	Hardware Requirements Specification
BID	Board ID
ID	Identification
PID	Project/ Product ID
SID	System ID
HRS	Hardware Requirement Specification
SYRS	System Requirement Specification
DDR	Double Data Rate
EEPROM	Electrically Erasable Programmable Read Only Memory
PCIe	Peripheral Component Interconnect Express
SATA	Serial AT Attachment
USB	Universal Serial Bus
DDI	Device Driver Interface
ADC	Analog to Digital Converter
SPI	Serial Peripheral Interface
PLL	Phase Locked Loop
RF	Radio Frequency
IF	Intermediate Frequency
UART	Universal Asynchronous Receiver Transmitter
PL	Programmable Logic
PS	Processing System

## Referenced Documents

This section gives the external and internal documents referred to prepare this manual.

### External Documents

Table 2 : External Documents

NA	NA

### Internal Documents

Table 3 : Internal Documents

[SyRS]	DP-RDR-7576-600-SYRS-0V01

# MODULE OVERVIEW

DP-VPX-0236 shall be a 3U VPX digital receiver Module compliant with VITA 67.2 standard. This module shall have Zynq Ultrascale Plus reprogrammable (MPSoC) Dual / Quad core Arm Processor signal processing hardware in combination with AFE based RF Receiver.

The Processing section (PS) operates with Dual / Quad Arm core which performs the system management functionality of receiver. This Section shall have on board 4GB 32-bit DDR4 dynamic memories and dual QSPI NOR flash for boot configuration. It shall have an EEPROM memory of 4Kb via I2C interface to store the DDR4 memory configuration details. an eMMC NAND flash of 16GB for application and user storage and a 4MB MRAM for storing critical information.It shall provide 1000Base-T Ethernet for Communication and 2x RS422 (or) 2x RS232 UART port for debugging purpose. It offers a x1 PCIe gen2 link, two x1 SATA interfaces and One SGMII Interface. It shall have two RS232/ RS422 UART port for debugging purpose.

The Programmable Logics(PL) Section shall have x8 25 Gbps JESD204B receiver Core for AFE ADC and x4 10G Link to Field for transmitting the IQ data and x4 10G lanes for optical communication through piggy module. This Section shall have on board 4GB 32-bit DDR4 dynamic memories for easing IQ data logics. It provides SPI interface Logic for RFADC and PLL . It shall have two RS232 UART port for communication purpose.It also provides 95Nos of control IO’s to DDC module.

This module shall have 5Nos of 2.2GHz +/-300MHz ADC Input path with 3GSPS sampling rate. This module shall have low noise on board clock generation and distribution section to provide jitter free Sampling Clock to RFADC and FPGA JESD Cores. This section shall also have a option of choosing internal and external reference clock.

On board Power Generator & Sequencing section shall be used for generation of all the power supplies in the module from +12V,+5V & +3.3V. This module shall have VPX P0 Connector for Power Supply, VPX P1 for all communication links and debugging interfaces and VITA 67.2 RF connector for receiving x1LO, x1 Clock references,x1 Monitoring port of LO and x5 ADC inputs. It also has an XMC connector for DDC module interface with 95 nos of Control Io’s and Power supply of +12V . This module shall have a temperature sensor for monitoring the FPGA temperature. The module shall be of conduction cooled type with Ruggedizer and wedge lock arrangement.

## Features

 The main features of DP-VPX-0236 module is given below:

- Zynq Ultra-scale Plus MPSoC from Xilinx
- 32Bit 4GB DDR4 Memory from PS & 32Bit 4GB DDR4 Memory from PL
- x5 14-bit 2.2GHz ADC input Channels with 3GSPS Sampling based on AFE7906 with JESD204B/C digital Interface.
- 16GB eMMC NAND flash for User storage and 64MB dual parallel QSPI for boot file storage.
- 512KB MRAM & 4Kb EEPROM memory interfaces for critical data storage.
- x1 1000 Base-T and x1 SGMII Ethernet Interface for communication.
- 2 x RS422 interface or 2xRS232, 1x RS422 for debugging.
- x4 10G interface to Filed for transmitting IQ Data and x4 10G lanes for Optical communication.
- x1 PCIe interface , x2 Sata interface from PS
- x95 TTL/LVTTL Control IO’s for DDC Module.
- On board clock generator section with Internal & External Reference
- On board Power supply generator & sequencer

## Applications

- V/U/SHF Search Receiver
- Digital Receiver for both RF & IF signals.
- Data Communications.
- Signal Processing.
# BLOCK DIAGRAM

Figure 1 : Block Diagram of DP-VPX-0236
# SPECIFICATIONS

Table 4 : Specifications

Requirement ID	Description	Specification
DP-VPX-0236-HRS-001	Type	3U VPX (VITA 67.2 Compliant)
DP-VPX-0236-HRS-002	Zynq Ultrascale+ MPSoC	Part: XCZU11EG-2FFVC1760I / Zynq Ultrascale+ MPSoC / Part reference:XCZU11EG-2FFVC1760I / Processing System / APU- 64-bit Quad core Arm Cortex™-A53 upto 1.5GHz / RPU- Dual-core Arm Cortex-R5 / Arm v7-R Architecture (32-bit) upto 600MHz / Graphics Processing Unit (GPU) / Programmable Logic / CLB LUTs : 298K / Distributed RAM size: 9.1Mb / Block RAM size : 21.1Mb / DSP Slices : 2928 / No of HPIO : 416 / No of HDIO : 96 / No of GTH Transceiver : 32 / No of GTY Transceiver : 16 / GTH Transceiver speed : 16.3Gbps / GTY Transceiver speed : 28.2Gbps
INPUT AND OUTPUT SPECIFICATIONS
DP-VPX-0236-HRS-003	RFADC Specifications	MFR Part:AFE7906IABJ / ADC Input : 5 Channels / RF input frequency: / • 2200 ± 2.5MHz (NB) / • 2200 ± 300MHz (WB) / IBW: 600MHz (Usable BW max) / Each ADC channel shall have with differential analog input from RF Balun. / ADC resolution: 14bit / ADC input level : 3 dBm(typ) / ADC Input Bandwidth(-3dB) : / 1.9 to 2.5GHz (Board capability) / 12 GHz (Chip Capability) / Sampling Rate : 3GSPS (Max) / DSA: 25dB in step of 0.5dB / Digital Data Interface: x8 JESD204B with a maximum data rate of, / upto 30Gbps(Chip Capability) / upto 25Gbps (Board capability) / The Module Specifications shall be, / SNR: / 56 dBFs @ -3dBFs IBW:600MHz / 60 dBFs @ -3dBFs IBW:360MHz / 70dBFs @ -3dBFs IBW: 5MHz / SFDR: / 68 dBc @ -3dBFs IBW:600MHz / 75 dBc @ -3dBFs IBW:360MHz / 80 dBc @ -3dBFs IBW: 5MHz / ENOB : / >9bits @ IBW: 600Mhz / >9.7bits @ IBW: 300Mhz / > 11.4 Bits @ 5MHz IBW / Crosstalk : > 65 dBc @ 2500 MHz / Phase matching : +/-3 deg / Amplitude Flatness: < 2dB
DP-VPX-0236-HRS-004	I/O Interface	LVTTL/LVCMOS I/O Signals / TTL outputs to XMC – 95 Nos / LVTTL Input from VPX- 6 Nos / LVTTL Output to VPX- 2 Nos / LVDS I/O Signals / LVDS Input from VPX – 2Nos / LVDS Output to VPX - 1No
CLOCK SPECIFICATIONS
DP-VPX-0236-HRS-005	Reference clock	32.768 KHz - RTC reference clock / 25MHz crystal for Digital PLL Reference. / External Clock for RFPLL Reference
DP-VPX-0236-HRS-006	Digital Clock Generation	Separate PLL shall be used for the generation of all the digital section clock such as, / 156.25 MHz to GTH Bank ref clock for PL 10G Ethernet interface. / 125 MHz to IO Bank SYSCLK for PLDDR4 interface. / 100 MHz to GTR Bank ref clocks for PS PCIe 2.0 & USB 3.0 interface. / 125 MHz to GTR Bank ref clocks for PS SGMII & SATA 2.0 interface. / 40MHz & 25MHz FPGA Reference clock. / 25MHz as reference to VPX, ETH PHY & RF PLL.
DP-VPX-0236-HRS-008	RF Clock Generation	Separate PLL shall be used for the generation of all the RF section clock such as / RF-AFE Sampling Clock : Upto 3 GHz / GTH Bank reference clock for PL Section JESD204B/C interface upto 250 MHz / SYSREF clock of upto 10 MHz for both AFE & FPGA JESD204B interface.
MEMORY
DP-VPX-0236-HRS-009	DDR4 Memory	One 32 Bit 4GB DDR4 Controller from PS Section with operating upto 2400MT/S. / One 32 Bit 4GB DDR4 Controller from PL Section with operating upto 2400MT/S.
DP-VPX-0236-HRS-0010	Configuration Flash	2 x 64MB Quad SPI NOR Flash
DP-VPX-0236-HRS-0011	eMMC NAND Flash	16GB eMMC NAND Flash (8bit)
DP-VPX-0236-HRS-0012	MRAM	4Mb MRAM via SPI Interface
DP-VPX-0236-HRS-0013	EEPROM	4Kb DDR4 SPD EEPROM
COMMUNICATION
DP-VPX-0236-HRS-0014	PS Section	1 x1 PCIe Gen2 / 2 x1 SATA / 1x USB2.0 / 1 x 1G Ethernet (SGMII) / 1 x 1G Ethernet (RGMII)
DP-VPX-0236-HRS-0015	PL Section*	x4 RIO from PL to support multiple protocols such as 10G Ethernet and x4 10G lanes for optical communication.
DP-VPX-0236-HRS-007	Test & Debug port	2 x RS232 / RS422 UART ports from PS / (or) / 2 x RS232 UART ports from PS & 2 x RS232 UART ports from PL
INTERFACE / CONNECTORS
DP-VPX-0236-HRS-0016	VPX Connector	VPX power Connector P0 / VS1=12V, VS3=5V, VS2=3.3V, 3.3V_AUX (optional) / One I2C link from PS / JTAG Interface
		VPX Differential IO connector P1 / 1 x4 RIO to support 10G Ethernet IP core from PL. / 1 x1 PCIe 2.0 from PS / 2 x1 SATA 2.0 from PS / 1 x 1G Ethernet (SGMII) from PS / 1 x 1000-Base-T Ethernet from PS(RGMII) / 2 x RS422 CH from PS / 2 x RS232 from PS & 2x RS232 from PL / 4x LVTTL IN & 2 LVTTL OUT / 2x LVDS IN & x1 LVTTLOUT for Synchronization
		VPX VITA67.2 Connector P2 / 5x Analog Input signal for Down conversion. / 1x LO reference for DDC module. / 1x External Sampling clock for AFE7906. / 1x IF Monitoring Output.
DP-VPX-0236-HRS-0017	Temperature Sensor	One No of temperature Sensor from PS Section via I2C interface to measure FPGA Temperature.
DP-VPX-0236-HRS-0018	RF Connectors	5 Nos of SMPM connectors for AFE inputs / 1 No of SMPM connector for External Sampling clock / 1 No for LO reference and 1 No monitoring clock for LO.
DP-VPX-0236-HRS-0019	Expansion Site Connectors	High speed XMC connector : / Connector Type- Socket VITA 42(Female) / Mount type- PCB solder / Orientation- straight / Interfaces from PL Section: / 95x IOs (LVTTL) / Power Supply : / +12V, 2A (typ)
DP-VPX-0236-HRS-0023	High Speed connector	1 x4 10G lanes for optical communication / x2 LVTTL Input / x4 LVTTL Output
SOFTWARE SUPPORT
DP-VPX-0236-HRS-0020	Device Drivers	Device drivers for all standard interfaces in PS section supported by BSP. / Device Drivers for all PL related peripheral Interfaces.
DP-VPX-0236-HRS-0024	OS	Linux 5.4 & above.
POWER REQUIREMENTS
DP-VPX-0236-HRS-0025	Voltage	VS1=+12V, VS3=+5V, VS2=+3.3V
DP-VPX-0236-HRS-0026	Current	+12V,2.5A / +5V,10A / +3.3V,3A
DP-VPX-0236-HRS-0027	Power Dissipation	89W max.
MECHANICAL
DP-VPX-0236-HRS-0028	Dimension (LxBxH) in mm with Ruggedizer and Piggy Module	160 mm x 100 mm x 12 mm
DP-VPX-0236-HRS-0029	Weight in gm	<1.3Kg
ENVIRONMENTAL
DP-VPX-0236-HRS-0021	Operating Temperature	-40ºC to +80ºC (Card edge).
DP-VPX-0236-HRS-0030	Storage Temperature	-55ºC to +90ºC
DP-VPX-0236-HRS-0031	Commercial / Rugged	Rugged
DP-VPX-0236-HRS-0022	Thermal Dissipation	Conduction Cooled

Note: * -FG specification Table

FG Specification Table
Requirement ID	Description	Specification
		DP-VPX-0236-660	DP-VPX-0236-XXX
DP-VPX-0236-HRS-0015	PL section	x2 RIO from PL to support multiple protocols such as 10G Ethernet and x4 10G lanes for optical communication	x4 RIO from PL to support multiple protocols such as 10G Ethernet and x4 10G lanes for optical communication

## Specification Statement – Type
Requirement ID :DP-VPX-0236-HRS-001
This module shall be 3U VPX based module compliant with VITA 67.2 standard.

## Specification Statement – Zynq Ultrascale+ MPSoC
Requirement ID :DP-VPX-0236-HRS-002
This module shall have one Zynq Ultra-scale+ (MPSoC) FPGA with following specifications.
Section	Parameters	Specifications
PS Section	Application Processor Core	Quad-core ARM® Cortex™-A53 MPCore™ up to 1.5GHz
	Real-Time Processor Core	Dual-core ARM Cortex-R5 MPCore™ up to 600MHz
	Graphics Processing Unit	Mali™-400 MP2 up to 667MHz
	Dynamic Memory Interface	x32: DDR4 with x8 ECC
	Static Memory Interfaces	2x Quad-SPI
	High-Speed Connectivity	PCIe® Gen2 , SATA 3.1
	General Connectivity	1x eMMC, 2x UART, 2x I2C, 1x SPI
	PS-GTR_6 Gbps	4
	PS IOs	214
PL Section	System Logic Cells (K)	653,100
	CLB Flip-Flops (K)	597,120
	CLB LUTs (K)	298,560
	Max. Distributed RAM (Mb)	9.1
	Total Block RAM (Mb)	21.1
	UltraRAM (Mb)	22.5
	Clock Management Tiles (CMTs)	8
	DSP Slices	2928
	GTH 16.3Gb/s Transceivers	32
	GTY 28.2Gb/s Transceivers	16
	HD IOs (1.2V- 3.3V)	96
	HP IOs (1V to 1.8V)	416

## Specification Statement – Input and Output Specifications
### RF ADC Specifications
Requirement ID :DP-VPX-0236-HRS-003
This module shall have 5ADC channels from One AFE7906 Transceiver. Each ADC channel shall have differential analog input from RF Balun.
Manufacturer Part :AFE7906
    • ADC Input : 5 Channels
    • RF input frequency: 2.2GHz +/- 300MHz
    • IBW: Narrow Band - 5MHz
        Wide Band - 600MHz
    • Each ADC channel shall have with differential analog input from RF Balun.
    • ADC resolution: 14bit
    • ADC input level : 3dBm (Typ)
    • ADC Input Bandwidth(-3dB) :
        ◦ 12 GHz (Chip Capability)
    • Sampling Rate : 3GSPS (Max)
    • DSA: 25dB in step of 0.5dB
    • Digital Data Interface: x8 JESD204B with a maximum data rate of,
        ◦ upto 30Gbps(Chip Capability)
        ◦ upto 25Gbps (Board capability)
    • The Module Specifications shall be,
SNR:
  - 56 dBFs @ -3dBFs IBW:600MHz
  - 60 dBFs @ -3dBFs IBW:360MHz
  - 70dBFs @ -3dBFs IBW: 5MHz
- SFDR:
  - 68 dBc @ -3dBFs IBW:600MHz
  - 75 dBc @ -3dBFs IBW:360MHz
  - 80 dBc @ -3dBFs IBW: 5MHz
- ENOB :
  - >9bits @ IBW: 600Mhz
  - >9.7bits @ IBW: 300Mhz
  - > 11.4 Bits @ 5MHz IBW
- Crosstalk :> 65 dBc @ 2500 MHz
- Phase matching :+/-3 deg
- Amplitude Flatness <2dB

### IO Interfaces
Requirement ID : DP-VPX-0236-HRS-004
This module shall have the following number of Field IO’s.
IO Logic Level	Input/Output	No of IOs
TTL IO	Output	95 Nos
	Input	-
LVTTL	Output	2Nos
	Input	4Nos
LVDS	Output	1Nos
	Input	2Nos

## Specification Statement – Clock Requirements
### Reference Clock

Requirement ID : DP-VPX-0236-HRS-005
This module shall have the following clocks mentioned below in the Table 5 : Clock split up.
Table 5 : Clock split up
S.No	Clock	Clock receiving section
1	32.768KHz Crystal	MPSoC PS RTC Section
2	External Clock	RF PLL Section
3	25MHz crystal	Digital PLL Section

### Digital Clock Generation

Requirement ID : DP-VPX-0236-HRS-006
This module shall have a Programmable PLL to generate the below Digital Clock as mentioned below,
- 156.25 MHz to GTH Bank ref clock for PL 10G Ethernet interface.
- 125 MHz to IO Bank SYSCLK for PLDDR4 interface.
- l.
- 125 MHz to GTR Bank ref clocks for PS SGMII & SATA 2.0 interface.
- 40MHz & 25MHz FPGA Reference clock.
- 25MHz as reference to VPX, ETH PHY & RF PLL.

### RF Clock Generation

Requirement ID : DP-VPX-0236-HRS-008
This module shall have a Programmable PLL to generate the below Digital Clock as mentioned below,
- RF-AFE Sampling Clock : Upto 3 GHz
- GTH Bank reference clock for PL Section JESD204B/C interface upto 250 MHz
- SYSREF clock of upto 10 MHz for both AFE & FPGA JESD204B interface.
Input Reference Clocks	Generated Ouput Clocks
1) External Clock / 2) 25 MHz from Digital PLL	RFADC sampling Clock	Upto 3GHz
	RFADC SYREF Clock	Upto 10 MHz
	RFADC GTH Bank Reference Clock	Upto 400 MHz
	SYSREF Clock to FPGA	Upto 10 MHz

## Specification Statement – Memory
### DDR4 memory

Requirement ID : DP-VPX-0236-HRS-009

- This Module shall have one 32 Bit Controller 4GB DDR4 SDRAM with Data Rate of 2400 MT/s from PS Section.
- This Module shall have one 32 Bit Controller 4GB DDR4 SDRAM with Data Rate of 2400 MT/s from PL Section.

### Configuration Flash

Requirement ID : DP-VPX-0236-HRS-0010

This module shall have two 64MB Quad SPI NOR Flash memory for booting process.

### EMMC NAND Flash

Requirement ID : DP-VPX-0236-HRS-0011

- This module shall have an EMMC NAND Flash memory of 16GB.
- NAND flash shall be used for storing Device tree, File system & User defined application.
- EMMC NAND Flash shall be interfaced with PS Section
### MRAM

Requirement ID : DP-VPX-0236-HRS-0012

- This module shall have an MRAM memory of 4Mb via SPI interface.
- MRAM memory shall be used for critical data storage during power OFF.
- MRAM Flash shall be interfaced with PS Section
### EEPROM

Requirement ID : DP-VPX-0236-HRS-0013

- This module shall have an EEPROM memory of 4Kb via I2C interface.
- DDR4 Serial Presence Detect EEPROM (4Kb) per controller to store the DDR4 memory configuration details (Data width, clock speed, data bit swap information etc.)

## Specification Statement – Communication
### PS Section

Requirement ID : DP-VPX-0236-HRS-0014

- This module shall have one x4 GTR Transceiver link terminating at VPX P1 connector from the Processing Section of the FPGA which can be configured as below,
  - 1 x1 PCIe
  - 2 x1 SATA 2.0
  - 1 x 1G Ethernet (SGMII)
- This following interfaces shall be connected with PSMIO Bank of FPGA and VPX P1 Connector
  - 1 x 1G Ethernet (RGMII)

### PL Section

Requirement ID : DP-VPX-0236-HRS-0015

- This module shall have 1 x4 RIO terminating at VPX P1 connector from PL section of FPGA to support 10G Ethernet IP core.
- This module shall have 1 x4 10G lanes connected to LSHM high speed connector for Optical communication .

### Test & Debug Port

Requirement ID : DP-VPX-0236-HRS-007
This module shall have UART ports for Test and Debugging purpose in the following configuration,
  - 2 x RS422 from PS section
  - 2 x RS232 from PS section & 2 x RS232 from PL section

## Specification Statement – Interface / Connectors

### VPX Connector

Requirement ID : DP-VPX-0236-HRS-0016

- The module shall comply VITA 42 standard connecterisation for back plane interface.
- The module shall have VPX Connector(P0, P1 ) with following interfaces.
  - VPX P0 Connector :
    - VS1=12V, VS3 = 5V, VS2 = 3.3V, 3.3V_AUX (optional)
    - One I2C link for PS section of FPGA
    - JTAG interface
  - VPX P1 Connector :
    - 95 x TTL IO's from PL section
    - 6x LVTTL IO’s from PL section
    - 3x LVDS IO’s from PL section
### Temperature Sensor

Requirement ID : DP-VPX-0236-HRS-0017

- This module shall have one temperature Sensor to measure FPGA Temperature.
- This temperature Sensor is connected via I2C link from PS Section of FPGA.
### RF SMPM Connectors

Requirement ID : DP-VPX-0236-HRS-0018

- This module shall have 8SMPM connectors for below functions,
  - 5 Nos of SMPM Connector for RFADC Input
  - 1 No for External Reference Clock
  - 1No for monitoring port for LO
  - 1No for LO reference.

### Expansion Site Connector

Requirement ID : DP-VPX-0236-HRS-0019

- This module shall have high speed XMC connectors for interfacing down converter Modules.
- XMC Connector
  - 95 Nos of LVTTL Output
  - +12V-S @ 2A(typ)
### High speed connector

Requirement ID : DP-VPX-0236-HRS-0023
- This module shall have one LSHM high speed connector for interfacing optical piggy module.
- It shall have x4 lanes for optical communication , x2 LVTTL Input & x4 LVTTL

## Specification Statement – Software Support

### Device Drivers

Requirement ID : DP-VPX-0236-HRS-0020

- Device Drivers shall be developed for all standard interfaces in PS section supported by BSP.
- Device Drivers shall be developed for validating all PL related interfaces.
### OS

Requirement ID : DP-VPX-0236-HRS-0024

This module shall have Uboot support and shall operate on Linux 5.4 & above.

## Specification Statement – Power Requirements

### Voltage

Requirement ID : DP-VPX-0236-HRS-0025
- The main input to the module is 3.3V, 5V,12V from the VPX P0 Connector.
- 3.3V_AUX supply shall be optional.
- Other required supplies for the module shall be generated from the above supplies which shall be monitored & sequenced by voltage monitor & sequencer.
### Current

Requirement ID : DP-VPX-0236-HRS-0026

The current requirement for the module shall be 2.5A on +12V,10A on 5V and 3A on 3.3V.

### Power Dissipation

Requirement ID : DP-VPX-0236-HRS-0027

The power requirement for the module shall be 89W (Max).
## Specification Statement – Mechanical

### Dimension (L x B x H) in mm with Ruggedizer & Piggy module

Requirement ID : DP-VPX-0236-HRS-0028

The mechanical dimension for the module shall be 160 mm x 100 mm x 12mm

## Specification Statement – Environmental

### Operating Temperature
Requirement ID : DP-VPX-0236-HRS-0021
The operating temperature of the module shall be -40°C to +80°C(Card edge).
### Storage Temperature
Requirement ID : DP-VPX-0236-HRS-0030
The storage temperature of the module shall be -55°C to +90°C.
### Commercial / Rugged
Requirement ID : DP-VPX-0236-HRS-0031
The module grade shall be rugged.
### Thermal Dissipation
Requirement ID : DP-VPX-0236-HRS-0022
The module thermal dissipation shall be of conduction cooled type.

# FPGA DESIGN REQUIREMENT
Requirement ID : DP-VPX-0236-HRS-002

## FPGA Description

This module shall have one Zynq Ultra-scale+ MPSoC "XCZU11EG-2FFVC1760I " from Xilinx shall be used for signal processing which includes following interfaces

## Functional Requirement

S.No	Function Name	Description	Reference if applicable
1	JESD204B Interface (PL)	x8 JESD204B receiver with FFT logic shall be implemented for RFADC digital SERDES output	DP-VPX-0227
2	DDR4 Interface (PL)	One 32 Bit DDR4 Controller logic shall be implemented.	DP-VPX-0227
3	10G Ethernet (PL)	10G Ethernet Logic shall be implemented & shall be Interfaced with X4 RIO lines to the P1 Connector.	DP-VPX-0206
4	SPI Interface (PL)	Seven SPI logic shall be implemented for register Configurations of ADC and PLL.	DP-VPX-0227, / DP-VPX-0206
5	UART Interface (PL)	The UART Logic shall be implemented.	DP-VPX-0206
6	IO Interface (PL)	IO Loop back Validation logic to be implemented	DP-VPX-0206
7	Zynq Ultrascale+ MPSoc Processing System	One Zynq Ultrascale+ MPSoC processing system core shall be implemented for configuration of desired PS interfaces.	DP-VPX-0227
8	IO Interface (PL)	x6 LVTTL and x3 LVDS outputs with walking 1’s and 0’s Test logic to be implemented.	DP-VPX-0206

### Functional Requirement Description
JESD204B Interface for RFADC:
x8 JESD204B Receiver core logic shall be implemented for AFE7906 based RFADC with following specifications
- Serial Lane Rate : 24.75 Gbps
- GTY Reference Clock : 204.8 MHz
- No of Lanes : 8
- FFT Logic shall be implemented for phase difference measurement
- RFADC Part Number: AFE7906IABJ

DDR4 Interface from PL Section:
One 32 Bit DDR4 Controller logic shall be implemented in HPIO Bank with following Specifications.
- Data Width : 32 Bit without ECC
- Address Width : 32 Bit
- Rank :1
- Memory Size : 4 GB
- Data transfer Rate : 2400MT/S
- SYSCLK Frequency : 125.05 MHz
- DDR4 Memory Part : MT40A1G16TB-062E IT:F
RIO Interface:
- x4 RIO from PL to support multiple protocols such as 10G Ethernet .
- x4 10G lanes for optical communication.

SPI Interface:
Seven SPI Logic shall be implemented for various ADC and PLL as per following specifications
Sl. No	Device	No of Lines	I/O Voltage Level	Maximum SPI Bus Frequency (MHz)
1	RF-AFE	3 wire	LVCMOS1V8	25
2		3 wire	LVCMOS1V8	25
4	RFPLL- On board	3 wire	LVCMOS3V3	20

UART Interface:
- UART Logic shall be implemented in PL Section to validate two RS232 UART Ports
- The Baud Rate shall be 115200bps.
IO Interface :
Registers shall be assigned for all the field IOs based on Loopback validation option
IO Logic Level	Input/Output	No of IOs
LVDS IO	Output	2 Nos
	Input	1 No
LVTTL IO	Output	2 Nos
	Input	4 No

# DEVELOPMENT PLATFORM

S.No	Parameter	Requirement
1	Architecture	ARM Cortex-A53, Dual Core ARM Cortex-R5, ARM Mali-400 Based GPU
2	OS	Linux 4.1
3	BUS	NA

# FAT VALIDATION REQUIREMENT

Requirement ID	Requirement	Testing Plan	Software
DP-VPX-0236-HRS-002	Zynq Ultrascale+ MPSoC	FPGA Part shall be detected & programmed by JTAG Cable.	NA
DP-VPX-0236-HRS-003	RFADC Specifications	Analog input shall be given to the RFADC from the Signal Generator. The digitized value shall be logged by the application & analyzed by High Speed Data Converter tool.	Test application shall be developed for ADC Configuration and logging the ADC samples in a (.csv) file.
DP-VPX-0236-HRS-004	IO Interfaces	LVDS, LVTTL, TTL and GPIOs shall be validated by loopback test between input and output.	Test application shall be developed for configuration of registers.
DP-VPX-0236-HRS-005	Digital clock generation	Digital section clock generation should be validated through Oscilloscope using probe.	Clock builder pro software is used for configuration.
DP-VPX-0236-HRS-006	RF Clock Generation	Lock status shall be read by FPGA through SPI configuration.	Test application shall be developed for configuration of registers.
DP-VPX-0236-HRS-009	DDR4 Memory	DDR4 will be tested using file read, file write and full memory test by automation	Test application shall be developed
DP-VPX-0236-HRS-0010	Configuration Flash	Uboot file shall be loaded and validated by booting process.	NA
DP-VPX-0236-HRS-0011	eMMC NAND Flash	EMMC NAND flash shall be validated by using file read, file write and full memory test by automation.	Test application shall be developed
DP-VPX-0236-HRS-0012	MRAM	MRAM shall be validated by using file read, file write and full memory test by automation.	Test application shall be developed
DP-VPX-0236-HRS-0014	PS Section / - PCIe 2.0	PCIe Enumeration, write test , read test shall be done from any other VPX standard board via Backplane	NA
	PS Section- SATA 2.0	SATA DOM shall be connected with this interface via Backplane and validated by File Read, Write test	Test application shall be developed
	PS Section- 1000Base -T	Ethernet Cable shall be connected from this interface to Test PC via Backplane. Functionality of the Ethernet port shall be validate by pinging a known IP and File transfer Test.	Test application shall be developed
	PS Section- 1000Base -X	Test Board shall be developed and Connected with this interface via Backplane. Ethernet Cable shall be connected from test board to Test PC. Functionality of the Ethernet port shall be validate by pinging a known IP and File transfer Test.	Test application shall be developed
DP-VPX-0236-HRS-0015	PL Section- RIO Interface	X4 RIO lines shall be validated to loopback with DP-VPX-2606 module	Test application shall be developed
DP-VPX-0236-HRS-0016	Test & Debug port	2 Nos of RS422 /RS232 ports functionality shall be tested by communicating with test PC using DP-SPL-4258, a RS422/RS232 to USB serial converter module.	Test application shall be developed
DP-VPX-0236-HRS-0017	Temperature Sensor	Measured Temperature value shall be read from the temperature sensor register & the test application shall display the temperature on the front panel.	Test application shall be developed for displaying the FPGA & board temperature.
DP-VPX-0236-HRS-0025	Voltage	All Voltages shall be measured by the Multi-meter, unsequenced voltages shall be monitored through voltage monitor section.	Software support to read back the voltage and ADC values from ADM1166 voltage monitor-sequencer.
DP-VPX-0236-HRS-0026	Current	Current shall be measured by the clamp meter for +12V,+5V & +3.3V.	NA
DP-VPX-0236-HRS-0027	Power Consumption	Power Consumption shall be determined by the measuring the current at +12V,+5V & +3.3V supply and then calculated for P=VI.	NA

# DEMO VALIDATION REQUIREMENT

Requirement ID	Requirement	Testing Plan	Software
NA	-	-	-

# SOFTWARE / FPGA LIBRARY :

DP Part Number	Library Part Number	Library Description	Remarks
NA	NA	NA	NA

# ANNEXURES
# 10 Annexure A : KC Implementation

Table A 6 : KC Implementation

Key Characteristics ID	KC Name/ Specification	Requirement/Section Ref
NA	NA	NA

# 11 Annexure B : Requirement Traceability Matrix

Table B 7 : Requirement Traceability Matrix

S. / No.	Requirement / ID	Description	DP-RDR-7576-600-SYRS-0V01 Requirement Specification ID/REF	CMB/ / CRQ ID/REF	HRS Section / No.
	DP-VPX-0236-HRS-001	Type	-	-	4.1
	DP-VPX-0236-HRS-002	Zynq Ultrascale+ MPSoC	4.3.1.	-	4.2
	DP-VPX-0236-HRS-003	RFADC Specifications	4.3.2	-	4.3.1
	DP-VPX-0236-HRS-004	IO interfaces	4.3.17	-	4.3.2
	DP-VPX-0236-HRS-005	Reference clock	4.3.4	-	4.4.1
	DP-VPX-0236-HRS-006	Digital Clock Generation	4.3.5	-	4.4.2
	DP-VPX-0236-HRS-008	RF Clock Generation	4.3.6	-	4.4.3
	DP-VPX-0236-HRS-009	DDR4 Memory	4.3.8	-	4.5.1
	DP-VPX-0236-HRS-0010	Configuration Flash	4.3.9	-	4.5.2
	DP-VPX-0236-HRS-0011	eMMC NAND Flash	4.3.10	-	4.5.3
	DP-VPX-0236-HRS-0012	MRAM	4.3.11	-	4.5.4
	DP-VPX-0236-HRS-0013	EEPROM	Derived Specification	-	4.5.5
	DP-VPX-0236-HRS-0014	PS Section	4.3.12, 4.3.13, 4.3.14	-	4.6.1
	DP-VPX-0236-HRS-0015	PL Section	4.3.15	-	4.6.2
	DP-VPX-0236-HRS-007	Test & Debug port	4.3.16	-	4.6.3
	DP-VPX-0236-HRS-0016	VPX Connector	4.3.17	-	4.7.1
	DP-VPX-0236-HRS-0017	RF SMPM Connectors	4.3.18 , 4.3.17	-	4.7.3
	DP-VPX-0236-HRS-0018	Expansion Site Connectors	4.3.19, 4.3.20	-	4.7.4
	DP-VPX-0236-HRS-0023	Temperature Sensor	4.3.21	-	4.7.2
	DP-VPX-0236-HRS-0020	Device Drivers	4.3.22	-	4.8.1
	DP-VPX-0236-HRS-0024	OS	4.3.23	-	4.8.2
	DP-VPX-0236-HRS-0025	Voltage	4.3.24	-	4.9.1
	DP-VPX-0236-HRS-0026	Current	4.3.25	-	4.9.2
	DP-VPX-0236-HRS-0027	Power Dissipation	4.3.26	-	4.9.3
	DP-VPX-0236-HRS-0028	Dimension (LxBxH) in mm with Ruggedizer and Piggy Module	4.3.27	-	4.10.1
	DP-VPX-0236-HRS-0021	Operating Temperature	4.3.28	-	4.11.1
	DP-VPX-0236-HRS-0030	Storage Temperature	4.3.29	-	4.11.2
	DP-VPX-0236-HRS-0031	Commercial / Rugged	4.3.30	-	4.11.3
	DP-VPX-0236-HRS-0022	Thermal Dissipation	4.3.31	-	4.11.4

# 12 Annexure C : FAT Validation Matrix

Table C 8 : FAT Validation Matrix

Requirement ID	Description	Verification Method					Note
		QUAL TEST	ATP	INTEGRATION	DEMO	INSPECTION	ANALYSIS
DP-VPX-0236-HRS-001	Type					Y
DP-VPX-0236-HRS-002	Zynq Ultrascale+ MPSoC		Y			Y
DP-VPX-0236-HRS-003	RFADC Specifications		Y
DP-VPX-0236-HRS-004	IO interfaces		Y
DP-VPX-0236-HRS-005	Reference clock		Y
DP-VPX-0236-HRS-006	Digital Clock Generation		Y
DP-VPX-0236-HRS-008	RF Clock Generation		Y
DP-VPX-0236-HRS-009	DDR4 Memory		Y
DP-VPX-0236-HRS-0010	Configuration Flash		Y
DP-VPX-0236-HRS-0011	eMMC NAND Flash		Y
DP-VPX-0236-HRS-0012	MRAM		Y
DP-VPX-0236-HRS-0013	EEPROM		Y
DP-VPX-0236-HRS-0014	PS Section		Y
DP-VPX-0236-HRS-0015	PL Section		Y
DP-VPX-0236-HRS-007	Test & Debug port		Y
DP-VPX-0236-HRS-0016	VPX Connector		Y
DP-VPX-0236-HRS-0017	RF Connectors		Y
DP-VPX-0236-HRS-0018	Expansion Site Connectors		Y
DP-VPX-0236-HRS-0023	Temperature Sensor		Y
DP-VPX-0236-HRS-0020	Device Drivers		Y
DP-VPX-0236-HRS-0024	OS		Y
DP-VPX-0236-HRS-0025	Voltage		Y
DP-VPX-0236-HRS-0026	Current		Y
DP-VPX-0236-HRS-0027	Power Dissipation		Y
DP-VPX-0236-HRS-0028	Dimension (LxBxH) in mm with Ruggedizer and Piggy Module					Y
DP-VPX-0236-HRS-0021	Operating Temperature	Y
DP-VPX-0236-HRS-0030	Storage Temperature	Y
DP-VPX-0236-HRS-0031	Commercial / Rugged	Y
DP-VPX-0236-HRS-0022	Thermal Dissipation	Y

QUAL TEST – If the requirement is complied with any qualification testing it comes under Qual Test. (Eg. Environment Specification).
FAT – If the requirement is complied with normal functional testing, it comes in ATP. (all the requirement which can be validated can comes under this category).
INTEGRATION – If the requirement is complied by integration testing, it comes in INTEGRATION (Unit level, System Level, External Interface level which requires external modules / system for compliance)
DEMO – If the requirement is complied with one time validation, it comes under DEMO. (The requirements which have to be qualified but not carried for the production testing)
INSPECTION –	If the requirement is complied with the physical inspection, it comes under INSPECION (Eg. Size of the module)
ANALYSIS – If the requirement is complied with the any analysis, design compliance it comes under ANALYSIS

# 13 Annexure D : Test Setup
Test Equipment s Required
This section shall be given with required test equipments, test cables (bought out), test cables (fabricated), test jig, test rig, external modules, JTAG, Emulators, software environment, programming file etc.
Table D 9 : Test Equipment To Be Used

S. No.	Equipments/ Tool	Manufacturer / (to be entered in report)	Model Number / (to be entered in report)
	Power Supply-5 V, 10A (Min)	TDK Lambda
	Power Supply-3.3 V, 3A (Min)	TDK Lambda
	Power Supply-12 V, 3A (Min)	TDK Lambda
	3U VPX Backplane	Data Patterns	DP-VPX-7196
	Test Jig	Data Patterns	DP-FAB-JIG-XXXXX
	ADM1166 sequencer cable	Analog Devices	USB-SDP-CABLEZ
	JTAG Cable	Xilinx	Digilent HS-2/HS-3
	Signal Generator (for RF/IF inputs) - 2Nos	Agilent	N5181A
	Digital Multi meter
	Test PC(1) (2No’s)	NA
	USB to Rs232/422 Converter – 2 No	Data Patterns	DP-SPL-4258-300
	Low Pass Filter (LPF) Switching Unit 1-Ch RF 50E 1.5MHz to 3GHz	Data Patterns	DP-ATE-7112-300
	FAN	NA
	Network Analyzer	Agilent
	Electronic Calibration Kit	Agilent
	SMA(F) to SMPM(F) adapter – 1 No	NA
	SATA DOM		DP-RM-BTM-34212
	Optical Transceiver
	Optical cable
	SMA(F) to SMA(F) adapter -7 Nos	In house
	50 Ohm terminator – 3 Nos	In house
	N-type to SMA Adapter	In house

Note:
(1) - Test PC 1 should have the following features :
- RAM – 4GB or more
- COM port
- Operating System – Windows 7
- Super Sequencer Evaluation Software
- WinSCP 5.19.6
- Putty
- High Speed Data Converter Pro 4.20
- Docklight
- Agilent Signal Generator driver - V 1.6.3.0
- NIVISA -V 15.01
- IVI shared Components – V2.4.2
- LATTE 2.8 version or above

 Test PC 2 should have the following features :
RAM – 4GB or more
- COM port
- Operating System – CentOS
- Vivado 2020.2 version
- Vitis 2020 version

Table D 10 : Programming file details
S. No.	CI Reference	Remarks
	DP-VPX-0236-Vx-01-U90-Rx-XXXXXXXX.zip	.bit file for FPGA Programming.
	DP-VPX-0236-V1-01-AO-ATP-ARM-LIN5V04-xVyz	Application executable
	DP-VPX-0236-V1-01-DO-ARM-LIN5V04-xVyz	Driver executable
	DP-VPX-0236-V1-01-AO-AUTOMATION-ARM-LIN5V04-xVyz	ATE Application executable
	DP-VPX-0236-V1-01-BLO-ARM-LIN5V04-xVyz	BOOT Loader Files
	DP-VPX-0236-V1-01-LIBO-ARM-LIN5V04-xVyz	Library Files
	DP-VPX-0236-V1-01-OSO-ARM-LIN5V04-xVyz	OS File
	DP-SDG-CMN-AO-HSDC-AUTO-X86-W7-xVyz	Automation GUI
	DP-VPX-0236-000-PWRSEQ-xVyz.txt	ADM1166 Programming file

Test Setup Block Diagram:

Figure 2: DP-VPX-0236 Test Setup diagram