SOFTWARE DESIGN DOCUMENT
FOR
3U VPX Zynq MPSoC with 6 Channels 14-bit 0.02 to 2GHZ I/P 3GSPS AFE7906 based Digital Receiver Module

DOCUMENT TITLE	SOFTWARE DESIGN DOCUMENT FOR 3U VPX Zynq MPSoC with 6 Channels 14-bit 0.02 to 2GHZ I/P 3GSPS AFE7906 based Digital Receiver Module DP-VPX-0233
DOCUMENT REFERENCE	DP-VPX-0233-V1-01-SDD-0V07
VERSION NUMBER	0.07
VERSION DATE	February 17, 2026
PREPARED BY	Name: Magima V M / Sign:
DOCUMENT REVIEW BY	Name: Gowthami V / Sign:
TECHNICAL REVIEW BY	Name: Kingshuk Mitra / Sign:
PROCESS REVIEW BY	Name: Gowthami V / Sign:
APPROVED BY	Name: / Sign:

Copyright @ (2025) by Data Patterns
All right reserved. These materials are proprietary to Data Patterns and no part of these materials should be reproduced, published in any form by any means, electronic or mechanical including photocopy or any information storage or retrieval system nor should the materials be disclosed to third parties without the written authorization of Data Patterns.

Revision History

S. NO.	VER. NO.	VER. DATE	CHANGED BY	SECTION (S) CHANGED	DESCRIPTION / OF CHANGE
1	0V01	03/11/2025	Magima V M	-	Initial Version
2	0V02	21/04/2025	Magima V M	Section 2.1, 2.2, 2.1.4.1.5 ,Section 5.2 , Appendix A , B	Internal Comments closed with DP-VPX-0233-SDG-SRR-0V04
3	0V03	02/05/2025	Gowthami V	Section 2.2.1.14 , 2.2.2.4 , 2.2.2.5	DRB Comments closed with DP-VPX-0233-SDG-SRR-0V05
4	0V04	10/07/2025	Magima V M	Section 2.1.4.1.6 , 2.1.4.3.7 , 2.1.4.4.4 , 5.1.2.1.6 , 5.1.2.3.7 , 5.1.2.4.4	QC Comments closed with DP-VPX-0233-SDG-SRR-0V06
5	0V05	22/07/2025	Magima V M	Section 5.1.2.3.7	DRB Comments closed with DP-VPX-0233-SDG-SRR-0V06
6	0V06	15/12/2025	Gowthami V , / Magima V M	Section 2.1 , 2.2 , 5.1	DRB Comments for TPR Documents closed with DP-VPX-0233-SDG-SRR-0V07
7	0V07	17/02/2026	Magima V M	Section 2.1.1.4.2.11 , 5.1.1.2.2.11	New requirement closed with DP-VPX-0233-SDG-SRR-0V08

# Introduction
This Software Design Document (SDD) describes the test application software design for DP-VPX-0233 module. This document uses the software requirement specification of DP-VPX-0233 to understand the hardware qualification requirements and to develop the application.

## Purpose
The purpose of this document to describe the detailed software design of application to validate DP-VPX-0233 module through console application. This document will assist the software developer in understanding the software design and also act as a guide to develop the software in terms of implementation. The design will reflect the requirements mentioned in the Software Requirements Specification (SRS) document and will be mapped with the requirement ID's for better understanding.

Table 1 :Entities involved in Test Application
Identification Number	DP-VPX-0233-V1-01-SDD-0V07
Title	SOFTWARE DESIGN DOCUMENT FOR 3U VPX Zynq MPSoC with 6 Channels 14-bit 0.02 to 2GHZ I/P 3GSPS AFE7906 based Digital Receiver Module DP-VPX-0233
Version Number	0.07
Abbreviation	SDD (Software Design Document)

## Scope
The scope of the document was able to understanding detailed information about DP-VPX-0233 components. This document is to describe design details in order to make a software developer to understand the design perspective of test cases of the module and validating the peripheral devices of the modules.

## Definitions, Acronyms, and Abbreviations

Table 2: List of Acronyms and Abbreviations
ATP	Acceptance Test Plan
UART	Universal Asynchronous Receiver Transmitter
DDR	Double Data Rate
PCI	Peripheral Component Interconnect
SRS	Software Requirement Specification
HRS	Hardware Requirement Specification
RTC	Real Time Clock
MRAM	Magneto-resistive Random Access Memory
UART	Universal Asynchronous Receiver Transmitter
USB	Universal Synchronous Bus
SATA	Serial Advanced Technology Attachment
RAM	Random Access Memory
EEPROM	Electrically Erasable Programmable Read-Only Memory
JTAG	Joint Test Action Group
FPGA	Field Programmable Gate Array
SPI	Serial Peripheral Interface
PLL	Phase Locked Loop
RF	Radio Frequency
IF	Intermediate Frequency
ADC	Analog to Digital Converter
DAC	Digital to Analog Converter
LVTTL	Low Voltage Transistor to Transistor Logic
LVDS	Low Voltage Differential Signalling
GPI/GPO	General Purpose Input / Output
NCO	Numerically Controlled Oscillator Frequency
DSA	Digital Step Attenuator

## References
Table 3: Reference Documents
S. No	Document	Board	Reference
	SRS	DP-VPX-0233	DP-VPX-0233-V1-01-SRS-0V05
	SDD	Common	DP-COMMON-SDG-SDD(ATP-ATE)-0V05-DRAFT

## Document Overview
Section 1: Describes the introduction about this SDD document.

Section 2: Describes the decomposition description of the ATP software.

Section 3: Describes the dependency description between the modules, processes and data.

Section 4: Describes the interface description of the modules and process.

Section 5: Describes the detailed design of the module and data.

Section 6: Describes the requirement traceability.

# Decomposition Description
The design specification is mainly decomposed as follows:

- Test Configuration
- Test Performance

Test Configuration
The test configuration effectively includes the configuration of the ATP test cases which describes the Manual / Auto mode test cases selection condition and test specific inputs from user. These test configuration details are stored in a file to be used for further performance of the test procedure with the same configuration details specific to the target processor.

Test Performance
The requirement of the test performance is to perform Manual /Auto mode test cases that are enabled by the user using the test configuration. Only the selected test cases will be executed.
## Module Decomposition
### DPVPX0233 Module
#### Test Configuration
The Test configuration is further decomposed as follows:
- Auto Mode Test Selection
- Manual Mode Test Selection
- Test Specific Details

Auto Mode Test Selection:
This test configuration is to enable/disable the Auto Mode test cases to be performed for the target processor.

Manual Mode Test Selection:
This test configuration is to enable/disable the Manual Mode test cases to be performed for the target processor.

Test Specific Details
This includes the test inputs specific to the enabled test cases in either or both of Auto /Manual mode test case.
#### Test Performance
The Test Performance is further decomposed into the following modules:
- Manual Mode Test Performance
- Auto Mode Test Performance

Manual Mode Test Performance
The requirement of the Manual mode test performance is to perform the manual mode test cases that are enabled by the user using the test configuration. The selected test cases will be displayed in the manual mode test case menu and can be selected to perform the particular test.

Auto Mode Test Performance
The requirement of the Auto mode test performance is to perform the auto mode test cases that are enabled by the user using the test configuration. Only the selected test cases will be executed for the number of cycles specified by the user.

The Module Decomposition are as follows:
Processing Section
1. Processor test
2. DDR4 test
3. EEPROM test
4. MRAM test
5. NOR Flash Test
6. NAND Flash test
7. USB test
8. SATA test
9. UART test
10. Ethernet test
11. RTC
12. Temperature sensor test
13. Voltage monitoring test
14. PCI Enumeration test
Programmable Logic
1. LMK PLL test
2. AFE7906 ADC test
3. DDR4 test
4. 10G Ethernet test
5. UART test
6. LVTTL test
7. LVDS test
8. GPI&GPO test
#### Processing Section
This Section will hold the module decomposition for the Processing section.

##### Processor test

This test shall be performed to qualify the ALU and FPU in the processor board by carrying out the following test cases. Refer the section 2.2.1.1.1 and 5.1.1.1.1 for Data decomposition and Flowchart.
###### ALU Test
Refer the section 5.1.1.1.1.1 for Flowchart.
Requirement ID	DP_VPX_0233_MANUAL_PS_PRCS_01
Design Details	In Addition test, two constant decimal numbers are added that are expected for the defined result. If the actual result is not equal to the expected result then print “Arithmetic addition operation: Failed” along with the expected and actual data, else continue to subtraction test / In Subtraction test, two constant decimal numbers are subtracted that are expected for the defined result. If the actual result is not equal to the expected result then print “Arithmetic subtraction operation: Failed” along with the expected and actual data, else continue to Multiplication test. / In Multiplication test, two constant decimal numbers are multiplied that are expected for the defined result. If the actual result is not equal to the expected result then print “Arithmetic Multiplication operation: Failed” along with the expected and actual data, else continue to Division test. / In Division test, two constant decimal numbers are divided that are expected for the defined result. If the actual result is not equal to the expected result then print “Arithmetic Division operation : Failed” along with the expected and actual data, else continue to Left shift test. / In Left Shift test, the value is left shifted by and expected for the defined result If the actual result is not equal to the expected result then print “Left shift operation: Failed” along with the expected and actual data, else continue to Right shift test. / In Left Shift test, the value is right shifted by and expected for the defined result. If the actual result is not equal to the expected result then print “Right shift operation: Failed” along with the expected and actual data, else continue to AND test / In AND test, the value is logical AND by and expected for the defined result. If the actual result is not equal to the expected result then print “Logical AND operation: Failed” along with the expected and actual data, else continue to OR test / In OR test, the value is logical OR by and expected for the defined result. If the actual result is not equal to the expected result then print “Logical OR operation: Failed” along with the expected and actual data, else continue to NOT test. / In NOT test, the value is logical NOT performed on the value and expected for the defined result.. If the actual result is not equal to the expected result then print “Logical OR operation: Failed” along with the expected and actual data, else print “ALU Test : Success” and then return.

###### FPU Test

Refer the section 5.1.1.1.1.2 for Flowchart.
Requirement ID	DP_VPX_0233_MANUAL_PS_PRCS_02
Design Details	In Floating point addition test, two constant decimal numbers are added that are expected for the defined result. If the actual result is not equal to the expected result then print “Floating point addition: Failed” along with the expected and actual data, else continue to floating point subtraction test. / In Floating point subtraction test, two constant decimal numbers are subtracted that are expected for the defined result. If the actual result is not equal to the expected result then print “Floating point subtraction : Failed” along with the expected and actual data, else continue to floating point multiplication test. / In Floating point multiplication test, two constant decimal numbers are multiplied that are expected for the defined result. If the actual result is not equal to the expected result then print “Floating point multiplication: Failed” along with the expected and actual data, else continue to floating point division test. / In Floating point division test, two constant decimal numbers are divided that are expected for the defined result. If the actual result is not equal to the expected result then print “Floating point division: Failed” along with the expected and actual data, else print “FPU test : Success” and then return.

##### DDR4 Test
This test shall be perform to qualify the DDR4 by carrying out to perform the following test cases. Refer the section 2.2.1.1.2 and 5.1.1.1.2 for Data decomposition and Flowchart.
###### Data Bus Test

Refer the section 5.1.1.1.2.1 for Flowchart.
Requirement ID	DP_VPX_0233_MANUAL_PS_DDR4_01
Design Details	Perform memory walking ones test by shifting data to the left and writing 1 bit at a time until you reach 64th bit, read data from the same memory location. / If write data and read data are not same print “Walking one’s test : Failed” along with the address ,expected and actual data. Else perform the walking zero’s test , / Perform memory walking zeros test by complement and shifting data to the left and writing 1 bit at a time until you reach 64 bits, read data from the same memory location. / If write data and read data are not same print “Walking zero’s test : Failed” along with the address ,expected and actual data. Else print “Data bus test : Success” and then return.

###### Address Bus Test
Refer the section 5.1.1.1.2.2 for Flowchart.
Requirement ID	DP_VPX_0233_MANUAL_PS_DDR4_02
Design Details	PATTERN data will be written in allocated memory of a particular size, ANTIPATTERN data will be written to the base address. Read all address values. / Check if the content of all the address except base address is PATTERN. If its content is not equal to PATTERN, then print “Pattern test : Failed” along with the offset, actual and excepted data. Else reinitialize the base address with PATTERN. / ANTIPATTERN data will be written to memory of a particular size. Read all address values. / Check if the content of all the address except base address is a ANTIPATTERN. If its content is not equal to ANTIPATTERN, then If content is not equal to PATTERN, then print “Anti Pattern test : Failed” along with the offset, actual and excepted data. Else print the “Address bus test: Success”.

###### Device Test
- Refer the section 5.1.1.1.2.3 for Flowchart.
Requirement ID	DP_VPX_0233_MANUAL_PS_DDR4_03
Design Details	Write 64 bit incremental counter data to allocated memory of a certain size. / Read the data from first memory location and check for previously written data, If both are not same then print “Increment counter test: Failed” along with the offset, expected data and actual data. / Else write the inverted incremental counter data to the same location. Repeat this sequence for all memory location until the maximum size is reached. / Read the data from first memory location and check the previously written inverted data. If both are not same then print “Inverted counter test: Failed” along with the offset, expected data and actual data. / Else the print “Device test : Success” and then return.

##### EEPROM Test
This test shall be performed to qualify the EEPROM device by carrying out the following test cases. Refer the section 2.2.1.1.3 and 5.1.1.1.3 for Data decomposition and Flowchart.
###### Upload Board Information
- Refer the section 5.1.1.1.3.1 for Flowchart.
Requirement ID	DP_VPX_0233_MANUAL_PS_EEPROM_01
Design Details	Write the board information data to the device. / Read board information from the device which was already written in the EEPROM. / Compare the read data with the board information data which is stored in the board information structure. / If both are not same then print “Upload board information Failed” along with structure field, excepted and actual data, else print “Upload board information : Success” and then return. / Note: Upload Board Information Test shall be done only once in a board.

###### Data Retention Test
- Refer the section 5.1.1.1.3.2 for Flowchart.
Requirement ID	DP_VPX_0233_MANUAL_PS_EEPROM_02
Design Details	Read the board signature from the device. / Compare the read data with the Board info which is stored in the board information structure. / If both are not same then print “Data Retention : Failed” along with the excepted and actual Board ID, else print “Data Retention : Success” and then return / Note: The system need to verify the data retention test after restart.

###### Checksum Test
- Refer the section 5.1.1.1.3.3 for Flowchart.
Requirement ID	DP_VPX_0233_MANUAL_PS_EEPROM_03
Design Details	Read the previously written data from a fixed area of the device and calculate the checksum from the read data omitting checksum field. / Compare the calculated checksum with the checksum field in the read board information structure. / If both are not same then print “Checksum : Failed” along with the excepted and actual Checksum, else print “Checksum : Success” and then return.

###### Read/Write Test

- Refer the section 5.1.1.1.3.4 for Flowchart.
Requirement ID	DP_VPX_0233_MANUAL_PS_EEPROM_04
Design Details	Get the address, location number and entry pattern from the user. / Write the data to the memory locations specified in the device. / Read the data from the same location in the device, compare the data. If both are not same then the print “Read/Write : Failed” along with excepted and actual data, Else print the “Read/ Write : Success” and then return.

##### MRAM Test
This test shall be performed to qualify the MRAM device by carrying out the following test cases. Refer the section 2.2.1.1.4 and 5.1.1.1.4 for Data decomposition and Flowchart.
###### Upload Board Information
- Refer the section 5.1.1.1.4.1 for Flowchart.
Requirement ID	DP_VPX_0233_MANUAL_PS_MRAM_01
Design Details	Refer the Section 2.1.1.3.3.1

###### Data Retention Test
- Refer the section 5.1.1.1.4.2 for Flowchart.
Requirement ID	DP_VPX_0233_MANUAL_PS_MRAM_02
Design Details	Refer the Section 2.1.1.3.3.2

###### Checksum Test
- Refer the section 5.1.1.1.4.3 for Flowchart.
Requirement ID	DP_VPX_0233_MANUAL_PS_MRAM_03
Design Details	Refer the Section 2.1.1.3.3.3

###### Full Memory Test

- Refer the section 5.1.1.1.4.4 for Flowchart.
Requirement ID	DP_VPX_0233_MANUAL_PS_MRAM_04
Design Details	Write the counter data to the all memory location except the board information location. / Read the counter data from the memory locations. / Compare the write and read data from the device. / If both are not same then print “Full memory test : Failed” along with the excepted and actual data, else print “Full memory test : Success” and then return.

##### NAND Flash Test
This test shall be performed to qualify the data flash device by carrying out the following test cases. Refer the section 2.2.1.1.5 and 5.1.1.1.5 for Data decomposition and Flowchart.

###### Upload Board Information
Refer the section 5.1.1.1.5.1 for Flowchart.

Requirement ID	DP_VPX_0233_MANUAL_PS_NAND_01
Design Details	Refer the Section 2.1.1.3.3.1

###### Data Retention Test
- Refer the section 5.1.1.1.5.2 for Flowchart.
Requirement ID	DP_VPX_0233_MANUAL_PS_NAND_02
Design Details	Refer the Section 2.1.1.3.3.2

###### Check Sum Test
- Refer the section 5.1.1.1.5.3 for Flowchart.
Requirement ID	DP_VPX_0233_MANUAL_PS_NAND_03
Design Details	Refer the Section 2.1.1.3.3.3

##### NOR Flash Test
This test shall be performed to qualify the user flash device by carrying out the following test cases. Refer the section 2.2.1.1.6 and 5.1.1.1.5.4 for Data decomposition and Flowchart.
###### Upload Board Information test
- Refer the section 5.1.1.1.5.5 for Flowchart.
Requirement ID	DP_VPX_0233_MANUAL_PS_NOR_01
Design Details	Refer the Section 2.1.1.3.3.1

###### Data Retention Test
- Refer the section 5.1.1.1.5.6 for Flowchart.
Requirement ID	DP_VPX_0233_MANUAL_PS_NOR_02
Design Details	Refer the Section 2.1.1.3.3.2

###### Check Sum Test
Refer the section 5.1.1.1.5.7 for Flowchart.
Requirement ID	DP_VPX_0233_MANUAL_PS_NOR_03
Design Details	Refer the Section 2.1.1.3.3.3

##### USB Test

This test shall be performed to qualify the USB port by carrying out the following test cases. Refer the section 2.2.1.1.7 and 5.1.1.1.6 for Data decomposition and Flowchart.

###### Read/Write test

Refer the section 5.1.1.1.6.1 for Flowchart.

Requirement ID	DP_VPX_0233_MANUAL_PS_USB_01
Design Details	Get the device name / mount path (e.g sda1, sdb1) to be tested from the user. / Mount the device (if required, based on the OS/firmware) through the standard OS command / Create a file in mounted device. / If file creation failed then print “CREATE AND OPEN FILE FAILED”. / Else write the sample data and close the file. / Re-open the file and read the data from the file. / Verify the read data with the previously written data. / If both are not same then print “DATA NOT MATCHING” along with the expected and actual data. / Else delete the file created on the device. / Check whether the file is deleted or not. / If the file is not deleted then then print “DELETE FILE FAILED” else print “READ / WRITE TEST PASSED”. / Unmount the device and then return. / Note : A text file with name “USBTest.txt“ will be created for this test.

##### SATA Test
This test shall be performed to qualify the SATA interface by carrying out the following case. Refer the section 2.2.1.1.8 and 5.1.1.1.7 for Data decomposition and Flowchart.
###### Read/Write test

Refer the section 5.1.1.1.7.1 for Flowchart.
Requirement ID	DP_VPX_0233_MANUAL_PS_SATA_01
Design Details	Refer the Section 2.1.1.3.7.1

##### UART Test

This test shall be performed to qualify the UART module by carrying out the following test cases. Refer the section 2.2.1.1.9 and 5.1.1.1.8 for Data decomposition and Flowchart.
###### Write test

- Refer the section 5.1.1.1.8.1 for Flowchart.
Requirement ID	DP_VPX_0233_MANUAL_PS_UART_01
Design Details	Select the COM port to be tested. / Get the Baud rate, number of stop bits and parity from user. / Ask the user whether you want to enter the data or not. / If yes, get the data to transmit from user else use fixed data of 256bytes. / Open the COM port with selected baud rate, number of stop bits and parity. / Ensure that the external system's COM port is configured with same baud rate and parity. / Send the data to the external system. / If Data Sent is same as the data received at the external system then consider it as Success / Note: Using the Docklite software to test the UART module.

###### Read Test

- Refer the section 5.1.1.1.8.2 for Flowchart.
Requirement ID	DP_VPX_0233_MANUAL_PS_UART_02
Design Details	Select the COM port to be tested. / Get the Baud rate, number of stop bits and parity from user. / Open the COM port with selected baud rate, number of stop bits and parity. / Ensure that the external system's COM port is configured with same baud rate and parity. / Send the data From the external system. / If Data received is same as the data sent from the external system then consider it as Success / Note: Using the Docklite software to test the UART module.

##### Ethernet Test

This test shall be performed to qualify the Ethernet module and optical transceiver by carrying out the following test cases. Refer the section 2.2.1.1.10 and 5.1.1.1.9 for Data decomposition and Flowchart.

###### Ethernet Ping test
- Refer the section 5.1.1.1.9.1 for Flowchart.
Requirement ID	DP_VPX_0233_MANUAL_PS_ETHERNET_01
Design Details	Get the IP Address and the number of times to ping the IP address from the user. / Ping the IP address using standard OS command. Set the target IP address ping up to the number of times specified by the user. / If data is sent and received not Successfully, then print “Ethernet ping test : Failed” else print “Ethernet Ping test : Success” and then return.

##### RTC test

This test shall be performed to qualify the RTC device. Refer the section 2.2.1.1.11 and 5.1.1.1.10 for data decomposition and flowchart.

Requirement ID	DP_VPX_0233_MANUAL_PS_RTC
Design Details	Get the date and time from the user. / Set the entered date and time to the RTC. / Wait for 8 seconds. / Read the date and time from RTC. / Print the values and compare the values with the expected date and time with +/-1 second tolerance. / If the values matches then print “RTC TEST PASSED” else print “RTC TEST FAILED”.

##### PCI Enumeration Test

This test shall be performed to qualify the PCI interface. Refer the section 2.2.1.1.12 and 5.1.1.1.11 for data decomposition and flowchart.

Requirement ID	DP_VPX_0233_MANUAL_PS_PCI
Design Details	Get the Vendor ID, Device ID and Device count of devices to be enumerated from the user. / Enumerate all the PCI devices available on the board. / Compare the enumerated devices with the expected devices. / Print all the matched device. / Print all the new device (if any). / If all the expected devices are enumerated then print “PCI ENUMERATION TEST PASSED” else print “PCI ENUMERATION TEST FAILED”.

##### Temperature sensor test
This test shall be performed to qualify the temperature sensor. Refer the section 2.2.1.1.13 and 5.1.1.1.12 for Data decomposition and Flowchart.

Requirement ID	DP_VPX_0233_MANUAL_PS_TEMPSNSR
Design Details	Open the temperature sensor device, Set the lower and upper limits of local [ -10 to 70 ] and external temperature to the device [ -10 to 70 ]. / Mentioned limits are write in the device, Get the lower and upper limit of local and external temperature from the device. / Get the current local and external temperature from the device. / Check whether the read temperature values are between the upper and lower limit. / If the temperatures are not within the defined limit then print “Temperature Sensor test : Failed” else print “Temperature Sensor test : Success”.

##### Voltage Monitoring test
This test shall be performed to report the ADM input channel voltages of processor. Refer the section 2.2.1.1.14 and 5.1.1.1.13 for Data decomposition and Flowchart.

Requirement ID	DP_VPX_0233_MANUAL_PS_ADM
Design Details	Get the upper and lower limits for all channels from the file and read the ADM input channel from processor. / Display the read voltages limits on the console. / Check whether the read voltages within the user given limits, / If voltages are not in the given limits then print “Voltage Monitoring test : Failed” else print “Voltage Monitoring test : Success”. / Note: The voltage limits are given in a ADM limit file “dpvpx0233_adm_limits.txt”.

#### Programmable Logic
This Section will hold the module decomposition for the Programmable logic section.

##### LMK PLL Test

 This test shall be performed to qualify the LMK PLL Test. Refer the section 2.2.1.2.1 and 5.1.1.2.1 for Data decomposition and Flowchart.
###### File Configuration

- Refer the section 5.1.1.2.1.1 for Flowchart.
Requirement ID	DP_VPX_0233_MANUAL_PL_LMK_PLL_01
Design Details	Validate the Handle. / Get the configuration file name from the user. / Check whether the file is present or not. / Read Data from the configuration file. / Write Data to the corresponding FPGA Registers. / If File write process completed then the test case is declared as Success, else it declared as Failure.

###### File Dump
- Refer the section 5.1.1.2.1.2 for Flowchart.
Requirement ID	DP_VPX_0233_MANUAL_PL_LMK_PLL_02
Design Details	Validate the Handle. / Get the configuration file name from the user. / Check whether the file is present or not. / Read Data from the corresponding FPGA Registers and store it in the Output file. / If File Read process completed, then the test case is declared as Success, else it declared as Failure.

###### Single Data Write

- Refer the section 5.1.1.2.1.3 for Flowchart.
Requirement ID	DP_VPX_0233_MANUAL_PL_LMK_PLL_03
Design Details	Validate the Handle. / Get the address and Data from the user. / Write the Data and Address in the corresponding FPGA Registers. / If write was completed then the test case is declared as Success, else it declared as Failure.

###### Single Data Read

- Refer the section 5.1.1.2.1.4 for Flowchart.
Requirement ID	DP_VPX_0233_MANUAL_PL_LMK_PLL_04
Design Details	Validate the Handle. / Get the address from the user. / Read the Data from the Corresponding FPGA Read register. / If Read was completed then the test case is declared as Success, else it declared as Failure.

###### PLL Lock Status

- Refer the section 5.1.1.2.1.5 for Flowchart.
Requirement ID	DP_VPX_0233_MANUAL_PL_LMK_PLL_05
Design Details	Validate the Handle. / Read lock status from the corresponding PLL status register. / If the read data is equal to 0x30 , then the test case is declared as Success, else it declared as Failure.

###### Sysref Enable/Disable

Refer the section 5.1.1.2.1.6 for Flowchart.
###### Sysref Enable

Refer the section 5.1.1.2.1.6.1 for Flowchart.
Requirement ID	DP_VPX_0233_MANUAL_PL_LMK_PLL_06_01
Design Details	Validate the Handle. / Write Data 0x15 in the corresponding register. / If the write process completed, then the test case is declared as Success, else it declared as Failure.

###### Sysref Disable

Refer the section 5.1.1.2.1.6.2 for Flowchart.
Requirement ID	DP_VPX_0233_MANUAL_PL_LMK_PLL_06_02
Design Details	Validate the Handle. / Write Data 0x5 in the corresponding register. / If the write process completed, then the test case is declared as Success, else it declared as Failure.

##### AFE7906 ADC Test

The purpose of this test is to qualify the AFE7906 ADC by carrying out the following test cases.
Refer the section 2.2.1.2.2 and 5.1.1.2.2 for data decomposition and flowchart.

###### AFE Core Reset
Refer the section 5.1.1.2.2.1 for Flowchart.
Requirement ID	DP_VPX_0233_MANUAL_PL_AFE7906_ADC_01
Design Details	Validate the Handle. / Reset the AFE chip by writing 1 and 0 in the corresponding FPGA Registers. / If Reset was Completed then the test case is declared as Success, else it declared as Failure.

###### AFE Single Write
Refer the section 5.1.1.2.2.2 for Flowchart.

Requirement ID	DP_VPX_0233_MANUAL_PL_AFE7906_ADC_02
Design Details	Validate the Handle. / Get the address and Data from the user. / Write the Data and Address in the corresponding FPGA Registers. / If write was completed then the test case is declared as Success, else it declared as Failure.

###### AFE Single Read
Refer the section 5.1.1.2.2.3 for Flowchart.
Requirement ID	DP_VPX_0233_MANUAL_PL_AFE7906_ADC_03
Design Details	Validate the Handle. / Get the address from the user. / Read the Data from the Corresponding FPGA Read register. / If Read was completed then the test case is declared as Success, else it declared as Failure.

###### AFE Bring up

Refer the section 5.1.1.2.2.4 for Flowchart.
Requirement ID	DP_VPX_0233_MANUAL_PL_AFE7906_ADC_04
Design Details	Validate the Handle. / Get the ADC Configuration File from the user. / Write the Data and Read the Data From the corresponding FPGA Registers. / If File Configuration is completed, then the test case is declared as SUCCESS, else it declared as FAIL.

###### AFE Core Initialization

Refer the section 5.1.1.2.2.5 for Flowchart.
Requirement ID	DP_VPX_0233_MANUAL_PL_AFE7906_ADC_05
Design Details	Validate the Handle. / Write corresponding Data to the FPGA Register. / Then Read the Core Initialization Data from the Corresponding Read Register. / Compare the Read Data it must be equal to 0xFFFFF. / If Comparison was Success, then declare the test case as SUCCESS, else it declared as FAIL.

###### JESD Bond status
Refer the section 5.1.1.2.2.6 for Flowchart.
Requirement ID	DP_VPX_0233_MANUAL_PL_AFE7906_ADC_06
Design Details	Validate the Handle. / Write corresponding Data to the FPGA Register. / Then Read the JESD Bond status from the corresponding FPGA Register. / If 1st bit is in high then chip is configured and JESD is Bonded Successfully, else declare it as FAIL.

###### ADC Data Logging
Refer the section 5.1.1.2.2.7 for Flowchart.
Requirement ID	DP_VPX_0233_MANUAL_PL_AFE7906_ADC_07
Design Details	Validate the Handle. / Validate the Rx Channel Selection. / Validate the Sample count. / Select the Rx channel by writing channel number in the corresponding FPGA Register. / Clear the ADC by writing Corresponding Data in the ADC Reset Register. / Read the FIFO count from the corresponding Register. / FIFO count must be greater or equal to the number of samples entered by user. / Read the Data from the corresponding FPGA Register and log in to a File. / Note: 6 number of Rx channels are available to collect Data.

###### HD2 Correction Enable

Refer the section 5.1.1.2.2.8 for Flowchart.
###### HD2 Coefficient Write

Refer the section 5.1.1.2.2.8.1 for Flowchart.

Requirement ID	DP_VPX_0233_MANUAL_PL_AFE7906_ADC_08_01
Design Details	Validate the Handle. / Validate the Rx Channel Selection. / Enable the HD2 pages by writing corresponding values in the corresponding registers. / Write the channel selection Data in the corresponding Register. / Get 2129 and 212a Data from the user . / Enable the write sequence by writing corresponding data in the corresponding Registers. / If write is completed, then declare the test case as SUCCESS, else declare it as FAIL. / Note: This sequence was shared by TI.

###### HD2 Coefficient Read

Refer the section 5.1.1.2.2.8.2 for Flowchart.

Requirement ID	DP_VPX_0233_MANUAL_PL_AFE7906_ADC_08_02
Design Details	Validate the Handle. / Validate the Channel Selection. / Write the channel selection Data in the corresponding Register. / Read the Data from 2129 and 212a . / Display the Read values. / If Reading Data is completed, then declare the test case as SUCCESS, else declare it as FAIL.

###### NCO Update

Refer the section 5.1.1.2.2.9 for Flowchart.
###### All Channel Enable

Refer the section 5.1.1.2.2.9.1.1 for Flowchart.

Requirement ID	DP_VPX_0233_MANUAL_PL_AFE7906_ADC_09_01
Design Details	Validate the Handle. / Write the Data 0x3F to the corresponding FPGA register to enable all channel NCO update. / If write is completed, then declare the test case as SUCCESS, else declare it as FAIL.

###### Single Channel Enable

Refer the section 5.1.1.2.2.9.1.2 for Flowchart.
.
Requirement ID	DP_VPX_0233_MANUAL_PL_AFE7906_ADC_09_02
Design Details	Validate the Handle. / Get the channel Number from the user. / Validate the channel Number. / Write the Data to the corresponding FPGA Register to enable single channel NCO update. / If write is completed, then declare the test case as SUCCESS, else declare it as FAIL.

###### All Channel Disable

Refer the section 5.1.1.2.2.9.2.1 for Flowchart.
Requirement ID	DP_VPX_0233_MANUAL_PL_AFE7906_ADC_09_03
Design Details	Validate the Handle. / Write the Data 0x0 to the corresponding FPGA register to enable all channel NCO update. / If write is completed, then declare the test case as SUCCESS, else declare it as FAIL.

###### Single Channel Disable

Refer the section 5.1.1.2.2.9.2.2 for Flowchart.

Requirement ID	DP_VPX_0233_MANUAL_PL_AFE7906_ADC_09_04
Design Details	Validate the Handle. / Get the channel Number from the user. / Validate the channel Number. / Write the Data to the corresponding FPGA Register to disable single channel NCO update. / If write is completed, then declare the test case as SUCCESS, else declare it as FAIL.

###### ADC Dynamic Configuration

ADC Dynamic Configuration shall be a part of the Acceptance test application and shall be performed to update NCO and DSA Settings.

Refer the section 5.1.1.2.2.10 for Flowchart.

###### Device Health Status

Refer the section 5.1.1.2.2.10.1 for Flowchart.

Requirement ID	DP_VPX_0233_MANUAL_PL_AFE7906_ADC_10_01
Design Details	Read the Health status of the chip from the corresponding registers. / If read is completed, then declare the test case as SUCCESS, else declare it as FAIL.

###### Update Rx NCO

Refer the section 5.1.1.2.2.10.2 for Flowchart.

Requirement ID	DP_VPX_0233_MANUAL_PL_AFE7906_ADC_10_02
Design Details	Get the Rx Mixer frequency from the user in MHZ / Get the Rx Band number from the user / Get the Rx NCO number from the user. / Write the Data in the corresponding Registers. / If Write process completed, then declare the test case as Success, else declare it as Failure. / Note: The Rx mixer Frequency varies from [0 MHz - 2457.6 MHz) / The Band Number and NCO number varies inbetween[0-1].

###### Set Rx DSA

Refer the section 5.1.1.2.2.10.3 for Flowchart.

Requirement ID	DP_VPX_0233_MANUAL_PL_AFE7906_ADC_10_03
Design Details	Get the Attentuation value from the user. / Write the value in the corresponding registers. / If write is completed, then declare the test case as SUCCESS, else declare it as FAIL. / Note: The DSA Value varies from 0 to 25 dbfs.

###### Update Fb NCO

Refer the section 5.1.1.2.2.10.4 for Flowchart.

Requirement ID	DP_VPX_0233_MANUAL_PL_AFE7906_ADC_10_04
Design Details	Refer the Section 2.1.1.4.2.10.2

###### Set Fb DSA
- Refer the section 5.1.1.2.2.10.5 for Flowchart.
Requirement ID	DP_VPX_0233_MANUAL_PL_AFE7906_ADC_10_05
Design Details	Refer the Section 2.1.1.4.2.10.3

###### Read Rx NCO

Refer the section 5.1.1.2.2.10.7 for Flowchart.
Requirement ID	DP_VPX_0233_MANUAL_PL_AFE7906_ADC_10_06
Design Details	Get the Rx Band number from the user. / Get the Rx NCO number from the user. / Read the data from the corresponding register. / If read is completed, then declare the test case as SUCCESS, else declare it as FAIL.

###### Read Fb NCO

Refer the section 5.1.1.2.2.10.6 for Flowchart.

Requirement ID	DP_VPX_0233_MANUAL_PL_AFE7906_ADC_10_07
Design Details	Refer the Section 2.1.1.4.2.10.6

###### Band Selection
Refer the section 5.1.1.2.2.11 for Flowchart.

Requirement ID	DP_VPX_0233_MANUAL_PL_AFE7906_ADC_11
Design Details	Validate the Handle. / Write 0x1 in ADC Band Selection Register for selecting NARROW Band. / Write 0x0 in ADC Band Selection Register for selecting WIDE Band.

###### ADC Automation
ADC Automation shall be a part of the acceptance test application and shall be performed to automate the data logging and phase matching.
###### Data Logging
###### Host Application
Requirement ID	DP_VPX_0233_MANUAL_PL_AFE7906_ADC_12_01_01
Design Details	Connect the Host application with Target application by click on “Initialize”. / Enter the configured IP address of Target in GUI panel. / Get the Rx channel number, no. of samples and Input file from the User. Then, Click on “Start” Button. / Frame the command packet with Command ID and Test ID send to target application. / Receive the response packet From target and Display the result in the GUI panel. / On Successful transmission it displays success message, else it displays the error message or failure message. / Note : HSDC Pro Required for this automation.

###### Target Application

Requirement ID	DP_VPX_0233_MANUAL_PL_AFE7906_ADC_12_01_02
Design Details	Receive the Command Packet from Host. / Execute the test case based on the Command ID and Test ID. / Read the Data from the corresponding FPGA Register(Refer Section 2.1.1.4.2.7 ). / Frame the Response packet and send to Host application.

###### Phase Matching
###### Host Application
Requirement ID	DP_VPX_0236_MANUAL_PL_AFE7906_ADC_12_02_01
Design Details	Connect the Host application with Target application by click on “Initialize”. / Enter the configured IP address of Target in GUI panel. / Click on “Phase Matching” button. / Frame the command packet with Command ID and Test ID send to target application. / Receive the response packet From target and Display the result in the GUI panel. / On Successful transmission it displays success message, else it displays the error message or failure message. / Note : Refer Appendix B for detailed description.

###### Target Application
Requirement ID	DP_VPX_0236_MANUAL_PL_AFE7906_ADC_12_02_02
Design Details	Receive the Command Packet from Host. / Execute the test case based on the Command ID and Test ID. / Validate the Handle. / Validate the Sample count. / Select the Rx channel by writing channel number in the corresponding FPGA Register. / Clear the ADC by writing Corresponding Data in the ADC Reset Register. / Read the FIFO count from the corresponding Register. / FIFO count must be greater or equal to the number of samples entered by user. / Read the Data from the corresponding FPGA Register and log in to a Files. / Frame the Response packet and send to Host application. / Note: 5 number of Rx and 1 number of Fb channels are available to collect Data at a time.

##### LVTTL Test

This test shall be performed to qualify LVTTL test. Refer the section 2.2.1.2.3and 5.1.1.2.3 for Data decomposition and flowchart.
###### IO Mode Test

        Refer the Section 5.1.1.2.3.1 for flow chart.

Requirement ID	DP_VPX_0233_MANUAL_PL_LVTTL_01
Design Details	Select any one of the four available registers[1-4]. / Write ZERO in the IO DATA SELECTION REGISTER . / Write 0x7 in the IO DIRECTION BUFFER OUTPUT REGISTER. / Write the pattern data(walking one's) to input channels. / Read the data through the output channels. / Compare the write and read data. / If both are not same print “LVTTL WALKING 1's TEST FAILED” along with the write and read data. / Write the pattern data(walking zero's) to input channels. / Read the data through the output channels. / Compare the write and read data. / If both are not same print “LVTTL WALKING 0's TEST FAILED” along with the write and read data. / If IO Validation completed then print LVTTL IO VALIDATION: SUCCESS, Otherwise LVTTL IO VALIDATION: FAILED.

###### Clock Mode Test
        Refer the Section 5.1.1.2.3.2 for flow chart.

Requirement ID	DP_VPX_0233_MANUAL_PL_LVTTL_02
Design Details	Write 0xFFFFFFFF in the IO DATA SELECTION REGISTER. / Write 0x7 in the IO DIRECTION BUFFER OUTPUT REGISTER. / Read the ON time and OFF time from the corresponding LVTTL CLOCK VALIDATION REGISTER [1 – 8]. / Compare the ON time and OFF time for each and every IO’s. / If the ON time and OFF time are within the limit print LVTTL CLOCK VALIDATION: SUCCESS, Otherwise LVTTL CLOCK VALIDATION: FAILED. / Note: A clock frequency of 1MHz will be generated.

###### Manual IO Mode Test

        Refer the Section 5.1.1.2.3.3 for flow chart.
Requirement ID	DP_VPX_0233_MANUAL_PL_LVTTL_03
Design Details	Select One of the available Four sets[1-4]. / Write ZERO in the IO DATA SELECTION REGISTER. / Write 0x7 in the IO DIRECTION BUFFER OUTPUT REGISTER. / Write the Data in the LVTTL IO DATA OUT REGISTER. / If Manual Mode Test completed then print LVTTL Manual IO Mode Test: SUCCESS, Otherwise LVTTL Manual IO Mode Test: FAILED.

###### Manual Clock Mode Test

        Refer the Section 5.1.1.2.3.3.1 for flow chart.
###### Manual Clock ON Test

 Refer the Section 5.1.1.2.3.3.1.1 for flow chart.

Requirement ID	DP_VPX_0233_MANUAL_PL_LVTTL_04_01
Design Details	Validate the Handle. / Write 0xFFFFFFFF in the IO Data Selection Register. / Write 0xFFFFFFFF in the corresponding Register. / Write 0xF in the IO Direction Buffer Output Register. / If Manual clock Mode Test completed then print LVTTL Manual Clock ON Test: SUCCESS, Otherwise LVTTL Manual Clock ON Test: FAILED.

###### Manual Clock OFF Test

 Refer the Section 5.1.1.2.3.3.1.2 for flow chart.

Requirement ID	DP_VPX_0233_MANUAL_PL_LVTTL_04_02
Design Details	Validate the Handle. / Write 0x0 in the IO Data Selection Register. / Write 0x0 in the corresponding Register. / Write 0x0 in the IO Direction Buffer Output Register. / If Manual clock Mode Test completed then print LVTTL Manual Clock OFF Test: SUCCESS, Otherwise LVTTL Manual Clock OFF Test: FAILED.

##### LVDS Test

 This test shall be used to perform the LVDS test. Refer the section 2.2.1.2.4 and 5.1.1.2.4 for Data decomposition and flowchart.
###### IO Mode Test
        Refer the Section 5.1.1.2.4.1 for flow chart.

Requirement ID	DP_VPX_0233_MANUAL_PL_LVDS_01
Design Details	Select any one of the Three available registers[1-3]. / Write ZERO in the IO DATA SELECTION REGISTER . / Write 0x7 in the IO DIRECTION BUFFER OUTPUT REGISTER. / Write the pattern data(walking one's) to input channels. / Read the data through the output channels. / Compare the write and read data. / If both are not same print “LVDS WALKING 1's TEST FAILED” along with the write and read data. / Write the pattern data(walking zero's) to input channels. / Read the data through the output channels. / Compare the write and read data. / If both are not same print “LVDS WALKING 0's TEST FAILED” along with the write and read data. / If IO Validation completed then print LVDS IO VALIDATION: SUCCESS, Otherwise LVDS IO VALIDATION: FAILED.

###### Clock Mode Test
        Refer the Section 5.1.1.2.4.2 for flow chart.
Requirement ID	DP_VPX_0233_MANUAL_PL_LVDS_02
Design Details	Write 0xFFFFFFFF in the IO DATA SELECTION REGISTER. / Write 0xF in the IO DIRECTION BUFFER OUTPUT REGISTER. / Read the ON time and OFF time from the corresponding LVDS CLOCK VALIDATION REGISTER [1 – 2]. / Compare the ON time and OFF time for each and ever IO’s. / If the ON time and OFF time are within the limit print LVDS CLOCK VALIDATION: SUCCESS, Otherwise LVDS CLOCK VALIDATION: FAILED / Note: A clock frequency of 1MHz will be generated.

###### Manual Mode Test
        Refer the Section 5.1.1.2.4.3 for flow chart.
Requirement ID	DP_VPX_0233_MANUAL_PL_LVDS_03
Design Details	Select One of the available Three sets.[1-3] / Write ZERO in the IO DATA SELECTION REGISTER. / Write 0xF in the IO DIRECTION BUFFER OUTPUT REGISTER. / Write the Data in the LVDS IO DATA OUT REGISTER. / If Manual Mode Test completed then print LVDS Manual Mode Test: SUCCESS, Otherwise LVDS Manual Mode Test: FAILED.

##### GPI/GPO Test

     This test is used to qualify the GPI/GPO test. Refer the section 2.2.1.2.5and 5.1.1.2.5 for Data decomposition and flowchart.

###### IO Mode Test
        Refer the Section 5.1.1.2.5.1 for flow chart.
Requirement ID	DP_VPX_0233_MANUAL_PL_GPI_GPO_01
Design Details	Write ZERO in the IO DATA SELECTION REGISTER . / Write 0xF in the IO DIRECTION BUFFER OUTPUT REGISTER. / Get the IO Data from the user [0 / 1] . / Write the data to the output channel. / Read the data from the input channel. / Compare the write and read data. / If both are not same print “GPI GPO Data Comparison Failed” along with the write and read data. / If IO Validation completed then print GPI GPO IO VALIDATION: SUCCESS, Otherwise GPI GPO IO VALIDATION: FAILED.

##### UART(PL) Test

    This test is used to qualify UART Interface. Refer the section 2.2.1.2.6and 5.1.1.2.6 for Data decomposition and flowchart.

###### Write test
- Refer the section for 5.1.1.2.6.2 Flowchart.
Requirement ID	DP_VPX_0233_MANUAL_PL_UART_01
Design Details	Get the Input Data from the User / Write Input data in the corresponding FPGA Register. / If Data sent is same as the Data received at the external system then consider it as Success, else consider as Failure.

###### Read Test

Refer the section for 5.1.1.2.6.1 Flowchart.

Requirement ID	DP_VPX_0233_MANUAL_PL_UART_02
Design Details	Send the data from the external system / Read the data count from the corresponding FPGA Register. / Read the data from the corresponding FPGA Register with respect to the count. / If Data received is same as the Data sent from the external system then consider it as Success, else then consider as Failure.

##### DDR4(PL) Test

    This test is used to qualify DDR4 by file read and file write. Refer the section 2.2.1.2.7 and 5.1.1.2.7 for Data decomposition and flowchart.
###### DDR4 Reset

- Refer the section for 5.1.1.2.7.1 Flowchart.
Requirement ID	DP_VPX_0233_MANUAL_PL_DDR4_01
Design Details	Reset the DDR4 by writing TWO and ZERO in the DDR4 CONTROL REGISTER. / If DDR reset completed print PL DDR RESET: SUCCESS, otherwise print PL DDR RESET: FAILED.

###### Full memory test

- Refer the section for 5.1.1.2.7.2 Flowchart.
Requirement ID	DP_VPX_0233_MANUAL_PL_DDR4_05
Design Details	Write PATTERN DATA in the corresponding FPGA Register. / Read Data from the corresponding FPGA Register. / Compare both Write and Read Data from the memory. / If Write Data and Read Data are same then Write ANTI PATTERN DATA in the corresponding FPGA Register, else the print “Full Memory test : Failed”. / Compare both Write and Read Data from the memory / If Write Data and Read Data are same then print “Full Memory test : Failed”, else then print “Full Memory test : Success”.

###### Data bus test
Refer the Section 5.1.1.2.7.3 Flowchart.
Requirement ID	DP_VPX_0233_MANUAL_PL_DDR4_02
Design Details	Refer the section 2.1.1.3.2.1

###### Address Bus Test
Refer the Section 5.1.1.2.7.4 Flowchart.
Requirement ID	DP_VPX_0233_MANUAL_PL_DDR4_3
Design Details	Refer the section 2.1.1.3.2.2

###### Device Test
Refer the Section 5.1.1.2.7.5 Flowchart.
Requirement ID	DP_VPX_0233_MANUAL_PL_DDR4_4
Design Details	Refer the section 2.1.1.3.2.3

##### 10G Ethernet Test

This test is used to qualify 10G Ethernet by performing the following test cases. Refer the section 2.2.1.2.8 and 5.1.1.2.8 for Data decomposition and flowchart.
###### Lane Repeater Configuration
Refer the Section 5.1.1.2.8.1 for flowchart.
Requirement ID	DP_VPX_0233_MANUAL_PL_10G_01
Design Details	Read the Data from the configuration file. / Write the Data in the respective address for the corresponding Lane Repeater through SMBUS. / If the write process completed Display Lane Repeater Configured: Successfully, Otherwise Display Lane Repeater Configured: Failed. / Note: 4 Channels are available for 10 G Validation.

###### Core Reset
Refer the Section 5.1.1.2.8.2 for flowchart.
Requirement ID	DP_VPX_0233_MANUAL_PL_10G_02
Design Details	Get the Core reset command from user. / Reset the IP core as per FPGA sequence. / Read the specific register given by FPGA. / If the data is valid the Display CORE RESET: SUCCESS, otherwise Display CORE RESET: FAILED.

###### Ethernet Reset
Refer the Section 5.1.1.2.8.3 for flowchart.
Requirement ID	DP_VPX_0233_MANUAL_PL_10G_03
Design Details	Get the Ethernet reset command from user. / Reset the Ethernet as per FPGA sequence. / If ethernet reset success then Display ETHERNET RESET: SUCCESS, otherwise Display ETHERNET RESET: FAILED.

###### Network Configuration
- Refer the Section 5.1.1.2.8.4 for flowchart.
Requirement ID	DP_VPX_0233_MANUAL_PL_10G_04
Design Details	Get MAC address from the user and Validate it. / If MAC address configured, Display MAC ADDRESS CONFIGURATION: SUCCESS, otherwise Display MAC ADDRESS CONFIGURATION: FAILED. / Then get the selection from the user as [1. Source IP address / 2. Destination IP address] and get the respective IP address from the user. / If Source IP address configured, Display SOURCE IP ADDRESS: SUCCESS, otherwise display SOURCE IP ADDRESS; FAILED. / If Destination IP address configured, Display DESTINATION IP ADDRESS: SUCCESS, otherwise display DESTINATION IP ADDRESS; FAILED.

###### Transmit Data
Refer the Section 5.1.1.2.8.5 for flowchart.
Requirement ID	DP_VPX_0233_MANUAL_PL_10G_05
Design Details	Get the No. of. Packets to be sent from board to PC as user input. / Get the delay for each packets in nano seconds from user. / Configure as per FPGA sequence to transmit the data. / If data transmitted then display TRANSMIT DATA: SUCCESS, otherwise display TRANSMIT DATA: FAILED.

###### Receiver Packet Summary
Refer the Section 5.1.1.2.8.6 for flowchart.
Requirement ID	DP_VPX_0233_MANUAL_PL_10G_06
Design Details	Get ‘1’ as user input to start receiving packets. / Read the packet time, packet count, Valid packets and Error bits from FPGA allocated registers. / Calculate the bandwidth using packet time. / If Packets received, Display packet count, Valid packets, Error bits and bandwidth, otherwise display RECEIVER PACKET SUMMARY: FAILED.

### DPSPL1255 Module
#### Test Performance
The Module Decomposition are as follows:
Programmable Logic
1. LMK PLL test
2. RFDAC Single DAC test
#### Programmable Logic
This Section will hold the module decomposition for the Programmable logic section.

##### LMK PLL Test

 This test shall be performed to qualify the LMK PLL Test. Refer the section 2.2.1.2.1 and 5.1.1.2.1 for Data decomposition and Flowchart.
###### File Configuration

Refer the section 2.1.1.4.1.1 for Module composition.
###### File Dump

Refer the section 2.1.1.4.1.2 for Module composition.
###### Single Data Write

Refer the section 2.1.1.4.1.3 for Module composition.
###### Single Data Read

Refer the section 2.1.1.4.1.4 for Module composition.

###### PLL Lock Status

Refer the section 2.1.1.4.1.5 for Module composition.

##### RFDAC Test
This test shall be performed to qualify RFDAC test.
###### File Write

Refer the section 5.1.2.1.2.1 for flow chart.
Requirement ID	DP_VPX_0233_MANUAL_PL_RFDAC_01
Design Details	Get the configuration file name from the user. / Check whether the file is present or not. / Read the configuration file. / Write the RFDAC selection value in RFDAC SELECTION REGISTER. / If the write process completed print RFDAC FILE WRITE: SUCCESS, otherwise RFDAC FILE WRITE: FAILED. / Note: The configuration Registers and Data will be given in a file “DP_VPX_0233_RFDAC_CONFIG.txt”

###### File Read

Refer the section 5.1.2.1.2.2 for flow chart.
Requirement ID	DP_VPX_0233_MANUAL_PL_RFDAC_02
Design Details	Get the configuration file name from the user. / Check whether the file is present or not. / Read the configuration file. / Get the Log file name from the user. / Create the Log File with the given file name. / Read the data from the corresponding registers through BRAM SPI Interface. / Print the data in the Log File. / If the read and logging Operation completed print RFDAC FILE READ: SUCCESS, otherwise RFDAC FILE READ: FAILED. / Note: The configuration Registers and Data will be given in a file “DP_VPX_0233_RFDAC_CONFIG.txt”.

###### Single Data Write
- Refer the section 5.1.2.1.2.3 for flow chart.
Requirement ID	DP_VPX_0233_MANUAL_PL_RFDAC_03
Design Details	Refer the section 2.1.1.4.1.3

###### Single Data Read

- Refer the section 5.1.2.1.2.4 for flow chart.
Requirement ID	DP_VPX_0233_MANUAL_PL_RFDAC_04
Design Details	Refer the section 2.1.1.4.1.4

###### Power Level Transmission

- Refer the section 5.1.2.1.2.5 for flow chart.
Requirement ID	DP_VPX_0233_MANUAL_PL_RFDAC_05
Design Details	Get the power level from the user [0- 0x6A]. / Write the power level value in SPI current control register. / If Power level enabled it prints Power Level transmission: SUCCESS. Otherwise Power Level Transmission: FAILED.

###### RFDAC Data Transmission

Refer the Section 5.1.2.1.2.6 for flow chart.
Requirement ID	DP_VPX_0233_MANUAL_PL_RFDAC_06
Design Details	Get the power level from the user and write in the corresponding registers through FPGA SPI interface. / Select any one of the two available RFDAC channels. / Get the Frequency from the user. / Channel1 – 20MHz to 2.5GHz / Channel2 – 2.5GHz to 6GHz / Write the frequency values to the corresponding RFDAC registers through FPGA SPI interface. / If Data Transmission completed print RFDAC DATA TRANSMISSION: SUCCESS, otherwise RFDAC DATA TRANSMISSION: FAILED.

###### RFDAC Reset

- Refer the Section 5.1.2.1.2.7 for flow chart.
Requirement ID	DP_VPX_0233_MANUAL_PL_RFDAC_07
Design Details	Validate the Handle. / Write Data 0x0 in the corresponding register. / If the write process completed, Then the test case is declared as Success, else it declared as Failure.

### DPSPL1276 Module
The Module Decomposition are as follows:
Programmable Logic
1. LMK PLL test
2. RFDAC Dual DAC test
#### Programmable Logic
This Section will hold the module decomposition for the Programmable logic section.

##### LMK PLL Test

 This test shall be performed to qualify the LMK PLL Test. Refer the section 2.2.1.2.1 and 5.1.1.2.1 for Data decomposition and Flowchart.

###### File Configuration

Refer the section 2.1.1.4.1.1 for Module composition.

###### File Dump

Refer the section 2.1.1.4.1.2 for Module composition.
###### Single Data Write

Refer the section 2.1.1.4.1.3 for Module composition.
###### Single Data Read

Refer the section 2.1.1.4.1.4 for Module composition.
###### PLL Lock Status

Refer the section 2.1.1.4.1.5 for Module composition.

##### RFDAC Test
This test shall be performed to qualify RFDAC test.
###### File Write

Refer the section 2.1.2.2.2.1 for Module composition.
###### File Read

Refer the section 2.1.2.2.2.2 for Module composition.
###### Single Data Write

Refer the section 2.1.2.2.2.3 for Module composition.
###### Single Data Read

Refer the section 2.1.2.2.2.4 for Module composition.
###### Power Level Transmission

Refer the section 2.1.2.2.2.5 for Module composition.
###### RFDAC Data Transmission

Refer the section 2.1.2.2.2.6 for Module composition.
###### RFDAC Reset

Refer the section 2.1.2.2.2.7 for Module composition.
## Data Decomposition
### DPVPX0233 Module
S. No	Data Name	Input/Output	Data Description
1.	Test configuration details	Input	This contains the entire configuration details including the Selected/Non-Selected state of all the test cases both in Auto Mode & Manual Mode test scenario.

The Test Configuration details is further decomposed into the following data:
- Auto Mode Test case Enable/Disable state given by user
- Manual Mode Test case Enable/Disable state.
#### Processing Section
- This Section contains the module decomposition for the processing section.
- Refer the section 2.1.1.3 and 5.1.1.1 for module decomposition and flowchart.
##### Processor Test

Refer the section 2.1.1.3.1 and 5.1.1.1.1 for module decomposition and flowchart.

S. No	Data Name	Input/Output	Data Description
	Arithmetic Unit Input Data	Input	0xFFFF 0000 and 0×0001 FFFF
	Arithmetic Unit Expected Data	Output	Addition - 0×0000FFFF / Subtraction - 0xFFFD 0001 / Multiplication - 0×00010000 / Division - 0×00007FFF
	Shift Unit Input Data	Input	0xFFFF 0000 and 16
	Shift Unit Expected Data	Output	Left Shift – 0×00000000 / Right Shift – 0×0000FFFF
	Logical Unit Input Data	Input	AND/OR (0xFFFF 0000 and 0×0001 FFFF) / NOT (0xFFFF 0000)
	Logical Unit Expected Data	Output	AND – 1 / OR – 1 / NOT – 0
	Floating Point Unit Input Data	Input	6.6 and 3.3
	Floating Point Expected Data	Output	Addition – (9.8999995 – 9.9000005) / Subtraction – (3.2999995 – 3.3000005) / Multiplication – (21.7799995 – 21.7800005) / Division – (1.9999995 – 2.0000005)

##### DDR Test
Refer the section 2.1.1.3.2 and 5.1.1.1.2 for module decomposition and flowchart.

S. No	Data Name	Input/Output	Data Description
	Allocated memory size	Input	2 MB memory allocated for data bus test, address bus test and device test.
	Pattern data	Input	0x55555555 for address bus test.
	Anti-Pattern data	Input	0xAAAAAAAA for address bus test.

##### EEPROM Test
Refer the section 2.1.1.3.3 and 5.1.1.1.3 for module decomposition and flowchart.

S. No	Data Name	Input/Output	Data Description
	Board information address	Input	Offset to write Board Information data.
	Board information data	Input	Refer section 5.2.1.
	Address from user	Input	For Read / Write, User Checksum Test.
	Pattern data from user	Input	For Read / Write Test.
	Expected Checksum from user	Output	User Checksum Test
	Number of locations from user	Input	For Read / Write, User Checksum test.

##### MRAM Test
Refer the section 2.1.1.3.4 and 5.1.1.1.4 for module decomposition and flowchart.

S. No	Data Name	Input/Output	Data Description
	Board information Offset	Input	Offset to write the Board Information data.
	Board information data	Input	Refer section 5.2.1
	Address from user	Input	For User Checksum Test
	Number of locations from user	Input	For User Checksum test.
	Expected Checksum from user	Output	User Checksum Test

##### NAND Flash Test
Refer the section 2.1.1.3.5 and 5.1.1.1.5 for module decomposition and flowchart.
S. No	Data Name	Input/Output	Data Description
	Board information Offset.	Input	Offset to write the Board Information data.
	Board information data	Input	Refer section 5.2.1.
	Address from user	Input	For User checksum test
	Number of locations from user	Input	For User Checksum test.
	Expected Checksum from user	Output	User Checksum Test

##### NOR Flash Test
Refer the section 2.1.1.3.6 and 5.1.1.1.5.4 for module decomposition and flowchart.
S. No	Data Name	Input/Output	Data Description
	Board information Offset.	Input	Offset to write the Board Information data.
	Board information data	Input	Refer section 5.2.1.
	Address from user	Input	For User checksum test
	Number of locations from user	Input	For User Checksum test.
	Expected Checksum from user	Output	User Checksum Test

##### USB Test
Refer the section 2.1.1.3.7 and 5.1.1.1.6 for module decomposition and flowchart.
S. No	Data Name	Input/Output	Data Description
	Device name / mount path / partition name	Input	Partition to mount and test .

##### SATA Test
Refer the section 2.1.1.3.8 and 5.1.1.1.7 for module decomposition and flowchart.
S. No	Data Name	Input/Output	Data Description
	Device name / mount path / partition	Input	Partition to mount and test .

##### UART Test

Refer the section 2.1.1.3.9 and 5.1.1.1.8 for module decomposition and flowchart.
S. No	Data Name	Input/Output	Data Description
	Baud rate	Input	4800/9600/19200/38400/57600/115200
	Parity	Input	Odd or even or none.
	COM Port	Input	Port to be tested.
	Stop bit	Input	1 or 2.
	Data Size	Input	Size of data to be transferred (or) received. Maximum size is 255bytes.
	Transmit data	Input	Data to be transmitted through the selected COM port.
	Receive data	Output	Data to be received through the selected COM port.

##### Ethernet Test
Refer the section 2.1.1.3.10 and 5.1.1.1.9 for module decomposition and flowchart.
S. No	Data Name	Input/Output	Data Description
	IP Address	Input	IP address to send and receive the data.

##### RTC Test

Refer the section 2.1.1.3.11 and 5.1.1.1.10 for module decomposition and flowchart.
S. No	Data Name	Input/Output	Data Description
	Year	Input	(1970-2035)
	Month	Input	(1 -12)
	Day	Input	(1 – 31)
	Hour	Input	(1 – 24)
	Minute	Input	(1 -60)
	Second	Input	( 1 - 60)

##### PCI Enumeration Test
Refer the section 2.1.1.3.12 and 5.1.1.1.11 for module decomposition and flowchart.
S. No	Data Name	Input/Output	Data Description
	Vendor ID	Input	Vendor ID's of expected PCI devices
	Device ID	Input	Device ID's of expected PCI devices
	Vendor ID	Output	Vendor ID's of detected PCI devices.
	Device ID	Output	Device ID's of detected PCI devices.

##### Temperature Sensor Test
Refer the section 2.1.1.3.13 and 5.1.1.1.12 for module decomposition and flowchart.
S. No	Data Name	Input/Output	Data Description
	Upper and Lower limit	Input	Acceptable range.
	Current temperature	Output	Temperature read from temperature sensor.

##### Voltage Monitoring Test
Refer the section 2.1.1.3.14 and 5.1.1.1.13 for module decomposition and flowchart.

S. No	Data Name	Input/Output	Data Description
	Channel Voltages	Output	Read voltages of the ADM Input Channel from the processor.
	Upper and Lower limit	Input	Acceptable range. / The Limits are Listed Below: / VX1- 0.88 to 0.93 / VX2- 0.94 to 1.02 / VX3- 1.14 to 1.26 / VX4-1.17 to 1.23 / VX5- 0.83 to 0.88 / VP1- 1.75 to 1.85 / VP2- 0.85 to 1.05 / VP3- 2.44 to 2.56 / VP4- 3.17 to 3.39 / VH- 4.53 to 5.41

#### Programmable Logic
This Section contains the module decomposition for the programmable logic section.

##### LMK PLL Test

Refer the section 2.1.1.4.1 and 5.1.1.2.1 for module decomposition and flowchart.

S. No	Data Name	Input/Output	Data Description
	Configuration File	Input	Provides for Input Configuration File.
	Read Log File	Output	Provides for Output Log File.
	SPI Address	Input	Provides for SPI Offset
	Write Data	Input	Provides for SPI offset and SPI Data
	Read Data	Output	Provides for SPI Read Data

##### AFE7906 Test

Refer the section 2.1.1.4.2 and 5.1.1.2.2 for module decomposition and flowchart.

S. No	Data Name	Input/Output	Data Description
	AFE Chip number	Input	Provides for AFE Chip Selection
	SPI Address	Input	Provides for SPI Offset
	Write Data	Input	Provides for SPI offset and SPI Data
	Read Data	Output	Provides for SPI Read Data
	Bring up File	Input	Provides for AFE Configuration FIle
	Channel Number	Input	Specifies the Rx Channel Number[1-6]
	Sample Data	Input	Specifies for no. of Samples[2K-128K]
	Data Log File	Output	Provides for IQ Data Logging from ADC
	Band Selection	Input	Specifies the Band Selection Narrow/Wide band / Narrow Band 1520 +/- 3MHz / Wide Band 1520 +/- 80MHz

##### LVTTL Test

Refer the section 2.1.1.4.3 and 5.1.1.2.3 for module decomposition and flowchart.

S. No	Data Name	Input/Output	Data Description
	Set Number	Input	Set number to select the available 4 Sets

##### LVDS Test

Refer the section 2.1.1.4.4 and 5.1.1.2.4 for module decomposition and flowchart.

S. No	Data Name	Input/Output	Data Description
	Set Number	Input	Set number to select the available 3 Sets

##### GPI GPO Test

Refer the section 2.1.1.4.5 and 5.1.1.2.5 for module decomposition and flowchart.

S. No	Data Name	Input/Output	Data Description
	Manual mode Input data	Input	Input data as either ONE or ZERO

##### UART (PL) Test
Refer the section 2.1.1.4.6 and 5.1.1.2.6 for module decomposition and flowchart.
S. No	Data Name	Input/Output	Data Description
	Data Size	Input	Size of data to be transferred (or) received. Maximum size is 255bytes.
	Transmit data	Input	Data to be transmitted through the selected COM port.
	Receive data	Output	Data to be received through the selected COM port.

##### DDR4 (PL) Test
Refer the section 2.1.1.4.7 and 5.1.1.2.7 for module decomposition and flowchart.

S. No	Data Name	Input/Output	Data Description
	Pattern data	Input	0x55555555 for full memory test.
	Anti-Pattern data	Input	0xAAAAAAAA for full memory test.

##### 10G Ethernet Test
Refer the section 2.1.1.4.8 and 5.1.1.2.8 for module decomposition and flowchart.
S. No	Data Name	Input/Output	Data Description
	Channel Selection	Input	User input to select the one of the four available Channels
	MAC address	Input	MAC address for the board.
	Source IP address	Input	IP address for the Board
	Destination IP address	Input	IP address for the host PC
	I2C Registers	Input	I2C registers to be written manually
	Data	Input	Data to be written in the I2C registers
	Packet received	Output	User can know how many packets received

### DPSPL1255 Module
#### Programmable Logic
This Section contains the module decomposition for the programmable logic section.

##### LMK PLL Test

Refer the section 2.2.1.2.1.
##### RFDAC Test
- Refer the section 2.1.2.2.2 and 5.1.2.1.2 for module decomposition and flowchart.
S. No	Data Name	Input/Output	Data Description
	Configuration file	Input	File contains the configuration details to configure the RFDAC. / “DP_VPX_0233_RFDAC_CONFIG.txt”
	Register Dump file	Output	File contains the register dump of the RFDAC
	RFDAC Register address	Input	Address of the RFDAC for read/write operation
	Write Data	Input	Data to be written in the RFDAC register
	Read Data	Output	Data read from the RFDAC
	RFDAC Selection	Input	Selecting one of the available 2 RFDAC channels
	JESD Bond Status	Output	Status of the JESD Bond.
	Power level	Input	Power level for the signal to be transmitted
	Frequency value	Input	Frequency of the signal to be transmitted / Channel 1 – 2MHz to 2.5GHz / Channel 2 – 2.5GHz to 6GHz

### DPSPL1276 Module
#### Programmable Logic
This Section contains the module decomposition for the programmable logic section.

##### LMK PLL Test

Refer the section 2.2.1.2.1.
##### RFDAC Test

Refer the section 2.2.2.1.2.
## Process Decomposition
The entire process of the ATP software can be decomposed as follows :
1. User Input
  This includes the process of getting the inputs from the user such as the Test Configuration details which has to be executed during Auto/Manual mode.
2. Input Processing
  This includes the process of executing the test cases that were entered by the user as input along with some additional details if required, such as device name in-case of nand flash test.
3. Test Result
This is to display the output of the requested test performance to the user at the terminal.
# Dependency Description
## Module Dependencies
### DEPENDENCY BETWEEN THE MODULES “TEST CONFIGURATION” AND “TEST PERFORMANCE”:
        Before performing any Auto Mode/Manual Mode test cases of the Test Performance module, the test to be performed should be initially enabled by the user using the Test Configuration module. Thus without Test Configuration module, the Test Performance module cannot be stabilized.
## Data Dependencies
The test cases that are possible to be executed in the Auto Mode/Manual Mode Test Performance module depends on the test case selection (ENA/DIS) data of Test Configuration module.
## Process Dependencies
### DEPENDENCY BETWEEN THE PROCESS ‘USER INPUT’ AND ‘INPUT PROCESSING’ :
        The process named as 'Input Processing' is meaningful only after completion of the process named as 'User Input' since the former requires the details given by the user in the later process for the execution of any test cases.

### DEPENDENCY BETWEEN THE PROCESS 'INPUT PROCESSING' AND 'TEST RESULT' :
        The process named, 'Test Result' depends on the 'Input Processing' since the result of any test case can be found only after the execution of particular test case.
# Interface Description
## Module Interface
In DPVPX0233 Module ,The configuration details entered by the user stored in the configuration file (dpvpx0233atp_config) is used for performing the test cases and acts as an interface between the modules.
## Process Interface
        NA
# Detailed Design
## Module Detailed Design
Note : In case of read/write failure in memory devices, failed offset/address, expected data and actual data will be printed along with the failure message.
### DPVPX0233 Module
#### Processing Section
##### Processor Test

Refer the section 2.1.1.3.1 and 2.2.1.1.1 for Module Decomposition and Data Decomposition..

Figure 5.1 : Processor Test Men
###### ALU Test
Refer the section 2.1.1.3.1.1and 2.2.1.1.1 for Module Decomposition and Data Decomposition..

Figure 5.2: Processor Test - ALU Test
###### FPU Test
Refer the section 2.1.1.3.1.2 and 2.2.1.1.1 for Module Decomposition and Data Decomposition..
Figure 5.3 : Processor Test – FPU Test
##### DDR4 Test
Refer the section 2.1.1.3.2 and 2.2.1.1.2 for Module Decomposition and Data Decomposition..

Figure 5.4 : DDR4 Test Menu

###### Data Bus Test
Refer the section 2.1.1.3.2.1 and 2.2.1.1.2 for Module Decomposition and Data Decomposition.

Figure 5.5: DDR4 Test – Data Bus Test

###### Address Bus Test
Refer the section 2.1.1.3.2.2 and 2.2.1.1.2 for Module Decomposition and Data Decomposition..

Figure 5.6: DDR4 Test – Address Bus Test

###### Device Test
Refer the section 2.1.1.3.2.3 and 2.2.1.1.2 for Module Decomposition and Data Decomposition..

Figure 5.7: DDR4 Test –Device Test

##### EEPROM Test
Refer the section 2.1.1.3.3 and 2.2.1.1.3 for Module Decomposition and Data Decomposition..

Figure 5.8 : EEPROM Test Menu

###### Upload Board Information Test
Refer the section 2.1.1.3.3.1 and 2.2.1.1.3 for Module Decomposition and Data Decomposition..

Figure 5.9 : EEPROM – Upload Board Information Test

###### Data Retention Test

Refer the section 2.1.1.3.3.2 and 2.2.1.1.3 for Module Decomposition and Data Decomposition..

Figure 5.10 : EEPROM – Data Retention Test

###### Checksum Test
Refer the section 2.1.1.3.3.3 and 2.2.1.1.3 for Module Decomposition and Data Decomposition..

Figure 5.11 : EEPROM – Checksum Test

###### Read/Write Test
Refer the section 2.1.1.3.3.4 and 2.2.1.1.3 for Module Decomposition and Data Decomposition.

Figure 5.12 : EEPROM – Read/Write Test

##### MRAM Test

Refer the section 2.1.1.3.4 and 2.2.1.1.4 for Module Decomposition and Data Decomposition..

Figure 5.13 : MRAM Test Menu

###### Upload Board Information test

Refer the section 2.1.1.3.4.1 and 2.2.1.1.4 for Module Decomposition and Data Decomposition..
Refer the Section 5.1.1.1.3.1 for Flowchart.

###### Data Retention test

Refer the section 2.1.1.3.4.2 and 2.2.1.1.4 for Module Decomposition and Data Decomposition..

Refer the Section 5.1.1.1.3.2 for Flowchart.

###### Checksum Test

Refer the section 2.1.1.3.4.3 and 2.2.1.1.4 for Module Decomposition and Data Decomposition..

Refer the Section 5.1.1.1.3.3 for Flowchart.

###### Full Memory test

Refer the section 2.1.1.3.4.4 and 2.2.1.1.4 for Module Decomposition and Data Decomposition..

Figure 5.14 : MRAM – Full Memory Test

##### NAND Flash Test
Refer the section 2.1.1.3.5 and 2.2.1.1.5 for Module Decomposition and Data Decomposition..

Figure 5.15 : NAND Flash Test Menu

###### Upload Board Information test
Refer the section 2.1.1.3.5.1 and 2.2.1.1.5 for Module Decomposition and Data Decomposition..
Refer the Section 5.1.1.1.3.1 for Flowchart.

###### Data Retention Test
Refer the section 2.1.1.3.5.2 and 2.2.1.1.5 for Module Decomposition and Data Decomposition..
Refer the Section 5.1.1.1.3.2 for Flowchart.

###### Checksum Test
Refer the section 2.1.1.3.5.3 and 2.2.1.1.5 for Module Decomposition and Data Decomposition..
Refer the Section 5.1.1.1.3.3 for Flowchart.

###### NOR Flash Test
Refer the section 2.1.1.3.6 and 2.2.1.1.6 for Module Decomposition and Data Decomposition..

Figure 5.16 : NOR Flash Test Menu

###### Upload Board Information test
Refer the section 2.1.1.3.6.1 and 2.2.1.1.6 for Module Decomposition and Data Decomposition.
Refer the Section 5.1.1.1.3.1 for Flowchart.

###### Data Retention Test
Refer the section 2.1.1.3.6.2 and 2.2.1.1.6 for Module Decomposition and Data Decomposition..
Refer the Section 5.1.1.1.3.2 for Flowchart.

###### Checksum Test
Refer the section 2.1.1.3.6.3 and 2.2.1.1.6 for Module Decomposition and Data Decomposition..
Refer the Section 5.1.1.1.3.3 for Flowchart.

##### USB Test
###### Read / Write Test
Refer the section 2.1.1.3.7.1 and 2.2.1.1.7 for Module Decomposition and Data Decomposition.
Figure 5.17: USB – Read / Write Test

##### SATA Test
###### Read / Write Test
Refer the section 2.1.1.3.8.1 and 2.2.1.1.8 for Module Decomposition and Data Decomposition..
Refer the Section 5.1.1.1.6.1 for Flowchart.

##### UART Test
Refer the section 2.1.1.3.9 and 2.2.1.1.9 for Module Decomposition and Data Decomposition..

Figure 5.18 : UART Main Menu

###### Write Test
Refer the section 2.1.1.3.9.1 and 2.2.1.1.9 for Module Decomposition and Data Decomposition..

Figure 5.19 : UART – Write Test

###### Read Test
Refer the section 2.1.1.3.9.2 and 2.2.1.1.9for Module Decomposition and Data Decomposition..

Figure 5.20 : UART – Read

##### Ethernet Test
Refer the section 2.1.1.3.10 and 2.2.1.1.10 for Module Decomposition and Data Decomposition..

Figure 5.21 : Ethernet - Test Menu

###### Ethernet ping Test

Refer the section 2.1.1.3.10.1 and 2.2.1.1.10 for Module Decomposition and Data Decomposition..

Figure 5.22 : Ethernet Ping Test

##### RTC

Refer the section 2.1.1.3.11 and 2.2.1.1.11 for module decomposition and data decomposition.

        Figure 5.23 : RTC Test

##### PCI Enumeration Test
Refer the section 2.1.1.3.12 and 2.2.1.1.12 for module decomposition and data decomposition.
        Figure 5.24 : PCI Enumeration Test
##### Temperature Sensor Test
Refer the section 2.1.1.3.13 and 2.2.1.1.13 for Module Decomposition and Data Decomposition..

Figure 5.25 : Temperature Sensor Test

##### Voltage Monitoring Test

Refer the section 2.1.1.3.14 and 2.2.1.1.14 for Module Decomposition and Data Decomposition..

Figure 5.26 : ADM – Voltage Monitoring Test

#### Programmable Logic
##### LMK PLL Test
Refer the section 2.1.1.4.1 and 2.2.1.2.1 for module decomposition and data decomposition.

Start

Select the Option:
1.File Configuration
2.File Dump
3.Single Write
4.Single Read
5.PLL Lock Status
6.Sysref Enable/Disable
99.Exit

Is File Configuration ?

Is File Dump ?

Is Single Write ?

Is Single Read ?

Return to Main Menu

No

A

B

C

D

Yes

Yes

Yes

Yes

No

No

No

No

Yes

Is PLL Lock status ?

No

Yes

E

Is Exit ?

Is Sysref Enable/Disable ?

No

No

Yes

No

No

F

Figure 5.27 : LMK PLL Menu
###### File Configuration
Refer the section 2.1.1.4.1.1 and 2.2.1.2.1 for module decomposition and data decomposition.

A

Is Handle Validated?

Print “Invalid Handle”

Get the configuration file from user

Is file is present?

Read data from the file

Write data to the corresponding FPGA registers

Is Write process completed?

Yes

Yes

Yes

No

Print “LMK PLL Configuration : FAIL”

Print “LMK PLL Configuration : SUCCESS”

Return to Menu

No

No

Print “File not found”

Figure 5.28 : File Configuration

###### File Dump
Refer the section 2.1.1.4.1.2 and 2.2.1.2.1 for module decomposition and data decomposition.

B

Is Handle Validated?

Get the configuration file from user

Is File Validated ?

Read Address from the configuration file

Write the address in corresponding FPGA Registers

Read Data from the corresponding FPGA Registers and store it in the Output file

Is Read process completed?

Print “LMK PLL Dump : SUCCESS”

Return to Menu

Print “Invalid Handle”

Print “File not found”

Print “LMK PLL Dump : FAIL”

Yes

Yes

Yes

No

No

No

Figure 5.29 : File Dump
###### Single Data Write

Refer the section 2.1.1.4.1.3 and 2.2.1.2.1for data decomposition and module decomposition.

C

Is Handle Validated?

Print “Invalid Handle”

Get the address and Data from the user

Write the Data and Address in the corresponding FPGA Registers

Is Write process is completed?

Print “LMK PLL Single Write : FAIL”

Print “LMK PLL Single Write : SUCCESS”

Return to Menu

Yes

Yes

No

No

Figure 5.30: Single Data Write

###### Single Data Read

Refer the section 2.1.1.4.1.4 and 2.2.1.2.1 for data decomposition and module decomposition.

D

Is Handle Validated?

Get the address from the user

Write the address and Read the Data from the Corresponding FPGA Read register

If Read process completed?

Print “LMK PLL Single Read : FAIL”

Print ”LMK PLL Single Read : SUCCESS”

Return to Menu

Print “Invalid Handle”

Yes

No

No

Display the read values

Yes

Figure 5.31:Single Data Read

###### PLL Lock Status
Refer the section 2.1.1.4.1.5 and 2.2.1.2.1 for data decomposition and module decomposition.

E

Is Handle Validated?

Print “Invalid Handle”

Read the Lock Status from the corresponding PLL Status Register

Is Read process is completed?

Print “LMK PLL Lock Status : FAIL”

Print “LMK PLL Lock Status : SUCCESS”

Return to Menu

Yes

Yes

No

No

Compare the Read data it must be equal to 0x30

Is Comparison was success ?

No

Print “LMK PLL Lock Status : FAIL”

Yes

Figure 5.32:PLL Lock Status

###### Sysref Enable/Disable

Refer the section 2.1.1.4.1.6 and 2.2.1.2.1 for data decomposition and module decomposition.

   Figure 5.33: Sysref Enable/Disable Menu

###### Sysref Enable

Refer the section 2.1.1.4.1.6.1 and 2.2.1.2.1 for data decomposition and module decomposition.

G

Is Handle validated ?

Print “Invalid Handle”

Write Data 0x15 in the corresponding register

Is write process completed ?

No

Yes

Print “SYSREF Enable : FAIL”

Print “SYSREF Enable : SUCCESS”

No

Yes

Return to PLL Menu

Figure 5.34: Sysref Enable Menu

###### Sysref Disable

Refer the section 2.1.1.4.1.6.2 and 2.2.1.2.1 for data decomposition and module decomposition.

H

Is Handle validated ?

Print “Invalid Handle”

Write Data 0x5 in the corresponding register

Is write process completed ?

No

Yes

Print “SYSREF Enable : FAIL”

Print “SYSREF Enable : SUCCESS”

No

Yes

Return to PLL Menu

Figure 5.35: Sysref Disable Menu

##### AFE7096 ADC Test

Refer the section 2.1.1.4.2 and 2.2.1.2.2 for module decomposition and data decomposition.

Select the option:
1. AFE Core Reset
2. AFE Single Write
3.AFE Single Read
4.AFE Bring up
5.AFE Core Initialization
6.JESD Bond Status
7.ADC Data Logging
8.HD2 Correction Enable
9.NCO Update
10.AFE Dynamic Configuration
11.Band Selection
99. Exit

Is AFE Core Reset?

A

Yes

Start

Is AFE Single Write?

Is ADC Data logging?

No

Is AFE Single Read?

Is AFE Bringup ?

No

No

Is AFE Core Initialization ?

No

Is JESD Bond Status ?

No

No

Yes

Yes

Yes

Yes

Yes

B

C

D

E

F

Is HD2 Correction Enable?

Is AFE Dynamic Configuration?

Is Band Selection?

Is Exit?

G

Yes

Yes

Yes

Yes

H

K

No

No

No

No

Return to Main Menu

Yes

Is NCO Update?

Yes

I

J

No

Figure 5.36:AFE7906 ADC Menu

###### AFE Core Reset
Refer the section 2.1.1.4.2.1 and 2.2.1.2.2 for module decomposition and data decomposition.

A

Is Handle Validated?

Reset the AFE chip by writing 1 and 0 in the corresponding FPGA Registers

If Reset process completed?

Print “AFE Core Reset : SUCCESS”

Print “AFE Core Reset : FAIL”

Return to Menu

Print “Invalid Handle”

Yes

No

No

Yes

Figure 5.37: AFE7906 Core Reset

###### AFE Single Write
Refer the section 2.1.1.4.2.2 and 2.2.1.2.2 for module decomposition and data decomposition.

B

Is Handle Validated?

Get the Write address and Data from the user

Write the Data and Address in the corresponding FPGA Registers

If write process complete?

Print “AFE
Write : SUCCESS”

Print “AFE
Write : FAIL”

Print “Invalid Handle”

Return to Menu

Yes

No

No

Yes

Figure 5.38: AFE Single Write

###### AFE Single Read
Refer the section 2.1.1.4.2.3 and 2.2.1.2.2 for module decomposition and data decomposition.

C

Is Handle Validated?

Get the Read address from the user

Write the address and Read the Data from the Corresponding FPGA Read register

If read process completed?

Print “AFE Read : FAIL”

Print “AFE Read : SUCCESS”

Print “Invalid Handle”

Return to Menu

Yes

No

No

Display the Read Values

Yes

Yes

Figure 5.39: AFE Single Read

###### AFE Bring up

Refer the section 2.1.1.4.2.4 and 2.2.1.2.2 for module decomposition and data decomposition.

D

Is Handle Validated?

Get the ADC Configuration File from the user

Write and Read the Data From the corresponding FPGA Registers

If File configuration is completed?

Print “AFE Bringup : FAIL”

Print “AFE Bringup : SUCCESS”

Return to Menu

Print “Invalid Handle”

Yes

Yes

No

No

Figure 5.40: AFE Bring up

###### AFE Core Initialization

Refer the section 2.1.1.4.2.5 and 2.2.1.2.2 for module decomposition and data decomposition.

E

Is Handle Validated?

write corresponding Data to the FPGA Register

Then Read the Core Initialization Data from the Corresponding Read Register

Compare the Read Data it must be equal to 0xFFFFF

Is Comparison was success?

Print “AFE Core Initialization : FAIL”

Print “Invalid Handle”

Print “AFE Core Initialization : SUCCESS”

Return to Main Menu

Yes

Yes

No

No

Figure 5.41: AFE Core Initialization

###### JESD Bond Status

Refer the section 2.1.1.4.2.6 and 2.2.1.2.2 for module decomposition and data decomposition.

F

Is Handle Validated?

Write corresponding Data to the FPGA Register

Then Read the JESD Bond status from the corresponding FPGA Register

Is chip configured and JESD is Bonded Successfully?

Print “ADC JESD : Success”

Print “ADC JESD : Failure”

Return to Menu

Print “Invalid Handle”

Yes

Yes

No

No

Figure 5.42: JESD Bond Status

###### Data Logging

Refer the section 2.1.1.4.2.7 and 2.2.1.2.2 for module decomposition and data decomposition.

G

Is Handle Validated?

Is Rx Channel Selection Validated?

Is Sample Count Validated?

Select the Rx channel by writing channel number in the corresponding FPGA Register

Clear the ADC by writing Corresponding Data in the ADC Reset Register

Read the FIFO count from the corresponding Register

FIFO count must be greater or equal to the number of samples entered by user

Read the Data from the corresponding FPGA Register and log in to a File

Is read process completed?

Print “ADC Data Logging : SUCCESS”

Return to Menu

   Print “Invalid Handle”

Print “Invalid Rx Channel Selection”

Print “Invalid ADC Sample Data”

Print “ADC Data Logging : FAIL”

Yes

Yes

No

No

No

No

Get the Sample Count as input from the user

Get the Rx Channel Selection as input from the user

Yes

Yes

Figure 5.43: Data Logging
###### HD2 Correction Enable

Refer the section 2.1.1.4.2.8 and 2.2.1.2.2 for module decomposition and data decomposition.

H

Select the Option:
1.HD2 Coefficient Write
2.HD2 Coefficient Read
99.Exit

Is HD2 Coefficient Write?

Is HD2 Coefficient Read?

No

Is Exit?

Return to Menu

No

Yes

No

A

B

Yes

Yes

Figure 5.44: AFE HD2 Menu

###### HD2 Coefficient Write
Refer the section 2.1.1.4.2.8.1 and 2.2.1.2.2 for module decomposition and data decomposition.

A

Is Handle Validated?

Is Rx Channel Selection Validated?

Enable the HD2 pages by writing corresponding values in the corresponding registers

Write the channel selection Data in the corresponding Register

Get 2129 and 212a Data from the user

Enable the write sequence by writing corresponding Data in the Corresponding Registers

Is write process completed?

Print “HD2 Write : FAIL”

Print “HD2 Write : SUCCESS”

Return to Menu

Print “Invalid Handle”

Print “Invalid Rx Channel Selection"

Yes

Yes

No

No

No

Get the Rx Channel Selection from the user

Yes

Figure 5.45: AFE7906 ADC – HD2 Correction Write

###### HD2 Coefficient Read
Refer the section 2.1.1.4.2.8.2 and 2.2.1.2.2 for module decomposition and data decomposition.

B

Is Handle Validated?

Is Channel Selection Validated?

Write the channel number in the corresponding FPGA Register

Read the Data from 2129 and 212a spi offset

Is Read process completed?

Print “HD2 Read : FAIL”

Print “HD2 Read : SUCCESS”

Return to Menu

Print “Invalid Handle”

Print “Invalid AFE Chip Selection"

Yes

Yes

No

Yes

No

No

Display the Read values

Figure 5.46: AFE7906 ADC – HD2 Correction Read

###### NCO Update
Refer the section 2.1.1.4.2.9 and 2.2.1.2.2 for module decomposition and data decomposition.

Figure 5.47: NCO Menu

###### NCO Enable menu

Refer the section 2.1.1.4.2.9 and 2.2.1.2.2 for module decomposition and data decomposition.

Figure 5.48: NCO Enable Menu

###### All Channel Enable

Refer the section 2.1.1.4.2.9.1 and 2.2.1.2.2 for module decomposition and data decomposition.

Figure 5.49: All channel Enable

###### Single Channel Enable

Refer the section 2.1.1.4.2.9.2 and 2.2.1.2.2 for module decomposition and data decomposition.

Figure 5.50: Single channel Enable

###### NCO Disable menu

Refer the section 2.1.1.4.2.9 and 2.2.1.2.2 for module decomposition and data decomposition.

Figure 5.51: NCO Disable Menu

###### All Channel Disable

Refer the section 2.1.1.4.2.9.3 and 2.2.1.2.2 for module decomposition and data decomposition.

Figure 5.52: All channel Disable

###### Single Channel Disable

Refer the section 2.1.1.4.2.9.4 and 2.2.1.2.2 for module decomposition and data decomposition.

Figure 5.53: Single channel Disable

###### AFE Dynamic Configuration

Refer the section 2.1.1.4.2.10 and 2.2.1.2.2 for module decomposition and data decomposition.
Figure 5.54: AFE Dynamic configuration

###### Device Health Status

Refer the section 2.1.1.4.2.10.1 and 2.2.1.2.2 for module decomposition and data decomposition.

A

Read the Health Status of the chip from the Corresponding Registers

Display the Health Status

Return to Menu

Is Read process completed?

Test case declared as Failure

Yes

No

Figure 5.55: Device Health Status

###### Update Rx NCO

Refer the section 2.1.1.4.2.10.2 and 2.2.1.2.2 for module decomposition and data decomposition.

B

Get the Rx Mixer frequency from the user in MHZ

Get the Rx Band number from the user

Get the Rx NCO number from the user

Write the Data in the corresponding Registers

Is Write process completed?

Test Case declared as Failure

Test Case declared as Success

Return to Menu

No

Yes

Figure 5.56: Update Rx NCO

###### Set Rx DSA

Refer the section 5.1.1.2.2.10.3 and 2.2.1.2.2 for module decomposition and data decomposition.

C

Get the Attenuation Value from the user

Write the value in the corresponding Registers

Is Write process completed?

Test Case declared as Failure

Test Case declared as Success

Return to Menu

No

Yes

Figure 5.57: Set Rx DSA

###### Update Fb NCO

- Refer the section 2.1.1.4.2.10.4 and 2.2.1.2.2 for module decomposition and data decomposition.
- Refer the section 5.1.1.2.2.10.2 for Flowchart.
###### Set Fb DSA

- Refer the section 2.1.1.4.2.10.5 and 2.2.1.2.2 for module decomposition and data decomposition.
- Refer the section 5.1.1.2.2.10.3 for Flowchart.
###### Read Fb NCO
- Refer the section 2.1.1.4.2.10.7 and 2.2.1.2.2 for module decomposition and data decomposition.
- Refer the section 5.1.1.2.2.10.7 for Flowchart.

###### Read Rx NCO
Refer the section 2.1.1.4.2.10.6 and 2.2.1.2.2 for module decomposition and data decomposition.

F

Get the Rx Band number from the user

Get the Rx NCO number from the user

Read the Data from the corresponding Register

Is Read process completed?

Test Case declared as Failure

Test Case declared as Success

Return to Menu

No

Yes

Figure 5.58: Read Rx NCO

###### Band Selection

Refer the section 2.1.1.4.2.11 and 2.2.1.2.2 for Module Decomposition and Data Decomposition.
Figure 5.59 : AFE7906 ADC – ADC Band Selection

###### ADC Automation
###### Data Logging
###### Host Application
Refer the section 2.1.1.4.2.12.1.1 and 2.2.1.2.2 for Module Decomposition and Data Decomposition.

Figure 5.60 : AFE7906 ADC – Automation Data Logging HOST
###### Target Application
Refer the section 2.1.1.4.2.12.1.2 and 2.2.1.2.2 for Module Decomposition and Data Decomposition.

Figure 5.61 : AFE7906 ADC – Automation Data Logging TARGET

###### Phase Matching
###### Host Application

Refer the section 2.1.1.4.2.12.1.2 and 2.2.1.2.2 for Module Decomposition and Data Decomposition.

Figure 5.62 : AFE7906 ADC – Automation Phase Matching HOST

###### Target Application

Refer the section 2.1.1.4.2.12.1.2 and 2.2.1.2.2 for Module Decomposition and Data Decomposition.

Figure 5.63 : AFE7906 ADC – Automation Phase Matching TARGET

##### LVTTL Test

Refer the section 2.1.1.4.3 and 2.2.1.2.3 for module decomposition and data decomposition.
        Figure 5.64 : LVTTL Test
###### IO Mode Test
Refer the 2.1.1.4.3.1 and 2.2.1.2.3section for module decomposition and data decomposition.

        Figure 5.65 : IO Mode Test

###### Clock Mode Test

Refer the section 2.1.1.4.3.2 and 2.2.1.2.3 for module decomposition and data decomposition.
        Figure 5.66: Clock Mode Test

###### Manual IO Mode Test

Refer the section 2.1.1.4.3.3 and 2.2.1.2.3 for module decomposition and data decomposition.
        Figure 5.67: IO Manual Mode Test

###### Manual Clock Mode Test

Refer the section 2.1.1.4.3.4 and 2.2.1.2.3 for module decomposition and data decomposition.

 Figure 5.68: Manual Clock Mode Test

###### Manual Clock ON Test

Refer the section 2.1.1.4.3.4.1 and 2.2.1.2.3 for module decomposition and data decomposition.

Figure 5.69: Manual Clock ON Test
###### Manual Clock OFF Test

Refer the section 2.1.1.4.3.4.2 and 2.2.1.2.3 for module decomposition and data decomposition.

Figure 5.70: Manual Clock OFF Test
##### LVDS Test

Refer the section 2.1.1.4.4 and 2.2.1.2.4 for module decomposition and data decomposition.

Figure 5.71: LVDS Test

###### IO Mode Test

Refer the section 2.1.1.4.4.1 and 2.2.1.2.4 for module decomposition and data decomposition.

        Figure 5.72 : IO Mode Test

###### Clock Mode Test

Refer the section 2.1.1.4.4.2 and 2.2.1.2.4 for module decomposition and data decomposition.
        Figure 5.73: Clock Mode Test

###### Manual Mode Test

Refer the section 2.1.1.4.4.3 and 2.2.1.2.4 for module decomposition and data decomposition.
        Figure 5.74: Manual Mode Test

##### GPI/GPO Test
Refer the section 2.1.1.4.5 and 2.2.1.2.5 for module decomposition and data decomposition.

Figure 5.75: GPI GPO Test

###### IO Mode Test

Refer the section 2.1.1.4.5.1 and 2.2.1.2.5 for module decomposition and data decomposition.

Figure 5.76: IO Mode Test

##### UART Test
Refer the section 2.1.1.4.6 and 2.2.1.2.6 for module decomposition and data decomposition.

Figure 5.77: UART Test

###### UART Read

Refer the section 2.1.1.4.6.2 and 2.2.1.2.6 for module decomposition and data decomposition.
Figure 5.78: UART Read

###### UART write
Refer the section 2.1.1.4.6.1 and 2.2.1.2.6 for module decomposition and data decomposition.

Figure 5.79: UART Write

##### DDR4(PL) Test
Refer the section 2.1.1.4.7 and 2.2.1.2.7 for module decomposition and data decomposition.
Figure 5.80: DDR4 (PL) Test

###### DDR4 Reset
Refer the section 2.1.1.4.7.1 and 2.2.1.2.7 for module decomposition and data decomposition.

  Figure 5.81: DDR4 (PL) Reset Test

###### Full Memory Test

Refer the section 2.1.1.4.7.2 and 2.2.1.2.7 for module decomposition and data decomposition.

        Figure 5.82: Full Memory Test

###### Data Bus Test
Refer the section 5.1.1.1.2.1 for Flowchart.
###### Address Bus Test
Refer the section 5.1.1.1.2.2 for Flowchart.
###### Device Test
Refer the section 5.1.1.1.2.3 for Flowchart.

##### 10G Ethernet Test

 Refer the section 2.1.1.4.8 and 2.2.1.2.8 for Module Decomposition and Data Decomposition.

        Figure 5.83: 10G Ethernet Test
###### Lane Repeater Configuration
Refer the section 2.1.1.4.8.1 and 2.2.1.2.8 for Module Decomposition and Data Decomposition.
        Figure 5.84: Lane Repeater Operation

###### Core Reset
Refer the section 2.1.1.4.8.2 and 2.2.1.2.8 for Module Decomposition and Data Decomposition.
        Figure 5.85 : Core Reset

###### Ethernet Reset
Refer the section 2.1.1.4.8.3 and 2.2.1.2.8 for Module Decomposition and Data Decomposition.

 Figure 5.86 : Ethernet Reset

###### Network Configuration

Refer the section 2.1.1.4.8.4 and 2.2.1.2.8 for Module Decomposition and Data Decomposition.

Figure 5.87 : Network Configuration
###### Transmit Data

Refer the section 2.1.1.4.8.5 and 2.2.1.2.8 for Module Decomposition and Data Decomposition.

Figure 5.88 : Transmit Data

###### Receiver Packet Summary
Refer the section 2.1.1.4.8.6 and 2.2.1.2.8 for Module Decomposition and Data Decomposition.

        Figure 5.89 : Receiver Packet Summary
### DPSPL1255 Module
#### Programmable Logic
##### LMK PLL Test

Refer the section 5.1.1.2.1 for Flowchart.
###### File Configuration

Refer the section 5.1.1.2.1.1 for Flowchart.
###### File Dump
Refer the section 5.1.1.2.1.2 for Flowchart.
###### Single Data Write

Refer the section 5.1.1.2.1.3 for Flowchart.
###### Single Data Read

Refer the section 5.1.1.2.1.4 for Flowchart.
###### PLL Lock Status

Refer the section 5.1.1.2.1.5 for Flowchart.

##### RFDAC Test

Refer the section 2.1.2.2.2 and 2.2.2.1.2 for module decomposition and data decomposition.
        Figure 5.90: RFDAC Test

###### File Write
Refer the 2.1.2.2.2.1 and 2.2.2.1.2 section for module decomposition and data decomposition.

Figure 5.91: File Write

###### File Read
Refer the section 2.1.2.2.2.2 and 2.2.2.1.2 for module decomposition and data decomposition.

        Figure 5.92: File Read

###### Single Data Write
Refer the section 2.1.2.2.2.3 and 2.2.2.1.2 for module decomposition and data decomposition.

        Figure 5.93 :Single Data Write

###### Single Data Read
Refer the section 2.1.2.2.2.4 and 2.2.2.1.2 for module decomposition and data decomposition.
        Figure 5.94: Single Data Read

###### Power Level Transmission

Refer the section 2.1.2.2.2.5 and 2.2.2.1.2 for module decomposition and data decomposition.

    Figure 5.95: Power Level Transmission

###### RFDAC Data Transmission
Refer the section 2.1.2.2.2.6 and 2.2.2.1.2 for module decomposition and data decomposition.

 Figure 5.96 : RFDAC Data Transmission

###### RFDAC Reset
Refer the section 2.1.2.2.2.7 and 2.2.2.1.2 for module decomposition and data decomposition.

 Figure 5.97 : RFDAC Reset

### DPSPL1276 Module
#### Programmable Logic
##### LMK PLL Test

Refer the section 5.1.1.2.1 for Flowchart.
###### File Configuration

Refer the section 5.1.1.2.1.1 for Flowchart.
###### File Dump
Refer the section 5.1.1.2.1.2 for Flowchart.
###### Single Data Write

Refer the section 5.1.1.2.1.3 for Flowchart.
###### Single Data Read

Refer the section 5.1.1.2.1.4 for Flowchart.
###### PLL Lock Status

Refer the section 5.1.1.2.1.5 for Flowchart.

##### RFDAC Test

Refer the section 5.1.2.1.2
###### File Write

Refer the 5.1.2.1.2.1 for Flowchart.
###### File Read

Refer the 5.1.2.1.2.2 for Flowchart.
###### Single Data Write

Refer the 5.1.2.1.2.3 for Flowchart.
###### Single Data Read

Refer the 5.1.2.1.2.4 for Flowchart.
###### Power Level Transmission

Refer the 5.1.2.1.2.5 for Flowchart.
###### RFDAC Data Transmission

Refer the 5.1.2.1.2.6 for Flowchart.
###### RFDAC Reset

Refer the 5.1.2.1.2.7 for Flowchart.

## Data Detailed Design
### Board Information Data
- Board ID	:	DP-VPX-0233
- Hardware version	:	1.00
- Software version	:	1.00
- Serial number of the board	:	Serial number given for the specific board
- DDR4 size	:	8 GB
- User flash size	:	64 MB
- NAND Flash size	:	16 GB
- MRAM size	:	4 MB
- EEPROM size	:	4 Kb

# Requirements Traceability
Sl No.	Test Cases	Requirement ID in SRS	Section Number in SDD
1	Processor Test	DP_VPX_0233_MANUAL_PS_PROCS	2.1.1.3.1
	ALU Test	DP_VPX_0233_MANUAL_PS_PRCS_01	2.1.1.3.1.1
	FPU Test	DP_VPX_0233_MANUAL_PS_PRCS_02	2.1.1.3.1.2
2	DDR4 Test	DP_VPX_0233_MANUAL_PS_DDR	2.1.1.3.2
	Data bus Test	DP_VPX_0233_MANUAL_PS_DDR4_01	2.1.1.3.2.1
	Address bus Test	DP_VPX_0233_MANUAL_PS_DDR4_02	2.1.1.3.2.2
	Device Test	DP_VPX_0233_MANUAL_PS_DDR4_03	2.1.1.3.2.3
3	EEPROM Test	DP_VPX_0233_MANUAL_PS_EEPROM	2.1.1.3.3
	Upload Information Test	DP_VPX_0233_MANUAL_PS_EEPROM_01	2.1.1.3.3.1
	Data Retention Test	DP_VPX_0233_MANUAL_PS_EEPROM_02	2.1.1.3.3.2
	Checksum Test	DP_VPX_0233_MANUAL_PS_EEPROM_03	2.1.1.3.3.3
	Read/Write Test	DP_VPX_0233_MANUAL_PS_EEPROM_04	2.1.1.3.3.4
4	MRAM Test	DP_VPX_0233_MANUAL_PS_MRAM	2.1.1.3.4
	Upload Information Test	DP_VPX_0233_MANUAL_PS_MRAM_01	2.1.1.3.4.1
	Data Retention Test	DP_VPX_0233_MANUAL_PS_MRAM_02	2.1.1.3.4.2
	Checksum Test	DP_VPX_0233_MANUAL_PS_MRAM_03	2.1.1.3.4.3
	Full Memory Test	DP_VPX_0233_MANUAL_PS_MRAM_04	2.1.1.3.4.4
5	NAND Test	DP_VPX_0233_MANUAL_PS_NAND	2.1.1.3.5
	Upload Information Test	DP_VPX_0233_MANUAL_PS_NAND_01	2.1.1.3.5.1
	Data Retention Test	DP_VPX_0233_MANUAL_PS_NAND_02	2.1.1.3.5.2
	Checksum Test	DP_VPX_0233_MANUAL_PS_NAND_03	2.1.1.3.5.3
6	NOR Test	DP_VPX_0233_MANUAL_PS_NOR	2.1.1.3.6
	Upload Information Test	DP_VPX_0233_MANUAL_PS_NOR_01	2.1.1.3.6.1
	Data Retention Test	DP_VPX_0233_MANUAL_PS_NOR_02	2.1.1.3.6.2
	Checksum Test	DP_VPX_0233_MANUAL_PS_NOR_03	2.1.1.3.6.3
7	USB Test	DP_VPX_0233_MANUAL_PS_USB	2.1.1.3.7
	Read/Write Test	DP_VPX_0233_MANUAL_PS_USB_01	2.1.1.3.7.1
8	SATA Test	DP_VPX_0233_MANUAL_PS_SATA	2.1.1.3.8
	Read/Write Test	DP_VPX_0233_MANUAL_PS_SATA_01	2.1.1.3.8.1
9	UART Test	DP_VPX_0233_MANUAL_PS_UART	2.1.1.3.9
	Write Test	DP_VPX_0233_MANUAL_PS_UART_01	2.1.1.3.9.1
	Read Test	DP_VPX_0233_MANUAL_PS_UART_02	2.1.1.3.9.2
10	Ethernet Test	DP_VPX_0233_MANUAL_PS_ETHERNET	2.1.1.3.10
	Ethernet ping Test	DP_VPX_0233_MANUAL_PS_ETHERNET_01	2.1.1.3.10.1
11	RTC Test	DP_VPX_0233_MANUAL_PS_RTC	2.1.1.3.11
12	PCI Enumeration Test	DP_VPX_0233_MANUAL_PS_PCI	2.1.1.3.12
13	Temperature Sensor Test	DP_VPX_0233_MANUAL_PS_TEMPSNSR	2.1.1.3.13
14	Voltage Monitoring Test	DP_VPX_0233_MANUAL_PS_ADM	2.1.1.3.14
15	LMK PLL Test	DP_VPX_0233_MANUAL_PL_LMK_PLL	2.1.1.4.1
	File Configuration	DP_VPX_0233_MANUAL_PL_LMK_PLL_01	2.1.1.4.1.1
	File Dump	DP_VPX_0233_MANUAL_PL_LMK_PLL_02	2.1.1.4.1.2
	Single Data Write	DP_VPX_0233_MANUAL_PL_LMK_PLL_03	2.1.1.4.1.3
	Single Data Read	DP_VPX_0233_MANUAL_PL_LMK_PLL_04	2.1.1.4.1.4
	PLL Lock Status	DP_VPX_0233_MANUAL_PL_LMK_PLL_05	2.1.1.4.1.5
	Sysref Enable/Disable	DP_VPX_0233_MANUAL_PL_LMK_PLL_06	2.1.1.4.1.6
	Sysref Enable	DP_VPX_0233_MANUAL_PL_LMK_PLL_06_01	2.1.1.4.1.6.1
	Sysref Disable	DP_VPX_0233_MANUAL_PL_LMK_PLL_06_02	2.1.1.4.1.6.2
16	AFE7906 ADC Test	DP_VPX_0233_MANUAL_PL_ADC	2.1.1.4.2
	AFE Core Reset	DP_VPX_0233_MANUAL_PL_ADC_01	2.1.1.4.2.1
	AFE Single Write	DP_VPX_0233_MANUAL_PL_ADC_02	2.1.1.4.2.2
	AFE Single Read	DP_VPX_0233_MANUAL_PL_ADC_03	2.1.1.4.2.3
	AFE Bring up	DP_VPX_0233_MANUAL_PL_ADC_04	2.1.1.4.2.4
	AFE Core Initialization	DP_VPX_0233_MANUAL_PL_ADC_05	2.1.1.4.2.5
	JESD Bond Status	DP_VPX_0233_MANUAL_PL_ADC_06	2.1.1.4.2.6
	ADC Data Logging	DP_VPX_0233_MANUAL_PL_ADC_07	2.1.1.4.2.7
	HD2 Correction Enable	DP_VPX_0233_MANUAL_PL_ADC_08	2.1.1.4.2.8
	HD2 Coefficient Write	DP_VPX_0233_MANUAL_PL_ADC_08_01	2.1.1.4.2.8.1
	HD2 Coefficient Read	DP_VPX_0233_MANUAL_PL_ADC_08_02	2.1.1.4.2.8.2
	NCO Update	DP_VPX0233_MANUAL_PL_ADC_09	2.1.1.4.2.9
	All Channel Enable	DP_VPX0233_MANUAL_PL_ADC_09_01	2.1.1.4.2.9.1
	Single Channel Enable	DP_VPX0233_MANUAL_PL_ADC_09_02	2.1.1.4.2.9.2
	All Channel Disable	DP_VPX0233_MANUAL_PL_ADC_09_03	2.1.1.4.2.9.3
	Single Channel Disable	DP_VPX0233_MANUAL_PL_ADC_09_04	2.1.1.4.2.9.4
	AFE Dynamic Configuration	DP_VPX_0233_MANUAL_PL_ADC_10	2.1.1.4.2.10
	Device Health Status	DP_VPX_0233_MANUAL_PL_ADC_10_01	2.1.1.4.2.10.1
	Update Rx NCO	DP_VPX_0233_MANUAL_PL_ADC_10_02	2.1.1.4.2.10.2
	Set Rx DSA	DP_VPX_0233_MANUAL_PL_ADC_10_03	2.1.1.4.2.10.3
	Update Fb NCO	DP_VPX_0233_MANUAL_PL_ADC_10_04	2.1.1.4.2.10.4
	Set Fb DSA	DP_VPX_0233_MANUAL_PL_ADC_10_05	2.1.1.4.2.10.5
	Read Rx NCO	DP_VPX_0233_MANUAL_PL_ADC_10_06	2.1.1.4.2.10.6
	Read Fb NCO	DP_VPX_0233_MANUAL_PL_ADC_10_07	2.1.1.4.2.10.7
	Band selection	DP_VPX_0233_MANUAL_PL_AFE7906_ADC_11	2.1.1.4.2.11
	ADC Automation	DP_VPX_0233_MANUAL_PL_ADC_12	2.1.1.4.2.12
	Data Logging	DP_VPX_0233_MANUAL_PL_ADC_12_01	2.1.1.4.2.12.1
	Host Application	DP_VPX_0233_MANUAL_PL_ADC_12_01_01	2.1.1.4.2.12.1.1
	Target Application	DP_VPX_0233_MANUAL_PL_ADC_12_01_02	2.1.1.4.2.12.1.2
	Phase Matching	DP_VPX_0233_MANUAL_PL_ADC_12_02	2.1.1.4.2.12.2
	Host Application	DP_VPX_0233_MANUAL_PL_ADC_12_02_01	2.1.1.4.2.12.2.1
	Target Application	DP_VPX_0233_MANUAL_PL_ADC_12_02_02	2.1.1.4.2.12.2.2
17	RFDAC Test	DP_VPX_0233_MANUAL_PL_RFDAC	2.1.2.2.2
	File Write	DP_VPX_0233_MANUAL_PL_RFDAC_01	2.1.2.2.2.1
	File Read	DP_VPX_0233_MANUAL_PL_RFDAC_02	2.1.2.2.2.2
	Single Data Write	DP_VPX_0233_MANUAL_PL_RFDAC_03	2.1.2.2.2.3
	Single Data Read	DP_VPX_0233_MANUAL_PL_RFDAC_04	2.1.2.2.2.4
	Power Level Transmission	DP_VPX_0233_MANUAL_PL_RFDAC_05	2.1.2.2.2.5
	RFDAC Data Transmission	DP_VPX_0233_MANUAL_PL_RFDAC_06	2.1.2.2.2.6
	RFDAC Reset	DP_VPX_0233_MANUAL_PL_RFDAC_07	2.1.2.2.2.7
18	LVTTL Test	DP_VPX_0233_MANUAL_PL_LVTTL	2.1.1.4.3
	IO Mode Test	DP_VPX_0233_MANUAL_PL_LVTTL_01	2.1.1.4.3.1
	Clock Mode Test	DP_VPX_0233_MANUAL_PL_LVTTL_02	2.1.1.4.3.2
	Manual IO Mode Test	DP_VPX_0233_MANUAL_PL_LVTTL_03	2.1.1.4.3.3
	Manual Clock Mode Test	DP_VPX_0233_MANUAL_PL_LVTTL_04	2.1.1.4.3.4
	Manual Clock ON Test	DP_VPX_0233_MANUAL_PL_LVTTL_04_01	2.1.1.4.3.4.1
	Manual Clock OFF Test	DP_VPX_0233_MANUAL_PL_LVTTL_04_02	2.1.1.4.3.4.2
19	LVDS Test	DP_VPX_0233_MANUAL_PL_LVDS	2.1.1.4.4
	IO Mode Test	DP_VPX_0233_MANUAL_PL_LVDS_01	2.1.1.4.4.1
	Clock Mode Test	DP_VPX_0233_MANUAL_PL_LVDS_02	2.1.1.4.4.2
	Manual Mode Test	DP_VPX_0233_MANUAL_PL_LVDS_03	2.1.1.4.4.3
20	GPI/GPO Test	DP_VPX_0233_MANUAL_PL_GPI_GPO	2.1.1.4.5
	IO Mode Test	DP_VPX_0233_MANUAL_PL_GPI_GPO_01	2.1.1.4.5.1
21	UART(PL) Test	DP_VPX_0233_MANUAL_PL_UART	2.1.1.4.6
	Write Test	DP_VPX_0233_MANUAL_PL_UART_01	2.1.1.4.6.1
	Read Test	DP_VPX_0233_MANUAL_PL_UART_02	2.1.1.4.6.2
22	DDR4(PL) Test	DP_VPX_0233_MANUAL_PL_DDR4	2.1.1.4.7
	DDR4 Reset	DP_VPX_0233_MANUAL_PL_DDR4_01	2.1.1.4.7.1
	Data bus test	DP_VPX_0233_MANUAL_PL_DDR4_02	2.1.1.4.7.3
	Address bus test	DP_VPX_0233_MANUAL_PL_DDR4_03	2.1.1.4.7.4
	Device test	DP_VPX_0233_MANUAL_PL_DDR4_04	2.1.1.4.7.5
	Full Memory test	DP_VPX_0233_MANUAL_PL_DDR4_05	2.1.1.4.7.2
23	10G Ethernet Test	DP_VPX_0233_MANUAL_PL_10G	2.1.1.4.8
	Lane Repeater Configuration	DP_VPX_0233_MANUAL_PL_10G_01	2.1.1.4.8.1
	Core Reset	DP_VPX_0233_MANUAL_PL_10G_02	2.1.1.4.8.2
	Ethernet Reset	DP_VPX_0233_MANUAL_PL_10G_03	2.1.1.4.8.3
	Network Configuration	DP_VPX_0233_MANUAL_PL_10G_04	2.1.1.4.8.4
	Transmit Data	DP_VPX_0233_MANUAL_PL_10G_05	2.1.1.4.8.5
	Receiver Packet Summary	DP_VPX_0233_MANUAL_PL_10G_06	2.1.1.4.8.6

######
# Appendix A
Structure Name : _SDPVPX0233_Command_Header
Member Name	Type	Description
m_uiHeader	Unsigned int	It indicates the test case Id for performing the respective test case operations. / DPVPX0233_HDR_HOST_CMD = 0x40510C3D, / DPVPX0233_HDR_TRGT_RSP = 0x1B610859
m_ucGroupID	Unsigned Char	It refers the selected test mode such as ADC Automation and Phase Matching. / DPVPX0233_GID_ADC = 0, / DPVPX0233_GID_ADC_PHASE_MATCH = 1
m_ucTestID	Unsigned Char	It indicates the test case Id for performing the respective test case operations . / DPVPX0233_TID_ADC_AUTOMATION = 0, / DPVPX0233_TID_ADC_PHASE_MATCH = 1

Structure Name : _SDPVPX0233_Command_Packet
Member Name	Type	Description
m_SHeader	SDPVPX0233_Command_Header	It refers the fixed value for data integrity.
m_usDataSz	Unsigned Short	It refers the Size of the data.
m_arrcData	Char	It refers the Array of Buffer data.
m_ucCheckSum	Unsigned Char	It refers the Checksum of this packet to identify the data loss.

Structure Name : _SDPVPX0233_Response_Packet
Member Name	Type	Description
m_SHeader	SDPVPX0233_Command_Header	It refers the fixed value for data integrity.
m_usDataSz	Unsigned Short	It refers the Size of the data.
m_arrcData	Char	It refers the Array of Buffer data.
m_cMsgStatus	Char	It refers the Status of the command packet.
m_ucCheckSum	Unsigned Char	It refers the Checksum of this packet to identify the data loss.

# Appendix B
Description for Phase Matching Buttons:

Get Data :
This Button is used to get the Non-Calibrated values and their Phase Angle and Fundamental Power of each channels in ADC through Target Application.

Calibrate Phase :
This Button is used to Export the Phase Difference of the ADC channels in Log file. This File contains Phase Matching values of All ADC Channels.

Measure Phase Difference :
This Button is used to get Calibrated values and their Phase Angle and Fundamental Power of each channels in ADC.