SOFTWARE REQUIREMENT SPECIFICATIONS
FOR
6U VPX Zynq MPSoC and AFE7906 based Digital receiver Module with 12Channel 3GSPS ADC I/P 5MHz to 12 GHz I/P IBW 600MHz

DOCUMENT TITLE	SOFTWARE REQUIREMENT SPECIFICATIONS FOR 6U VPX Zynq MPSoC and AFE7906 based Digital receiver Module with 12Channel 3GSPS ADC I/P 5MHz to 12 GHz I/P IBW 600MHz
DOCUMENT REFERENCE	DP-VPX-0227-V1-01-SRS-1V00
VERSION NUMBER	1.00
VERSION DATE	April 16, 2025
PREPARED BY	Name: Ashok R / Sign:
DOCUMENT REVIEW BY	Name: Gowthami V / Sign:
TECHNICAL REVIEW BY	Name: Kingshuk mitra / Sign:
PROCESS REVIEW BY	Name: Gowthami V / Sign:
APPROVED BY	Name: DRB / Sign:

Copyright @ (2024) by Data Patterns
All right reserved. These materials are proprietary to Data Patterns and no part of these materials should be reproduced, published in any form by any means, electronic or mechanical including photocopy or any information storage or retrieval system nor should the materials be disclosed to third parties without the written authorization of Data Patterns.

Revision History
S. NO.	VER. NO.	VER. DATE	CHANGED BY	SECTION (S) CHANGED	DESCRIPTION / OF CHANGE
1	0V01	October 7, 2024	Ashok R	-	Initial Version
2	0V02	November 4, / 2024	Ashok R	4.2.2.2.2.1 to 4.2.2.2.2.6, 4.2.2.2.6 t0 4.2.2.2.8	Internal Comments closed(Refer DP-VPX-0227-V1-01-SRR-0V02)
3	0V03	December 19, / 2024	Ashok R	4.2.2.2.2, 4.2.2.2.4 and 7	Internal Comments closed(Refer DP-VPX-0227-V1-01-SRR-0V03)
4	0V04	February 14, / 2025	Ashok R	4.2.2.2.9 to 4.2.2.2.12	Internal Comments closed(Refer DP-VPX-0227-V1-01-SRR-0V04)
5	0V05	March 24, / 2025	Ashok R	4.2.2.2.2, 4.2.2.2.5 and 4.2.2.2.7	Internal Comments closed(Refer DP-VPX-0227-V1-01-SRR-0V05)
6	0V06	April 8, 2025	Ashok R	4, 4.2.2.1.12, 4.2.2.2.3, 4.2.2.2.11 and 7	DRB Comments closed(Refer DP-VPX-0227-V1-01-SRR-0V06) DRB APPROVED ON 16-4-2025.
7	1V00	March 24, 2026	Gowthami V	-	Base Lined

# Introduction
## Purpose
The purpose of this document is to bring out the requirements, identified for the design and development of test software for DP-VPX-0227 module. It aids the designer to test & qualify the hardware through the test software.
## Scope
The scope of this document describes the aspects related to functional and performance tests of DP-VPX- 0227 module through Linux ATP. The identification details are provided below:

Table 1: Entities Involved in ATP Development
Identification Number	DP-VPX-0227-V1-01-SRS-1V00
Title	SOFTWARE REQUIREMENT SPECIFICATIONS FOR 6U VPX Zynq MPSoC and AFE7906 based Digital receiver Module with 12Channel 3GSPS ADC I/P 5MHz to 12 GHz I/P IBW 600MHz
Version Number	1.00
Abbreviation	SRS (Software Requirement Specification)

## Definitions, Acronyms, and Abbreviations
The acronyms and abbreviations used in this document are listed in the below Table 2.
Table 2 : List of Acronyms and Abbreviations
Acronyms	Abbreviation
HRS	Hardware Requirement Specification
SRS	Software Requirement Specification
DDR4	Double Data Rate
EEPROM	Electrically Erasable Programmable Read Only Memory
SATA	Serial AT Attachment
USB	Universal Serial Bus
ADC	Analog to Digital Converter
SPI	Serial Peripheral Interface
PLL	Phase Locked Loop
RF	Radio Frequency
IF	Intermediate Frequency
UART	Universal Asynchronous Receiver Transmitter
PL	Programmable Logic
PS	Processing System
RTC	Real Time Clock
JESD	JEDEC Serializer De-serializer
ATP	Acceptance Test Plan
I2C	Inter – Integrated Circuit
MRAM	Magneto-resistive Random Access Memory
NCO	Numerical Controller Oscillator Frequency
DSA	Digital Step Attenuation
PCIe	Pheripheral Component Interconect Express

## References
The following list of documents were referred for deriving this requirements specification
Table 3 : Reference Documents
S. No	Document Name	Document Reference
1	Hardware Requirement Specification - DP-VPX-0227	DP-VPX-0227-000-HRS-0V05
2	Software Requirement Specification - DP-SPL-0220	DP-SPL-0220-V1-01-SRS-1V00
3	Common Software Requirement Specification	DP-COMMON-SDG-SRS(ATP-ATE)-0V05-DRAFT

## Document Overview
Section 1: Introduction
Describes about the introduction of this document such as purpose, scope, and document overview. It also lists the acronyms and referenced documents.

Section 2: Overall Description
This section provides overall description covering the product perspective, product functions, user characteristics, operating environment, design and implementation constraints, user documentation and assumptions & dependencies.
Section 3: External Interface Requirements
This section describes the details of user interfaces, hardware interfaces, software interfaces and communication interfaces.
Section 4: Functional Requirements
This section lists out the details of functional requirements of Common tests.
Section 5: Software System Attributes
This section specifies performance requirements, safety requirements, security requirements, software quality attributes and business rules.
Section 6: Other Requirements
This section describes other requirements.
Section 7: Requirements Traceability
This section lists out the requirement traceability matrix.

# Overall Description
## Product Perspective
DP-VPX-0227 is an 6U VPX 9-10GHz 9Channel Digital Receiver with integrated RF Down converter module, Zynq Ultrascale Plus re-programmable (MPSoC) hardware in combination with Quad core ARM processor for signal processing.

The Processing section (PS) operates with 64-bit Quad Arm core which performs the system management functionality. This Section shall have on board 32 Bit + 8Bit ECC DDR4 dynamic memories, two 64MB QSPI NOR flash for boot configuration, an EEPROM memory of 4KB via I2C interface to store the DDR4 memory configuration details, an eMMC NAND flash of 16GB for application and user storage and a 16Mbit MRAM for storing critical information.It shall provide USB3.0 (USB 2.0 Backward Compatible) and 1000Base-T Ethernet for Communication and 2x RS422 (or) 2x RS232 UART port for debugging purpose.

The Programmable Logics(PL) Section shall have on board 4GB 32bit DDR4 dynamic memory and an 128MB QSPI NOR flash for user storage. It shall have two RS232 UART port for communication purpose.One x8 PCIe interface,x4 10G ethernet and x4RIO interface to P1 connector then One x4 PCIe interface,x4 RIO interface to P2 Connector.Also one x4 10G ethernet to P4 Connector.One I2C interface to P0 connector.It consists of multi board sync input group such as Trigger,SOB and Sysref for ADC channels Synchronization.

This module have AFE7906 chip to handle nine number of 960MHz to 1680MHz input RF signals with 3GSPS sampling rate with JESD204B standard and also shall have a XMC Connector to connect with 9 Channel 9-10GHz Receiver Down converter board, IF OUT as 1320MHz with 360MHz Instantaneous BW DDC Piggy Module. This module shall have low noise on board clock generation and distribution section to provide jitter free Sampling Clock to AFE7906 ADC, FPGA JESD Cores and Piggy Modules. This section shall also have a option of choosing internal and external reference clock.

On board Power Generator & Sequencing section shall be used for generation of all the power supplies in the module from +12V & +5V. This module shall have VPX P0 Connector for Power Supply, VPX P1 & P2 Connector all communication links and debugging interfaces and x24LVTTL or x12 LVDS in P2 and P4 for Field IOs. This module shall have a temperature sensor for monitoring the FPGA temperature.
The module shall be of conduction cooled type with Ruggedizer and wedge lock arrangement and comply 1” slot width dimensions.

Onboard power supply generation such as +5V,+6V,+3.5V,-5V for down converter module DP-CRF-7910 by using external +12V supply.

The main features of DP-VPX-0227 module is given below:
- Zynq Ultra-scale Plus MPSoC from Xilinx
- One 32 Bit+8 Bit ECC 4GB DDR4 Memory from PS & 4GB 32 Bit DDR4 Memory from PL
- Two 14 bit 3GSPS ADC 9 channels with JESD204B Interface.
- One XMC Connector for DDC Piggy module DP-CRF-7910.
- 1 x8 PCIe interface to P1
- 1 x4 PCIe interface to P2
- 2 x1 PCIe/SATA interface
- 1 x1 USB 3.0 interface (USB 2.0 Backward Compatible)
- 1 x 1G 1000 Base-T RGMII interface from PS.
- 1 x 1G Base-T PS SGMII/PL RGMII interface
- 2 x RS422 interface or 4 xRS232.
- 2 x4 RIO1 to support 10G Ethernet
- 2 x4 10Gig Ethernet from PL.
- 28 Single-Ended IO (LVTTL/LVCMOS) or 12 Differential IO (LVDS) to P2 and P4 connector.
- On board clock generator section with Internal & External Reference
- On board Power supply generator & sequencer
- 9 Channel 3GSPS ADC input receiver.

The main applications of DP-VPX-0227 module is given below:
- Digital Receiver for RF signals.
- Data Communications.
- Signal Processing.

### Block Diagram

Figure 1: Block diagram of DP-VPX-0227
## Software Perspective
1. This shall be a standalone ATP Software whose main purpose is to qualify functionality of the devices available on DP-VPX-0227 Processor board.
2. The Software shall run at the DP-VPX-0227 Processor board.
## Product Functions
DP-VPX-0227 is an 6U VPX 9-10GHz 9Channel Digital Receiver with integrated RF Down converter module, Zynq Ultrascale Plus re-programmable (MPSoC) hardware in combination with Quad core ARM processor for signal processing.
DP-VPX-0227 software requirements are categorized into 2 major requirements based on the MPSOC’s
- Processing Section
- Programmable Logic
## User Classes and Characteristics
NA
## Operating Environment
The operating environment details of the software are given in the below table.
Table 4 : Operating Environment (Target Application)
S. No	Name	Details
1	Operating System	Linux 5.10
2	Architecture	AARCH 64
3	Cross Compiler	aarch64-xilinx-linux-gcc
4	Build Tool	Petalinux 2021.2
5	Programming Language	C

Table 5 : Operating Environment (Host Application)
S. No	Name	Details
1	Operating System	Windows 7
2	Architecture	X86
3	Build Tool	Qt Creator
4	Programming Language	C++

## Design and Implementation Constraints
COM1 / ttyPS0 of DP-VPX-0227 target board is used as the debug port and will not be tested separately as part of application software. It will be considered as working, if the boot up messages displayed on the console during board booting.
## User Documentation
The Following Documents should be prepared and submitted for DP-VPX-0227
1. Software Requirement Specifications(SRS)
2. Software Design Document(SDD)
## Assumptions and Dependencies
NA

# External Interface Requirements
## User Interfaces
The following main menu shall be displayed according to the selection.

          -------------------------------------------------------------------------------------------------
                  1. Manual Mode Test
          2. Auto Mode Test
              99. Exit
        --------------------------------------------------------------------------------------------------
Enter the option :

The console shall be cleared after getting input from user and the selected test case options will be displayed from the beginning of the console.

## Hardware Interfaces
Table 6 : Hardware Interfaces
S. No	Hardware	Description
	RS232 or RS422 Serial Port	UART Serial port used for debugging.
	Ethernet	Ethernet is used to transfer data.
	DDR4	4GB 32Bit DDR4 +8 Bit ECC Memory Interfaced to PS side. 4GB 32Bit DDR4 Memory Interfaced to PL side.
	MRAM	4Mbit MRAM for critical Information recording.
	NAND FLASH (User Flash)	16GB eMMC NAND Flash is used as the user flash for storage device.
	NOR FLASH (Boot Flash)	128MB PS NOR Flash is used as the boot flash.
	NOR FLASH (User Flash)	128MB PL NOR Flash is used as the user flash.
	EEPROM	256k bits EEPROM is used for module information storage
	Temperature Sensor	It is used to monitor the Internal and External temperature.
	USB	USB memory stick is used for USB testing.
	SATA	SATA device (SATA DOM) is used for SATA testing.
	Programmable Logic	Programmable logic is used to configure AFE7906 ADC and LMK04828 PLL based on the board configuration.

## Software Interfaces
Table 7: Target Software interface

S. No	Software	Requirement Description
1.	Windows	Putty
2.	Linux	Minicom

Table 8: Target Software interface

S. No	Software	Requirement Description
1.	Windows	Qt Creator

## Communications Interfaces
UART
    - Serial cable (RS232 or RS422) is required to connect the Target to the serial port of the Host PC for target console.
    - The DP-VPX-0227 Consists of 4No’s of RS232 ports and 2No’s of RS422 ports.

Table 9: UART Communication Interface
S. No	Configuration	Range
1	Baud rate	RS232- 115200 / RS422- 115200
2	Parity	None
3	Stop Bits	1
4	Number of bits	8

1. Ethernet
    - Ethernet is required to connect the target to the LAN. It is used to transfer data between the target board and the host machine. It is also used for target console via ssh.

# Functional Requirements

Table 10: Functional Requirement Test
Requirement Identification Number	Requirement Description	Reference Requirement ID
PROCESSING SECTION
DP_VPX_0227_MANUAL_PS_PRCS	Processor Test	DP_SDG_COM_PERI_04_PROCS_01
DP_VPX_0227_MANUAL_PS_DDR4	DDR4 Test	DP_SDG_COM_MEM_01_DDR_07
DP_VPX_0227_MANUAL_PS_EEPROM	EEPROM Test	DP_SDG_COM_MEM_01_EEPROM_02
DP_VPX_0227_MANUAL_PS_MRAM	MRAM Test	DP_VPX_0206_MRAM_03_01_04
DP_VPX_0227_MANUAL_PS_NAND	NAND Flash Test	DP_SDG_COM_MEM_01_FLASH_04
DP_VPX_0227_MANUAL_PS_NOR	NOR Flash Test	DP_VPX_0206_NORFLASH_03_01_06
DP_VPX_0227_MANUAL_PS_USB	USB Test	DP_VPX_0206_USB_03_01_07
DP_VPX_0227_MANUAL_PS_SATA	SATA Test	DP_SDG_COM_MEM_01_SATA_06
DP_VPX_0227_MANUAL_PS_UART	UART Test	DP_SDG_COM_COMM_02_RS422RS232/RS485_01
DP_VPX_0227_MANUAL_PS_ETH	Ethernet Test	DP_SDG_COM_COMM_02_ETH_02
DP_VPX_0227_MANUAL_PS_RTC	RTC Test	DP_SDG_COM_PERI_04_RTC_04
DP_VPX_0227_MANUAL_PS_TEMPSNSR	Temperature Sensor Test	DP_SDG_COM_PERI_04_TEMPSNSR_13
PROGRAMMABLE LOGIC
DP_VPX_0227_MANUAL_PL_LMK04828 PLL	LMK04828 PLL Test	DP_SPL_0220_MANUAL_PL_LTC_PLL
DP_VPX_0227_MANUAL_PL_AFE7906_ADC	AFE7906 ADC Test	New
DP_VPX_0227_MANUAL_PL_DIGITAL_ATTEN	Digital Attenuation	New
DP_VPX_0227_MANUAL_PL_DDR4	DDR4 (PL) Test	DP_SDG_COM_MEM_01_DDR_07
DP_VPX_0227_MANUAL_PL_NORFLASH	NOR Flash (PL) Test	DP-SPL-6865_MC_FLASH_OPERATION_06
DP_VPX_0227_MANUAL_PL_RGMII_1G_ETH	RGMII Test	New
DP_VPX_0227_MANUAL_PL_UART	UART (PL) Test	DP_SDG_COM_COMM_02_RS422RS232/RS485_01
DP_VPX_0227_MANUAL_PL_AURORA	Aurora Test	DP_SPL_0220_MANUAL_PL_SFP
DP_VPX_0227_MANUAL_PL_10G	10G Test	DP_SPL_0220_MANUAL_PL_SFP
DP_VPX_0227_MANUAL_PL_ADM	ADM(PL) Test	New
DP_VPX_0227_MANUAL_PL_CLOCK_IO	Clock Test	DP_SPL_0220_MANUAL_PL_LVTTL
DP_VPX_0227_MANUAL_PL_LVDS_IO	LVDS IO Test	DP_SPL_0220_MANUAL_PL_LVTTL
DP_VPX_0227_MANUAL_PL_TTL_IO	TTL IO Test	DP_SPL_0220_MANUAL_PL_LVTTL
DP_VPX_0227_MANUAL_PL_JUNC_TEMP	FPGA Junction Temeperature	DP_SPL_0220_MANUAL_PL_JN_TEMP
DP_VPX_0227_MANUAL_PL_PCIe	PCIe Test	New

## Test Configuration
Requirement ID :
DP_VPX_0227_CONFIG
Test configuration shall enable the user to configure each of the Auto/manual mode test cases. If the configuration file is already available (in a predefined path) then it shall be be read and stored in an appropriate data structures. If configuration file is unavailable (in a predefined path) then the following test cases shall be perform.
### Auto Mode Test Selection
Requirement ID :
DP_VPX_0227_MODE_AUTO
Description :
This shall configure the Auto Mode test cases by getting the input from user to Enable/Disable the state of all the available test cases in Auto mode.
### Manual Mode Test Selection
Requirement ID :
DP_VPX_0227_MODE_MANUAL
Description :
This shall configures the Manual Mode test cases by getting the input from user to Enable/Disable the state of all the available test cases in Manual mode.
### Test Specific Details
Requirement ID :
DP_VPX_0227_TEST_DETAIL
Description :
This is to provide the configuration details specific to the enabled test cases in either or both of the auto and manual mode test case options.

## Test Performance
Requirement ID :

DP_VPX_0227_PERFORMANCE
### Auto Mode Test Performance
The auto mode test performance shall perform the auto mode test cases that are enabled using the target configuration for qualifying the board. The selection of the auto mode test depends on the user (Refer 4.1 for Test Configuration). The following are the inputs for performing auto mode test :

- ENTER THE NO OF CYCLE[1-200]:
- ITERATION GAP (in Seconds) [1s - 10s]:
- INTER-ITERATION GAP (in Seconds) [1s – 10s]:

The user shall need to enter input first. The enabled auto mode test cases will then be performed for the specified number of cycles. The summary of the auto mode test results will be displayed as a consolidated report once the test process is over. The Test process shall be paused at any time (using Ctrl+C) to see the status report and can be continued further or stopped to get back to the main menu. A consolidated report shows the status of the auto mode Test cases that are executed shall be displayed in the console and the report shall be stored in a file.
### Manual Mode Test Performance
The manual mode test performance shall perform the manual mode test cases that are enabled using the target configuration for qualifying the board. The selection of the manual mode test depends on the user (Refer 4.1 for Test Configuration).
The following are the details regarding the test cases included in manual mode Test Performance.

#### Processing Section
Requirement ID :
DP_VPX_0227_MANUAL_PS
##### Processor Test
The following test cases shall be performed to qualify the processor ALU and FPU test cases. The following test cases are listed below.
Requirement ID :
DP_VPX_0227_MANUAL_PS_PRCS
###### ALU Test
Requirement ID	DP_VPX_0227_MANUAL_PS_PRCS_01
Description	This test shall be performed to qualify the processor (ALU). The following tests are to be carried out. / 1. Arithmetic operation Test (Addition, Subtraction, Division and Multiplication) / 2. Shift operation Test (Left shift and Right shift) / 3. Logical operation Test (AND, OR and NOT)

###### FPU Test
Requirement ID	DP_VPX_0227_MANUAL_PS_PRCS_02
Description	This test shall be performed to qualify the processor (FPU). The following tests are to be carried out. / 1. Floating point Arithmetic Test (Floating point Addition, Subtraction, Multiplication and Division).

##### DDR4 Test
The following test cases shall be performed to qualify the DDR4. The following test cases are listed below
Requirement ID :
DP_VPX_0227_MANUAL_PS_DDR4
###### Data Bus Test
Requirement ID	DP_VPX_0227_MANUAL_PS_DDR4_01
Description	This test shall be performed to qualify the data bus lines in the memory device. The Walking 1's and Walking 0's test shall be carried out. Perform memory walking ones test by left shifting the data, 1 bit at a time until it reaches the 32nd bit. Perform memory walking zero tests by left shifting the complement of data , 1 bit at a time until it reaches the 32nd bit. If both test cases are success, then the test shall be considered as PASS, otherwise FAIL.

###### Address Bus Test
Requirement ID	DP_VPX_0227_MANUAL_PS_DDR4_02
Description	This test shall be performed to qualify the address bus lines in the memory device. A base address shall be written with known Pattern and rest of the addresses are written with Anti pattern. Read the data from all these locations. If the read value and written value are not same, then return error else the base address shall be written with anti pattern and rest of the addresses are written with pattern. Read the data from all these locations. If the read value and written value are same, then test shall be considered as PASS, otherwise FAIL

###### Device Test
Requirement ID	DP_VPX_0227_MANUAL_PS_DDR4_03
Description	This test shall be performed to determine whether every bit in the device is capable of holding both 0 and 1. Write the incremental counter 32-bit data (0x00 00 00 00 , 0x00 00 00 01, 0x00 00 00 02,......,n) in the allocated memory of particular size (RAM size). Start reading the data from starting memory location and check for previously written data if both are not same then return error, else write inverted data to same location. Repeat this sequence for next memory location until maximum size (RAM size) is reached. Start reading the data from first memory location and check for previously written inverted data. If both are not same then return error else repeat this sequence for next memory location until maximum size (RAM size) is reached. If the written values and read back values are same, then test shall be considered as PASS, otherwise FAIL.

##### EEPROM Test
The following test cases shall be performed to qualify the EEPROM. The following test cases are listed below
Requirement ID :
DP_VPX_0227_MANUAL_PS_EEPROM
###### Upload Board Information
Requirement ID	DP_VPX_0227_MANUAL_PS_EEPROM_01
Description	This test shall be performed to validate the proper initialization of flash device. The device shall be initialized and a predefined data shall be loaded and read back to ensure proper initialization of the device. If both values are same, then test shall be declared as PASS, otherwise FAIL. / Note: Information shall be loaded only once for each board.

###### Data Retention Test
Requirement ID	DP_VPX_0227_MANUAL_PS_EEPROM_02
Description	This test shall be performed to qualify the authenticity of the memory device. A read operation shall be performed to get the Data stored in the memory. If the read data is the expected value, then test shall be declared PASS, otherwise FAIL.

###### Checksum Test
Requirement ID	DP_VPX_0227_MANUAL_PS_EEPROM_03
Description	This test shall performed to check the data integrity in the memory device. The data in the memory device shall be read from a fixed area/locations and checksum shall be computed. The computed checksum shall be compared against the pre-loaded/known checksum value.

###### Write / Read Test
Requirement ID	DP_VPX_0227_MANUAL_PS_EEPROM_04
Description	This test shall be performed by getting offset address and data from the user as an input and write the input data in the input address and read the data from the user given input address, If both write and read data are same then shall be considered as PASS else FAIL.

##### MRAM Test
The following test cases shall be performed to qualify the MRAM. The following test cases are listed below
Requirement ID :
DP_VPX_0227_MANUAL_PS_MRAM
###### Upload Board Information
Requirement ID	DP_VPX_0227_MANUAL_PS_MRAM_01
Description	Refer the section 4.2.2.1.3.1 .

###### Data Retention Test
Requirement ID	DP_VPX_0227_MANUAL_PS_MRAM_02
Description	Refer the section 4.2.2.1.3.2 .

###### Checksum Test
Requirement ID	DP_VPX_0227_MANUAL_PS_MRAM_03
Description	Refer the section 4.2.2.1.3.3 .

###### Memory Test
Requirement ID	DP_VPX_0227_MANUAL_PS_MRAM_04
Description	This test shall be conducted to validate the Read and Write operation in the MRAM. All memory locations shall be written with counter and inverted counter data and same shall be read back. Verify read and write values, if both are same, then test shall be declared as PASS, otherwise FAIL.

##### NAND Flash Test
The following test cases shall be performed to qualify the NAND Flash. The following test cases are listed below
Requirement ID :
DP_VPX_0227_MANUAL_PS_NANDFLASH
###### Upload Board Information
Requirement ID	DP_VPX_0227_MANUAL_PS_NANDFLASH_01
Description	Refer the section 4.2.2.1.3.1

###### Data Retention Test
Requirement ID	DP_VPX_0227_MANUAL_PS_NANDFLASH_02
Description	Refer the section 4.2.2.1.3.2 .

###### Checksum Test
Requirement ID	DP_VPX_0227_MANUAL_PS_NANDFLASH_03
Description	Refer the section 4.2.2.1.3.3 .

##### NOR Flash Test
The following test cases shall be performed to qualify the NOR Flash. The following test cases are listed below
Requirement ID :
DP_VPX_0227_MANUAL_PS_NORFLASH
###### Upload Board Information
Requirement ID	DP_VPX_0227_MANUAL_PS_NORFLASH_01
Description	Refer the section 4.2.2.1.3.1 .

###### Data Retention Test
Requirement ID	DP_VPX_0227_MANUAL_PS_NORFLASH_02
Description	Refer the section 4.2.2.1.3.2 .

###### Checksum Test
Requirement ID	DP_VPX_0227_MANUAL_PS_NORFLASH_03
Description	Refer the section 4.2.2.1.3.3 .

##### USB Test
The following test cases shall be performed to qualify the USB. The following test cases are listed below
Requirement ID :
DP_VPX_0227_MANUAL_PS_USB
###### Read/Write Test
Requirement ID	DP_VPX_0227_MANUAL_PS_USB_01
Description	This will mount the USB memory stick partition in the mount directory & shall create a file in the USB device and by performing the read/write operations on that file. If both written data and read data are same then test shall be declared as PASS, otherwise FAIL. / NOTE: Make sure that the USB device is connected with the board and formatted as linux Partition.

##### SATA Test
The following test cases shall be performed to qualify the SATA. The following test cases are listed below
Requirement ID :
DP_VPX_0227_MANUAL_PS_SATA
###### Read/Write Test
Requirement ID	DP_VPX_0227_MANUAL_PS_SATA_01
Description	This test shall mount the SATA device in the specified mount point and will create and write sample data in a file in the mounted partition. This test shall read the file content from the device and compare with the written file. If both written and read data is same, it will return success, otherwise failure. / NOTE: Make sure that the SATA device is connected with the board and formatted as linux Partition.

##### UART Test
The test cases shall be performed to qualify the UART. The following test cases are listed below
Requirement ID :
DP_VPX_0227_MANUAL_PS_UART
###### Write Test
Requirement ID	DP_VPX_0227_MANUAL_PS_UART_01
Description	This test shall be performed to qualify the UART Write Functionality. A user entered data or a predefined data is transmitted. If the transmitted data and the data received at the host are same, declare the test case as PASS, otherwise as FAIL.

###### Read Test
Requirement ID	DP_VPX_0227_MANUAL_PS_UART_02
Description	This test shall be performed to qualify the UART Read Functionality. The data entered at the host is received. If the received data and the data transmitted from the host are same, declare the test case as PASS, otherwise as FAIL. / NOTE: Make sure that the SATA device is connected with the board and formatted as linux Partition.

##### Ethernet Test
The following test cases shall be performed to qualify the Ethernet. The following test cases are listed below
Requirement ID :
DP_VPX_0227_MANUAL_PS_ETH
###### Ethernet Ping Test
Requirement ID	DP_VPX_0227_MANUAL_PS_ETH_01
Description	This test shall be performed between 2 ports of different systems considering that both ports are connected with LAN cable. This shall be carried out by sending & receiving data through ping command to/from Target port IP address. If ping test is passed, declare the test case as PASS, otherwise as FAIL. / Note: Pre-loaded data will be transferred by Operating System as part of Ethernet Ping test

##### RTC Test
The following test cases shall be performed to qualify the RTC. The following test cases are listed below
Requirement ID :
DP_VPX_0227_MANUAL_PS_RTC
###### RTC Test
Requirement ID	DP_VPX_0227_MANUAL_PS_RTC_01
Description	The RTC parameters are configured with the user selected values and reading it after a predefined gap (EX. 8 secs). If the read time is updated with an addition of predefined gap then the test is considered as pass, else fail. / Note: The test result with tolerance of +/-1 second in addition to the expected seconds will be accepted.

##### Temperature Sensor Test
The following test cases shall be performed to qualify the Temperature Sensor. The following test cases are listed below
Requirement ID:
DP_VPX_0227_MANUAL_PS_TEMPSNSR
###### Temperature Sensor Test
Requirement ID	DP_VPX_0227_MANUAL_PS_TEMPSNSR_01
Description	This test shall be carried out by reading the Temperature Sensor value and checking whether the read value is within the low limit and high limit of Local temperature which is configured by the user. If the Temperature values are within the limits then the test case is declared as PASS, otherwise as FAIL. / Note:Temperature Sensor Limits are listed below. / Local Temperature ( -10 to 70) / External Temperature(-10 to 70)

#### Programmable Logic
Requirement ID :
DP_VPX_0227_MANUAL_PL
##### LMK04828 PLL Test
The following test cases shall be performed to qualify the LMK04828 PLL Interface. The following test cases are listed below.
Requirement ID :
DP_VPX_0227_MANUAL_PL_LMK04828 PLL
###### File Configuration
Requirement ID	DP_VPX_0227_MANUAL_PL_LMK04828 PLL_01
Description	This operation shall provide an option to configure PLL. This can be done through Reading and writing the Data in particular offset through SPI Interface. / Note: PLL_CONFIG.txt file will be used to configure the PLL.

###### File Dump
Requirement ID	DP_VPX_0227_MANUAL_PL_LMK04828 PLL_02
Description	This operation shall provide an option to Read the Data from PLL trough SPI Interface.

###### Single Write
Requirement ID	DP_VPX_0227_MANUAL_PL_LMK04828 PLL_03
Description	This test shall provide an option to write single Data through SPI Interface.

###### Single Read
Requirement ID	DP_VPX_0227_MANUAL_PL_LMK04828_PLL_04
Description	This test shall provide an option to Read Back single data through SPI Interface.

##### AFE7906 ADC Test Cases
The following test cases shall be performed to qualify the AFE7906 ADC Interface. The following test cases are listed below.
Requirement ID :
DP_VPX_0227_MANUAL_PL_AFE7906_ADC
###### AFE Core Reset
Requirement ID	DP_VPX_0227_MANUAL_PL_AFE7906_ADC_01
Description	This operation provides an option to Reset the AFE chip. / Note: 2 AFE chips are available for Resetting.

###### AFE Single Write
Requirement ID	DP_VPX_0227_MANUAL_PL_AFE7906_ADC_02
Description	This operation provides an option to perform the single write operation in AFE chip.

###### AFE Single Read
Requirement ID	DP_VPX_0227_MANUAL_PL_AFE7906_ADC_03
Description	This operation provides an option to perform the single read operation in AFE chip.

###### AFE Bring-up
Requirement ID	DP_VPX_0227_MANUAL_PL_AFE7906_ADC_04
Description	This operation shall be performed to configure the AFE7906 ADC. This can be done by loading Text file which was followed by Reset and Core Initialization. / Note: A separate utility Latte Software used to generate the Text file for 2 AFE chips.[AFE 1 having 5 Rx channels & AFE 2 having 4 Rx channels]. / ADC_CONFIG.txt file is used to configure the ADC.

###### AFE Core Initialization
Requirement ID	DP_VPX_0227_MANUAL_PL_AFE7906_ADC_05
Description	This operation provides an option to check the Core Initialization for AFE Chip. / Note: 2 AFE chips are available for Resetting.

###### JESD Bond Status
Requirement ID	DP_VPX_0227_MANUAL_PL_AFE7906_ADC_06
Description	This Operation shall be performed to synchronize the JESD and FPGA. It can be verified by reading the BOND STATUS REGISTER.

###### ADC Sync
Requirement ID	DP_VPX_0227_MANUAL_PL_AFE7906_ADC_07
Description	This Operation shall be performed to set the ADC sync bond status. / Note: ADC Synchronize should be done before ADC Data Logging.

###### ADC Band Selection
Requirement ID	DP_VPX_0227_MANUAL_PL_AFE7906_ADC_08
Description	This Operation shall provide an option to select the band of ADC which is either Narrow Band/Wide Band.

###### Data Logging
Requirement ID	DP_VPX_0227_MANUAL_PL_AFE7906_ADC_09
Description	This operation shall be performed to get the IQ Data From AFE chip. / Note: Data Plotting is done by a separate tool – HSDC Pro, 9 number of Rx channels are available to get the IQ Data.

###### NCO Update
Requirement ID	DP_VPX_0227_MANUAL_PL_AFE7906_ADC_10
Description	This operation shall be performed to Enable / Disable the NCO update in ADC.

###### HD2 Correction Enable
Requirement ID :
DP_VPX_0227_MANUAL_PL_AFE7906_ADC_HD2
###### HD2 Coeff Write
Requirement ID	DP_VPX_0227_MANUAL_PL_AFE7906_HD2_01
Description	This Operation provides an option to write HD2 Coefficient Values in AFE.

###### HD2 Coeff Read
Requirement ID	DP_VPX_0227_MANUAL_PL_AFE7906_HD2_02
Description	This Operation provides an option to Read HD2 Coefficient Values from AFE.

###### ADC Dynamic Configuration
Requirement ID :
DP_VPX_0227_MANUAL_PL_AFE7906_ADC_DYNAMIC
###### Device Health Status
Requirement ID	DP_VPX_0227_MANUAL_PL_AFE7906_ADC_DYNAMIC_01
Description	This Operation shall Provide an option the Check the Device Health status

###### Update RxNco
Requirement ID	DP_VPX_0227_MANUAL_PL_AFE7906_ADC_DYNAMIC_02
Description	This Operation shall Provide an option to update the Rx NCO Frequency. / Note: 7 number of Rx channels are available to change the Nco Freqency.

###### Update FbNco
Requirement ID	DP_VPX_0227_MANUAL_PL_AFE7906_ADC_DYNAMIC_03
Description	This Operation shall Provide an option to update the Fb Nco Frequency. / Note: 2 number of Fb channels are available to change the Nco Freqency.

###### Set Rx DSA
Requirement ID	DP_VPX_0227_MANUAL_PL_AFE7906_ADC_DYNAMIC_04
Description	This Operation shall Provide an option to update the Rx DSA / Note: 7 number of Rx channels are available to change the Rx DSA.

###### Set Fb DSA
Requirement ID	DP_VPX_0227_MANUAL_PL_AFE7906_ADC_DYNAMIC_05
Description	This Operation shall Provide an option to update the Fb DSA / Note: 2 number of Fb channels are available to change the Fb DSA.

###### ADC Automation
Requirement ID :
DP_VPX_0227_MANUAL_PL_AFE7906_ADC_AUTOMATION
###### Automation Data Logging
Requirement ID	DP_VPX_0227_MANUAL_PL_AFE7906_ADC_AUTOMATION_01
Description	This operation shall provide an option to get the IQ Data From AFE chip with different frequencies at a time and plot that data in HSDC Pro.

###### Automation Phase Matching
Requirement ID	DP_VPX_0227_MANUAL_PL_AFE7906_ADC_AUTOMATION_02
Description	This operation shall Provide an option to get the phase difference of all channels at a time.

##### Digital Attenuation
Requirement ID :
DP_VPX_0227_MANUAL_PL_DIGITAL_ATTEN
Requirement ID	DP_VPX_0227_MANUAL_PL_DIGITAL_ATTEN
Description	This operation shall provide an option to write and Read Digital Attenuator Settings through SPI interface. / Note: AGC, MSTC, CAL settings are available for Attenuation Settings.

###### AGC Digital Attenuation
Requirement ID	DP_VPX_0227_MANUAL_PL_DIGITAL_ATTEN_01
Description	This operation shall provide an option to write and Read AGC attenuation value through corresponding FPGA register. / Note: Attenuation Range [0 to 31.5]

###### MSTC Digital Attenuation
Requirement ID	DP_VPX_0227_MANUAL_PL_DIGITAL_ATTEN_02
Description	This operation shall provide an option to write and Read MSTC attenuation value through corresponding FPGA register. / Note: Attenuation Range [0 to 31.5]

###### CAL Digital Attenuation
Requirement ID	DP_VPX_0227_MANUAL_PL_DIGITAL_ATTEN_03
Description	This operation shall provide an option to write and Read CAL attenuation value through corresponding FPGA register. / Note: Attenuation Range [0 to 31.5]

##### PL DDR4 Test
The following test cases shall be performed to qualify the PL DDR4 Interface. The following test cases are listed below.
Requirement ID :
DP_VPX_0227_MANUAL_PL_DDR4
###### Data Bus Test
Requirement ID	DP_VPX_0227_MANUAL_PL_DDR4_01
Description	Refer section 4.2.2.1.2.1

###### Address Bus Test
Requirement ID	DP_VPX_0227_MANUAL_PL_DDR4_02
Description	Refer section 4.2.2.1.2.2

###### Device Test
Requirement ID	DP_VPX_0227_MANUAL_PL_DDR4_03
Description	Refer section 4.2.2.1.2.3

###### Full Memory Test
Requirement ID	DP_VPX_0227_MANUAL_PL_DDR4_04
Description	This test shall be performed to determine whether each memory location of DDR4 is usable for read and write operations. Firstly, incremental counter is being written from the starting base address of the DDR4 upto its full size (8GB). / Secondly, the read operation is carried out for the full DDR4 (8GB) from the base address. If the read data is not same as written date, then the test is failed, else the test is passed. / Note : There are 8 banks in PL DDR4

##### PL NOR Flash Test
The following test cases shall be performed to qualify the NOR Flash (PL). The following test cases are listed below
Requirement ID :
DP_VPX_0227_MANUAL_PL_NORFLASH
###### Device ID Retention
Requirement ID	DP_VPX_0227_MANUAL_PL_NORFLASH_01
Description	This module shall provide an option to read the DeviceID.

###### Chip Erase
Requirement ID	DP_VPX_0227_MANUAL_PL_NORFLASH_02
Description	This module shall provide an option to erase the flash memory.

###### Sector Erase
Requirement ID	DP_VPX_0227_MANUAL_PL_NORFLASH_03
Description	This module shall provide an option to erase the user specified sector in the flash memory.

###### Single Write
Requirement ID	DP_VPX_0227_MANUAL_PL_NORFLASH_04
Description	This module shall provide option to write single Data into user specified flash offset.

###### Single Read
Requirement ID	DP_VPX_0227_MANUAL_PL_NORFLASH_05
Description	This module shall provide option to read single Data from user specified flash offset.

###### Page Write
Requirement ID	DP_VPX_0227_MANUAL_PL_NORFLASH_06
Description	Get the flash page number from the user. Write the command to perform the page write operation through the FPGA registers. If it’s failed to preform the page write operation then declare test case as FAIL otherwise PASS

###### Page Read
Requirement ID	DP_VPX_0227_MANUAL_PL_NORFLASH_07
Description	Get the flash page number from the user. Write the command to perform the page read operation through the FPGA registers. If it’s failed to preform the page read operation then declare test case as FAIL otherwise PASS.

###### Full Memory Test
Requirement ID	DP_VPX_0227_MANUAL_PL_NORFLASH_08
Description	This Module provides a provision to perform full memory test for PL NOR Flash. / Note: Before Performing full memory test make sure that Sector Erase and Die Erase should be done.

##### RGMII Test
The following test cases shall be performed to qualify the RGMII 1G Ethernet. The following test case are listed below.
Requirement ID:
DP_VPX_0227_MANUAL_PL_RGMII
###### RGMII IP Configuration
Requirement ID	DP_VPX_0227_MANUAL_PL_RGMII_01
Description	This test shall be done to configure the RGMII 1G Ethernet through a file which contains IP address for source and destination, MAC address, Subnet Mask, Gateway IP, and Port number for source and destination.

###### RGMII IP Dump
Requirement ID	DP_VPX_0227_MANUAL_PL_RGMII_02
Description	This test shall be done to read the configuration of RGMII 1G Ethernet through a file which store the IP address for source and destination, MAC address, Subnet Mask, Gateway IP, and Port number for source and destination.

###### RGMII Bandwidth Test
Requirement ID:
DP_VPX_0227_MANUAL_PL_RGMII_03
###### Bandwidth Reset
Requirement ID	DP_VPX_0227_MANUAL_PL_RGMII_03_01
Description	This test shall be used to reset the bandwidth of RGMII.

###### Bandwidth Tx
Requirement ID	DP_VPX_0227_MANUAL_PL_RGMII_03_02
Description	This test shall be used to validate the bandwidth of the RGMII 1G ethernet by calculating the speed of transmission through transmitting the data.

###### Bandwidth Rx
Requirement ID	DP_VPX_0227_MANUAL_PL_RGMII_03_03
Description	This test shall be used to validate the bandwidth of the RGMII 1G ethernet by calculating the speed of transmission through receiving of data.

##### Aurora Test Case
The following test cases shall be performed to qualify the Aurora. The following test cases are listed below.
Requirement ID :
DP_VPX_0227_MANUAL_PL_AURORA
###### Aurora Core Reset
Requirement ID	DP_VPX_0227_MANUAL_PL_AURORA_01
Description	This Operation shall provide an option to reset the Aurora core.

###### Aurora Lane Status
Requirement ID	DP_VPX_0227_MANUAL_PL_AURORA_02
Description	This Module provides a provision to check the Lane status. / Note:18 no.of channels are available to check the Lane status.

###### Aurora Bandwidth Test
Requirement ID:
DP_VPX_0227_MANUAL_PL_AURORA_03
###### Bandwidth Reset
Requirement ID	DP_VPX_0227_MANUAL_PL_AURORA_03_01
Description	Refer Section 4.2.2.2.6.3.1.

###### Bandwidth Tx
Requirement ID	DP_VPX_0227_MANUAL_PL_AURORA_03_02
Description	Refer Section 4.2.2.2.6.3.2.

###### Bandwidth Rx
Requirement ID	DP_VPX_0227_MANUAL_PL_AURORA_03_03
Description	Refer Section 4.2.2.2.6.3.3.

##### 10G Test Cases
The following test cases shall be performed to qualify the 10G Interface. The following test cases are listed below.
Requirement ID :
DP_VPX_0227_MANUAL_PL_10G
###### PL 10G IP Configuration
Requirement ID	DP_VPX_0227_MANUAL_PL_10G_01
Description	Refer Section 4.2.2.2.6.1. / Note: 6 no.of channels are available to configure.

###### PL 10G IP Dump
Requirement ID	DP_VPX_0227_MANUAL_PL_10G_02
Description	Refer Section 4.2.2.2.6.2. / Note: 6 no.of channels are available to dump the configuration.

###### PL 10G Core Reset
Requirement ID	DP_VPX_0227_MANUAL_PL_10G_03
Description	Refer Section 4.2.2.2.7.1.

###### PL 10G Core Status
Requirement ID	DP_VPX_0227_MANUAL_PL_10G_04
Description	Refer Section 4.2.2.2.7.2.

###### PL 10G BandWidth Test
Requirement ID:
DP_VPX_0227_MANUAL_PL_10G_05
###### Bandwidth Reset
Requirement ID	DP_VPX_0227_MANUAL_PL_10G_05_01
Description	Refer Section 4.2.2.2.6.3.1.

###### Bandwidth Tx
Requirement ID	DP_VPX_0227_MANUAL_PL_10G_05_02
Description	Refer Section 4.2.2.2.6.3.2.

###### Bandwidth Rx
Requirement ID	DP_VPX_0227_MANUAL_PL_10G_05_03
Description	Refer Section 4.2.2.2.6.3.3.

##### ADM(PL)Test
The following test cases shall be performed to qualify the PL ADM. The following test cases are listed below
Requirement ID :
DP_VPX_0227_MANUAL_PL_ADM
###### Voltage Monitoring Test
Requirement ID	DP_VPX_0227_MANUAL_PL_ADM_01
Description	This operation shall provide an option to read Board Voltages .

##### PL UART Test
The following test cases shall be performed to qualify the UART Interface. The following test cases are listed below.
Requirement ID :
DP_VPX_0227_MANUAL_PL_UART
###### Tx Channel Selection
Requirement ID	DP_VPX_0227_MANUAL_PL_UART_01
Description	This Operation shall provide an option to select the UART Tx channel.

###### Write Test
Requirement ID	DP_VPX_0227_MANUAL_PL_UART_02
Description	This test shall be performed to qualify the UART Write Functionality. A user entered data or a predefined data is transmitted. If the transmitted data and the data received at the host are same, declare the test case as PASS, otherwise as FAIL. / Note: Make sure that the UART is connected with the board and the internal /external system.

###### Rx channel Selection
Requirement ID	DP_VPX_0227_MANUAL_PL_UART_03
Description	This Operation shall provide an option to select UART Rx channel.

###### Read Test
Requirement ID	DP_VPX_0227_MANUAL_PL_UART_04
Description	This test shall be performed to qualify the UART Read Functionality. The data entered at the host is received. If the received data and the data transmitted from the host are same, declare the test case as PASS, otherwise as FAIL.

##### GPIO Clock Test
The following test cases shall be performed to qualify the Clock IO interface. The following test cases are listed below.
Requirement ID:
DP_VPX_0227_MANUAL_PL_GPIO_CLOCK
###### IO Test
Requirement ID	DP_VPX_0227_MANUAL_PL_GPIO_CLOCK_01
Description	This test shall be performed to qualify the Clock IO's by emitting the frequency through FPGA. If the emitting process done then PASS otherwise FAIL. / Note : There are 4 IN pins and 1 OUT pin

##### LVDS IO Test
The following test cases shall be performed to qualify the LVDS Interface. The following test cases are listed below.
Requirement ID:
DP_VPX_0227_MANUAL_PL_LVDS_IO
###### IO Loop Back Test
Requirement ID	DP_VPX_0227_MANUAL_PL_LVDS_IO_1
Description	This test shall be performed to qualify the LVDS IO's data loop back shall be done to validate the working of the LVDS IO's. If the read value and written values are same then this test is declared as PASS otherwise FAIL / Note : There are 4 IN pins and 4 OUT pins

###### Clock Test
Requirement ID	DP_VPX_0227_MANUAL_PL_LVDS_IO_2
Description	This test shall be performed to qualify the LVDS Clock by pulse generation. If the pulse generation process done then PASS otherwise FAIL. / Note : There are 4 IN pins and 4 OUT pins

##### TTL IO Test
The following test cases shall be performed to qualify the TTL Interface. The following test cases are listed below.
Requirement ID:
DP_VPX_0227_MANUAL_PL_TTL_IO
###### IO Loop Back Test
Requirement ID	DP_VPX_0227_MANUAL_PL_TTL_IO_1
Description	This test shall be performed to qualify the TTL IO's by make the OUT pins as high and low. If the process done then PASS otherwise FAIL. / Note : There are 12 OUT pins

###### Clock Test
Requirement ID	DP_VPX_0227_MANUAL_PL_TTL_IO_2
Description	This test shall be performed to qualify the TTL Clock by emitting the frequency through FPGA. If the emitting process done then PASS otherwise FAIL. declared as PASS otherwise FAIL. / Note : There are 12 OUT pins

##### Junction Temperature Test
The following test cases shall be performed to qualify the FPGA Junction Temperature. The following test cases are listed below.
Requirement ID:
DP_VPX_0227_MANUAL_PL_JUNC_TEMP
###### Junction Temperature Read
Requirement ID	DP_VPX_0227_MANUAL_PL_JUNC_TEMP_1
Description	This test shall be performed to read the FPGA Junction temperature value. If the read process done then PASS otherwise FAIL.

##### PCIe Test
The following test cases shall be performed to qualify the PCIe. The following test cases are listed below.
Requirement ID:
DP_VPX_0227_MANUAL_PL_PCIe
###### PCIe Write
Requirement ID	DP_VPX_0227_MANUAL_PL_PCIe_1
Description	This module shall provide option to write single Data into user specified pcie offset. If the write process done then PASS otherwise FAIL.

###### PCIe Read
Requirement ID	DP_VPX_0227_MANUAL_PL_PCIe_2
Description	This module shall provide option to read single Data into user specified pcie offset. If the read process done then PASS otherwise FAIL.

###### PCIe Full Memory Test
Requirement ID	DP_VPX_0227_MANUAL_PL_PCIe_3
Description	This test shall be performed to compare the write and read data are same in all possible address of PCIe up to the total size. If the verification process done then PASS otherwise FAIL. / Note: Total size of PCIe is 8192 bytes.

### Auto Mode Test Cases
In auto mode test shall be performed auto mode test cases that are enable by user configure by ATP hardware to qualify in the board. The following inputs are allow the user to select the test to perform, number of cycles to perform, delay between each cycle and delay between each tests.
Requirement ID :
DP_VPX_0227_AUTO
#### Processor Test
Refer the section 4.2.2.1.1
#### DDR4 Test
Refer the section 4.2.2.1.2
#### EEPROM Test
Refer the section 4.2.2.1.3
#### MRAM Test
Refer the section 4.2.2.1.4
#### NOR Flash Test
Refer the section 4.2.2.1.5
#### NAND Flash Test
Refer the section 4.2.2.1.6
#### UART Test
Refer the section 4.2.2.1.9
#### Ethernet Test
Refer the section 4.2.2.1.10
#### Temperature Sensor Test
Refer the section 4.2.2.1.12
# Software System Attributes
## Performance Requirements
The Ethernet data transfer rate shall be minimum of 100mbps.
## Safety Requirements
NA
## Security Requirements
NA
## Software Quality Attributes
NA
## Business Rules
NA

# Other Requirements
NA

# Requirements Traceability
Requirement ID in SRS	Section / Requirement ID in HRS Document
DP_VPX_0227_MANUAL_PS_PRCS	DP-VPX-0227-HRS-002
DP_VPX_0227_MANUAL_PS_DDR4	DP-VPX-0227-HRS-0010
DP_VPX_0227_MANUAL_PS_EEPROM	DP-VPX-0227-HRS-0013
DP_VPX_0227_MANUAL_PS_MRAM	DP-VPX-0227-HRS-0014
DP_VPX_0227_MANUAL_PS_NANDFLASH	DP-VPX-0227-HRS-0011
DP_VPX_0227_MANUAL_PS_NORFLASH	DP-VPX-0227-HRS-0012
DP_VPX_0227_MANUAL_PS_USB	DP-VPX-0227-HRS-0015
DP_VPX_0227_MANUAL_PS_SATA	DP-VPX-0227-HRS-0015
DP_VPX_0227_MANUAL_PS_UART	DP-VPX-0227-HRS-009
DP_VPX_0227_MANUAL_PS_ETH	DP-VPX-0227-HRS-009
DP_VPX_0227_MANUAL_PS_RTC	DP-VPX-0227-HRS-006
DP_VPX_0227_MANUAL_PS_TEMPSNSR	DP-VPX-0227-HRS-0017
DP_VPX_0227_MANUAL_PL_LMK04828 PLL	DP-VPX-0227-HRS-007
DP_VPX_0227_MANUAL_PL_AFE7906_ADC	DP-VPX-0227-HRS-003
DP_VPX_0227_MANUAL_PL_DIGITAL_ATTEN	DP-VPX-0227-HRS-003
DP_VPX_0227_MANUAL_PL_DDR4	DP-VPX-0227-HRS-0010
DP_VPX_0227_MANUAL_PL_NORFLASH	DP-VPX-0227-HRS-0012
DP_VPX_0227_MANUAL_PL_RGMII	DP-VPX-0227-HRS-0015
DP_VPX_0227_MANUAL_PL_AURORA	DP-VPX-0227-HRS-0016
DP_VPX_0227_MANUAL_PL_10G	DP-VPX-0227-HRS-0016
DP_VPX_0227_MANUAL_PL_UART	DP-VPX-0227-HRS-009
DP_VPX_0227_MANUAL_PL_ADM	DP-VPX-0227-HRS-002
DP_VPX_0227_MANUAL_PL_GPIO_CLOCK	DP-VPX-0227-HRS-0019
DP_VPX_0227_MANUAL_PL_LVDS_IO	DP-VPX-0227-HRS-004
DP_VPX_0227_MANUAL_PL_TTL_IO	DP-VPX-0227-HRS-0019
DP_VPX_0227_MANUAL_PL_PCIe	DP-VPX-0227-HRS-0019