SOFTWARE REQUIREMENT SPECIFICATIONS
FOR
3U VPX Zynq MPSoC with 6 Channels 14-bit 0.02 to 2GHZ I/P 3GSPS AFE7906 based Digital Receiver Module DP-VPX-0233

DOCUMENT TITLE	SOFTWARE REQUIREMENT SPECIFICATIONS FOR 3U VPX Zynq MPSoC with 6 Channels 14-bit 0.02 to 2GHZ I/P 3GSPS AFE7906 based Digital Receiver Module
DOCUMENT REFERENCE	DP-VPX-0233-V1-01-SRS-0V08
VERSION NUMBER	0.08
VERSION DATE	February 13, 2026
PREPARED BY	Name: Magima V M / Sign:
DOCUMENT REVIEW BY	Name: Gowthami V / Sign:
TECHNICAL REVIEW BY	Name: Kingshuk Mitra / Sign:
PROCESS REVIEW BY	Name: Gowthami V / Sign:
APPROVED BY	Name: / Sign:

Copyright @ (2025) by Data Patterns
All right reserved. These materials are proprietary to Data Patterns and no part of these materials should be reproduced, published in any form by any means, electronic or mechanical including photocopy or any information storage or retrieval system nor should the materials be disclosed to third parties without the written authorization of Data Patterns.

Revision History

S. NO.	VER. NO.	VER. DATE	CHANGED BY	SECTION (S) CHANGED	DESCRIPTION / OF CHANGE
1	0V01	January 21 ,2025	Magima V M	-	Initial Version
2	0V02	February 3 ,2025	Magima V M	Section 4 , 4.3.2.2.11 , 4.2.2.2 , 4.3.2.2.9 , 2.2 , 3.2	Internal Comments closed with DP-VPX-0233-SDG-SRR-0V02
3	0V03	March 24 ,2025	Magima V M	Section 2.5 , ,4.2.2.1 , 4.2.2.2	Internal Comments closed with DP-VPX-0233-SDG-SRR-0V03
4	0V04	April 8 ,2025	Magima V M	Section 4.2.2.2.2, 4.2.2.2.1, 4.2.2.2.2.9	Internal Comments closed with DP-VPX-0233-SDG-SRR-0V04
5	0V05	May 2, 2025	Gowthami V	Section 4.2.2.1.12 4.2.2.2.7 , 4.2.2.2.8 , 4.2.2.2.5	DRB Comments closed with DP-VPX-0233-SDG-SRR-0V05
6	0V06	July 9,2025	Magima V M	Section 4.2.2.2.1.6 , 4.2.2.2.4.7 , 4.2.2.2.7.4	QC Comments closed with DP-VPX-0233-SDG-SRR-0V06
7	0V07	December 15, 2025	Gowthami V, / Magima V M	Section 4	DRB Comments for TPR Documents closed with DP-VPX-0233-SDG-SRR-0V07
8	0V08	February 13, 2026	Magima V M	Section 4.1.2.2.2.2.11	New Requirement closed with DP-VPX-0233-SDG-SRR-0V08

# Introduction
This Software Requirement Specification document describes the requirements involved in the design and development of the test application software for DP-VPX-0233, that is used to qualify the hardware requirements.
## Purpose
The purpose of this document is to provide the software requirements for the development of software for DP-VPX-0233.It aids the designer to test & qualify the hardware through the test software.
The intended audience for this SRS is Design Review Board (DRB). The expected users of this document are the internal QAC (Quality Assurance and Control) department, HDD (Hardware Design and Development) department and SDG (Software Design Group) department. The various entities involved in the design and development of this SRS are listed in the below table.

## Scope
The scope of this document describes the aspects related to functional and performance tests of DP-VPX-0233 module through Linux ATP. The identification details are provided below:

Table 1: Entities Involved in ATP Development
Identification Number	DP-VPX-0233-000-V1-01-SRS-0V08
Title	SOFTWARE REQUIREMENT SPECIFICATIONS FOR 3U VPX Zynq MPSoC with 6 Channels 14-bit 0.02 to 2GHZ I/P 3GSPS AFE7906 based Digital Receiver Module DP-VPX-0233
Version Number	0.08
Abbreviation	SRS

## Definitions, Acronyms, and Abbreviations
The acronyms and abbreviations used in this document are listed in the below Table 2.

Table 2 : List of Acronyms and Abbreviations

ATP	Acceptance Test Plan
UART	Universal Asynchronous Receiver Transmitter
DDR	Double Data Rate
PCI	Peripheral Component Interconnect
SRS	Software Requirement Specification
HRS	Hardware Requirement Specification
RTC	Real Time Clock
MRAM	Magneto-resistive Random Access Memory
GPIO	General Purpose Input Output
USB	Universal Synchronous Bus
SATA	Serial Advanced Technology Attachment
RAM	Random Access Memory
EEPROM	Electrically Erasable Programmable Read-Only Memory
JTAG	Joint Test Action Group
ADC	Analog to Digital Converter
DAC	Digital to Analog Converter
SPI	Serial Peripheral Interface
PLL	Phase Locked Loop
RF	Radio Frequency
IF	Intermediate Frequency
NCO	Numerically Controlled Oscillator Frequency
DSA	Digital Step Attenuator

## References
The following list of documents were referred for deriving this requirements specification

Table 3 : Reference Documents
S. No	Document Name	Document Reference

1	Hardware Requirement Specification - DP-VPX-0233	DP-VPX-0233-000-HRS-0V03
2	Software Requirement Specification - DP-VPX-0206	DP-VPX-0206-V1-01-SRS-1V00
3	Software Requirement Specification - DP-VPX-0227	DP-VPX-0227-V1-01-SRS-0V03
4	Common Software Requirement Specification	DP-COMMON-SDG-SRS(ATP-ATE)-0V05-DRAFT

## Document Overview

Section 1: Introduction
Describes about the introduction of this document such as purpose, scope, and document overview. It also lists the acronyms and referenced documents.

Section 2: Overall Description
This section provides overall description covering the product perspective, product functions, user characteristics, operating environment, design and implementation constraints, user documentation and assumptions & dependencies.
Section 3: External Interface Requirements
This section describes the details of user interfaces, hardware interfaces, software interfaces and communication interfaces.
Section 4: Functional Requirements
This section lists out the details of functional requirements.
Section 5: Software System Attributes
This section specifies performance requirements, safety requirements, security requirements, software quality attributes and business rules.
Section 6: Other Requirements
This section describes other requirements.
Section 7: Requirements Traceability
This section lists out the requirement traceability matrix.

# Overall Description
## Product Perspective
DP-VPX-0233 shall be a 3U VPX high end latest technology digital receiver Module compliant with VITA 46 standard. This module shall have Zynq Ultrascale Plus reprogrammable (MPSoC) hardware in combination with Dual / Quad core Arm Processor signal processing.

The Processing section (PS) operates with Dual / Quad Arm core which performs the system management functionality of receiver. This Section shall have on board 8GB 64 Bit DDR4 dynamic memories and two QSPI NOR flash for boot configuration. It shall have an EEPROM memory of 4Kb via I2C interface to store the DDR4 memory configuration details. Through XMC connector, It shall have an eMMC NAND flash for application and user storage and MRAM for general storage pupose. It offers a x1 PCIe gen2 link, One x1 SATA interfaces, One x1 SATA/USB 3.0 interface (backward compatible to USB 2.0) and One SGMII Interface. It shall have two RS232/ RS422 UART port for debugging purpose.

The Programmable Logics(PL) Section shall have x8 16.375 Gbps JESD204B receiver Core for AFE7906 based RFADC, One x8 transceiver for JESD204B core for RFDAC, IFADC and IFDAC through XMC Connector and x4 10G Ethernet core in optional basis. This section shall have SPI interface Logic for RFADC, PLL and RFDAC, IFADC and IFDAC of Piggy Module for register Configuration. It shall have two RS232 UART port for communication purpose.

This module shall handle six number of 20MHz – 2GHz input RF signals with 3GSPS sampling rate and also shall have a XMC Connector to connect 5 channel 1MHz-30MHz input 105MSPS IFADC piggy module or single channel 20MHz to 6GHz Output 12.6GSPS DAC Piggy Module. This module shall have low noise on board clock generation and distribution section to provide jitter free Sampling Clock to RFADC, FPGA JESD Cores and Piggy Modules. This section shall also have a option of choosing internal and external reference clock.

On board Power Generator & Sequencing section shall be used for generation of all the power supplies in the module from +5V & +3.3V. This module shall have VPX P0 Connector for Power Supply, VPX P1 & P2 Connector all communication links and debugging interfaces and 62 no of Field IOs. This module shall have a temperature sensor for monitoring the FPGA temperature.
The module shall be of conduction cooled type with Ruggedizer and wedge lock arrangement and comply 1” slot width dimensions.

 The main features of DP-VPX-0233 module is given below:

- Zynq Ultra-scale Plus MPSoC from Xilinx
- One 72 Bit 8GB DDR4 Memory from PS & 2GB 16 Bit DDR4 Memory from PL
- AFE7906 based 14 bit 3GSPS ADC with 12 channels and JESD204B digital Interface.
- Primary XMC for Five channel 16 Bit 105MSPS IFADC channels or Single 16 Bit 12.6GSPS DAC channel Piggy Module with JESD204B Interface.
- Secondary XMC Connector for eMMC NAND flash, MRAM memory interfaces and Ethernet 1000 Base-T and USB connectivity interfaces.
- 1 x4 PCIe interface
- 1 x1 PCIe/SATA interface
- 1 x1 USB 3.0 interface (USB 2.0 Backward Compatible)
- 1 x 1G 1000 Base-X SGMII interface
- 1 x 1G Base-T RGMII interface
- 2 x RS422 interface or 2xRS232, 1x RS422.
- 1 x4 RIO to support 10G Ethernet
- 48 Single-Ended IO (LVTTL/LVCMOS) & 12 Differential IO
- 1 no of 5V logic Output & 1 no of 5V Logic input
- On board clock generator section with Internal & External Reference
- On board Power supply generator & sequencer
The main applications of DP-VPX-0233 module is given below:

- V/U/SHF Search Receiver
- Digital Receiver for both RF & IF signals.
- Data Communications.
- Signal Processing.

### Block Diagram

Figure 1: Block diagram of DP_VPX_0233
## Software Perspective
1. This shall be a standalone ATP Software whose main purpose is to qualify the functionality of the devices available on DP-VPX-0233 Processor board.
2. The Software shall run at the DP-VPX-0233 Processor board.
## Product Functions
DP-VPX-0233 is an 3U VPX high end latest technology digital receiver Module compliant with VITA 46 standard. This module shall have Zynq Ultrascale Plus reprogrammable (MPSoC) hardware in combination with Dual / Quad core Arm Processor signal processing.

DP-VPX-0233 software requirements are categorized into 2 major requirements based on the MPSOC’s
- Processing Section
- Programmable Logic
## User Classes and Characteristics
The different users of DP-VPX-0233 test application area Data patterns – SDG, HDD,
production, QA team. The users are expected to test the product functionality of module.
## Operating Environment
The operating environment details of the software are given in the below table.
Table 4: Target Software Environment

S. No	Software	Description
1	Operating system	Linux 5.4
2	Architecture	AARCH64
3	Cross Compiler	aarch64-xilinx-linux-gcc
4	Build Tool	Petalinux 2020.2
5	Programming Language	C
6	GUI	Qt5.14.2

## Design and Implementation Constraints
COM1 / ttyPS0 of DP-VPX-0233 target board is used as the debug port and will not be tested separately as part of application software. It will be considered as working, if the boot up messages displayed on the console during board booting.
## User Documentation
The Following Documents should be prepared and submitted for DP_VPX_0233

       1. Software Requirement Specifications(SRS)
       2. Software Design Document(SDD)
## Assumptions and Dependencies
NA

# External Interface Requirements
## User Interfaces
The following main menu shall be displayed according to the selection.

--------------------------------------------------------------------------------------------------
        DPVPX0233 – Board Selection
--------------------------------------------------------------------------------------------------
        1. DP-VPX-0233
2. DP-SPL-1255
3. DP-SPL-1276
99. Exit the Application
        --------------------------------------------------------------------------------------------------
Enter Your Choice [ 1 - 3 ] :

After selecting the board, the following main menu shall be displayed according to the selection.

-------------------------------------------------------------------------------------------------
        MAIN MENU
        --------------------------------------------------------------------------------------------------
        1. Manual Mode Test
2. Auto Mode Test
3. About
        99. Exit
        --------------------------------------------------------------------------------------------------
Enter the option :

The console shall be cleared after getting input from user and the selected test case options will be displayed from the beginning of the console.

## Hardware Interfaces
Table 5 : Hardware Interfaces
S. No	Hardware Interfaces	Description
	RS232 or RS422 Serial Port	UART Serial port used for debugging and as the interface between the host and target.
	Ethernet	Ethernet is used to transfer data between host and the target.
	DDR4	One 64 Bit + 8bit ECC 8GB DDR4 Controller from PS Section. / One 16 Bit 2GB DDR4 Controller from PL Section.
	MRAM	4Mb MRAM via SPI Interface is used for critical storage during power off.
	NAND FLASH (User Flash)	16GB NAND Flash is used as the user flash for storage device.
	NOR FLASH (Boot Flash)	2 x 64MB Quad SPI NOR Flash is used as the boot flash.
	EEPROM	4Kb DDR4 SPD EEPROM is used to store the DDR4 configuration details.
	RTC	Real Time Clock is used to update the current time and date.
	Temperature Sensor	Temperature sensor is used to monitor the processor temperature.
	USB	USB memory stick is used for USB testing.
	SATA	SATA device (SATA DOM) is used for SATA testing.
	Programmable Logic	Programmable logic is used to configure AFE7906 ADC and LMK PLL based on the board configuration.

## Software Interfaces
Table 6 : software interfaces
S. No	Software	Requirement Description
1.	Windows	Putty
2.	Linux	Minicom

## Communications Interfaces
UART
- Serial cable (RS232 or RS422) is required to connect the Target to the serial port of the Host PC for target console.
- The DP-VPX-0233 Consists of 4No’s of RS232 ports and 2No’s of RS422 ports.
Table 7: UART Communication Interface
S. No	Configuration	Range
1	Baud rate	RS232- 115200 / RS422- 115200
2	Parity	None
3	Stop Bits	1
4	Number of bits	8

Ethernet
Ethernet is required to connect the target to the LAN. It is used to transfer data between the target board and the host machine. It is also used for target console via ssh.

# Functional Requirements
Table 8: Functional Requirement Test
Requirement Identification Number	Requirement Description	Reference Requirement ID
PROCESSING SECTION
DP_VPX_0233_MANUAL_PS_PRCS	Processor Test	DP_VPX_0206_PROCS_03_01_01
DP_VPX_0233_MANUAL_PS_DDR4	DDR4 Test	DP_VPX_0206_DDR4_03_01_02
DP_VPX_0233_MANUAL_PS_EEPROM	EEPROM Test	DP_VPX_0206_EEPROM_03_01_03
DP_VPX_0233_MANUAL_PS_MRAM	MRAM Test	DP_VPX_0206_MRAM_03_01_04
DP_VPX_0233_MANUAL_PS_NAND	NAND Flash Test	DP_VPX_0206_NANDFLASH_03_01_05
DP_VPX_0233_MANUAL_PS_NOR	NOR Flash Test	DP_VPX_0206_NORFLASH_03_01_06
DP_VPX_0233_MANUAL_PS_USB	USB Test	DP_VPX_0206_USB_03_01_07
DP_VPX_0233_MANUAL_PS_SATA	SATA Test	DP_VPX_0206_SATA_03_01_08
DP_VPX_0233_MANUAL_PS_UART	UART Test	DP_VPX_0206_UART_03_01_09
DP_VPX_0233_MANUAL_PS_ETH	Ethernet Test	DP_VPX_0206_ETH_03_01_10
DP_VPX_0233_MANUAL_PS_RTC	RTC Test	DP_VPX_0206_RTC_03_01_11
DP_VPX_0233_MANUAL_PS_TEMPSNSR	Temperature Sensor Test	DP_VPX_0206_TEMPSNSR_03_01_13
DP_VPX_0233_MANUAL_PS_ADM	Voltage Monitoring Test	DP_VPX_0206_ADM_03_01_14
DP_VPX_0233_MANUAL_PS_PCI	PCI Enumeration Test	DP_VPX_0206_PCI_03_01_12
PROGRAMMABLE LOGIC
DP_VPX_0233_MANUAL_PL_LMK_PLL	LMK PLL Test	DP_VPX_0227_MANUAL_PL_LMK04828_PLL
DP_VPX_0233_MANUAL_PL_AFE7906_ADC	AFE7906 ADC Test	DP_VPX_0227_MANUAL_PL_AFE7906_ADC
DP_VPX_0233_MANUAL_PL_DDR4	DDR4 (PL) Test	DP_VPX_0206_PL_DDR4_03_02_12
DP_VPX_0233_MANUAL_PL_RFDAC	RFDAC Test	DP_VPX_0206_RFDAC_03_02_04
DP_VPX_0233_MANUAL_PL_10GETHERNET	10G Ethernet Test	DP_VPX_0206_10GETHERNET_03_02_07
DP_VPX_0233_MANUAL_PL_UART	PL UART Test	DP_VPX_0206_UART_03_02_08
DP_VPX_0233_MANUAL_PL_LVTTL	LVTTL Test	DP_VPX_0206_LVTTL_03_02_09
DP_VPX_0233_MANUAL_PL_LVDS	LVDS Test	DP_VPX_0206_LVDS_03_02_10
DP_VPX_0233_MANUAL_PL_GPI_GPO	GPI and GPO Test	DP_VPX_0206_GPI_GPO_03_02_11

## DPVPX0233 Module
### Test Configuration
Test configuration shall enable the user to configure each of the Auto/manual mode test cases. If the configuration file is already available (in a predefined path) then it shall be be read and stored in an appropriate data structures. If configuration file is unavailable (in a predefined path) then the following test cases shall be perform.
#### Auto Mode Test Selection
This shall configure the Auto Mode test cases by getting the input from user to Enable/Disable the state of all the available test cases in Auto mode.
#### Manual Mode Test Selection
This shall configures the Manual Mode test cases by getting the input from user to Enable/Disable the state of all the available test cases in Manual mode.
#### Test Specific Details
This is to provide the configuration details specific to the enabled test cases in either or both of the auto and manual mode test case options.
### Test Performance
#### Auto Mode Test Performance
The auto mode test performance shall perform the auto mode test cases that are enabled using the target configuration for qualifying the board. The selection of the auto mode test depends on the user (Refer 4.1 for Test Configuration). The following are the inputs for performing auto mode test :

- ENTER THE NO OF CYCLE [1-200]:
- ITERATION GAP (in Seconds) [1s - 10s]:
- INTER-ITERATION GAP (in Seconds) [1s – 10s]:

The user shall need to enter input first. The enabled auto mode test cases will then be performed for the specified number of cycles. The summary of the auto mode test results will be displayed as a consolidated report once the test process is over. The Test process shall be paused at any time (using Ctrl+C) to see the status report and can be continued further or stopped to get back to the main menu. A consolidated report shows the status of the auto mode Test cases that are executed shall be displayed in the console and the report shall be stored in a file.
#### Manual Mode Test Performance
The manual mode test performance shall perform the manual mode test cases that are enabled using the target configuration for qualifying the board. The selection of the manual mode test depends on the user (Refer 4.1 for Test Configuration).

The following are the details regarding the test cases included in manual mode Test Performance.

##### Processing Section

Requirement ID :
DP_VPX_0233_MANUAL_PS
###### Processor Test
The following test cases shall be performed to qualify the processor ALU and FPU test cases. The following test cases are listed below.
Requirement ID :
DP_VPX_0233_MANUAL_PS_PRCS
###### ALU Test
Requirement ID	DP_VPX_0233_MANUAL_PS_PRCS_01
Description	This test shall be performed to qualify the processor (ALU). The following tests are to be carried out. / 1. Arithmetic operation Test (Addition, Subtraction, Division and Multiplication) / 2. Shift operation Test (Left shift and Right shift) / 3. Logical operation Test (AND, OR and NOT)

###### FPU Test
Requirement ID	DP_VPX_0233_MANUAL_PS_PRCS_02
Description	This test shall be performed to qualify the processor (FPU). The following tests are to be carried out. / 1. Floating point Arithmetic Test (Floating point Addition, Subtraction, Multiplication and Division).

###### DDR4 Test
The following test cases shall be performed to qualify the DDR4. The following test cases are listed below

Requirement ID :
DP_VPX_0233_MANUAL_PS_DDR4
###### Data Bus Test
Requirement ID	DP_VPX_0233_MANUAL_PS_DDR4_01
Description	This test shall be performed to qualify the data bus lines in the memory device. The Walking 1's and Walking 0's test shall be carried out. Perform memory walking ones test by left shifting the data, 1 bit at a time until it reaches the 32nd bit. Perform memory walking zero tests by left shifting the complement of data , 1 bit at a time until it reaches the 32nd bit. If both test cases are success, then the test shall be considered as PASS, otherwise FAIL.

###### Address Bus Test
Requirement ID	DP_VPX_0233_MANUAL_PS_DDR4_02
Description	This test shall be performed to qualify the address bus lines in the memory device. A base address shall be written with known Pattern and rest of the addresses are written with Anti pattern. Read the data from all these locations. If the read value and written value are not same, then return error else the base address shall be written with anti pattern and rest of the addresses are written with pattern. Read the data from all these locations. If the read value and written value are same, then test shall be considered as PASS, otherwise FAIL

###### Device Test
Requirement ID	DP_VPX_0233_MANUAL_PS_DDR4_03
Description	This test shall be performed to determine whether every bit in the device is capable of holding both 0 and 1. Write the incremental counter 32-bit data (0x00 00 00 00 , 0x00 00 00 01, 0x00 00 00 02,......,n) in the allocated memory of particular size (RAM size). Start reading the data from starting memory location and check for previously written data if both are not same then return error, else write inverted data to same location. Repeat this sequence for next memory location until maximum size (RAM size) is reached. Start reading the data from first memory location and check for previously written inverted data. If both are not same then return error else repeat this sequence for next memory location until maximum size (RAM size) is reached. If the written values and read back values are same, then test shall be considered as PASS, otherwise FAIL.

###### EEPROM Test
The following test cases shall be performed to qualify the EEPROM. The following test cases are listed below

Requirement ID :
DP_VPX_0233_MANUAL_PS_EEPROM
###### Upload Board Information
Requirement ID	DP_VPX_0233_MANUAL_PS_EEPROM_01
Description	This test shall be performed to validate the proper initialization of flash device. The device shall be initialized and a predefined data shall be loaded and read back to ensure proper initialization of the device. If both values are same, then test shall be declared as PASS, otherwise FAIL. / Note: Information shall be loaded only once for each board.

###### Data Retention Test
Requirement ID	DP_VPX_0233_MANUAL_PS_EEPROM_02
Description	This test shall be performed to qualify the authenticity of the memory device. A read operation shall be performed to get the Data stored in the memory. If the read data is the expected value, then test shall be declared PASS, otherwise FAIL.

###### Checksum Test
Requirement ID	DP_VPX_0233_MANUAL_PS_EEPROM_03
Description	This test shall performed to check the data integrity in the memory device. The data in the memory device shall be read from a fixed area/locations and checksum shall be computed. The computed checksum shall be compared against the pre-loaded/known checksum value.

###### Write / Read Test
Requirement ID	DP_VPX_0233_MANUAL_PS_EEPROM_04
Description	This test shall be performed by getting offset address and data from the user as an input and write the input data in the input address and read the data from the user given input address, If both write and read data are same then shall be considered as PASS else FAIL.

###### MRAM Test
The following test cases shall be performed to qualify the MRAM. The following test cases are listed below.
Requirement ID :
DP_VPX_0233_MANUAL_PS_MRAM
###### Upload Board Information
Requirement ID	DP_VPX_0233_MANUAL_PS_MRAM_01
Description	Refer the Section 4.1.2.2.1.3.1

###### Data Retention Test
Requirement ID	DP_VPX_0233_MANUAL_PS_MRAM_02
Description	Refer the Section 4.1.2.2.1.3.2

###### Checksum Test
Requirement ID	DP_VPX_0233_MANUAL_PS_MRAM_03
Description	Refer the Section 4.1.2.2.1.3.3

###### Full Memory Test
Requirement ID	DP_VPX_0233_MANUAL_PS_MRAM_04
Description	This test shall be conducted to validate the Read and Write operation in the MRAM. All memory locations shall be written with counter and inverted counter data and same shall be read back. Verify read and write values,if both are same, then test shall be declared as PASS, otherwise FAIL.

###### NOR Flash Test
The following test cases shall be performed to qualify the NOR Flash. The following test cases are listed below
Requirement ID :
DP_VPX_0233_MANUAL_PS_NORFLASH
###### Upload Board Information
Requirement ID	DP_VPX_0233_MANUAL_PS_NORFLASH_01
Description	Refer the Section 4.1.2.2.1.3.1

###### Data Retention Test
Requirement ID	DP_VPX_0233_MANUAL_PS_NORFLASH_02
Description	Refer the Section 4.1.2.2.1.3.2

###### Checksum Test
Requirement ID	DP_VPX_0233_MANUAL_PS_NORFLASH_03
Description	Refer the Section 4.1.2.2.1.3.3

###### NAND Flash Test
The following test cases shall be performed to qualify the NAND Flash. The following test cases are listed below
Requirement ID :
DP_VPX_0233_MANUAL_PS_NANDFLASH
###### Upload Board Information
Requirement ID	DP_VPX_0233_MANUAL_PS_NANDFLASH_01
Description	Refer the Section 4.1.2.2.1.3.1

###### Data Retention Test
Requirement ID	DP_VPX_0233_MANUAL_PS_NANDFLASH_02
Description	Refer the Section 4.1.2.2.1.3.2

###### Checksum Test
Requirement ID	DP_VPX_0233_MANUAL_PS_NANDFLASH_03
Description	Refer the Section 4.1.2.2.1.3.3

###### USB Test
The following test cases shall be performed to qualify the USB. The following test cases are listed below

Requirement ID :
DP_VPX_0233_MANUAL_PS_USB
###### Read/Write Test

Requirement ID	DP_VPX_0233_MANUAL_PS_USB_01
Description	This will mount the USB memory stick partition in the mount directory & shall create a file in the USB device and by performing the read/write operations on that file. If both written data and read data are same then test shall be declared as PASS, otherwise FAIL. / Note: Make sure that the USB device is connected with the board and formatted as linux Partition.

###### SATA Test
The following test cases shall be performed to qualify the SATA. The following test cases are listed below
Requirement ID :
DP_VPX_0233_MANUAL_PS_SATA
###### Read/Write Test

Requirement ID	DP_VPX_0233_MANUAL_PS_SATA_01
Description	This test shall mount the SATA device in the specified mount point and will create and write sample data in a file in the mounted partition. This test shall read the file content from the device and compare with the written file. If both written and read data is same, it will return success, otherwise failure. / Note: Make sure that the SATA device is connected with the board and formatted as linux Partition.

###### UART Test
The test cases shall be performed to qualify the UART. The following test cases are listed below
Requirement ID :
DP_VPX_0233_MANUAL_PS_UART

###### Write Test
Requirement ID	DP_VPX_0233_MANUAL_PS_UART_01
Description	This test shall be performed to qualify the UART Write Functionality. A user entered data or a predefined data is transmitted. If the transmitted data and the data received at the host are same, declare the test case as PASS, otherwise as FAIL.

###### Read Test
Requirement ID	DP_VPX_0233_MANUAL_PS_UART_02
Description	This test shall be performed to qualify the UART Read Functionality. The data entered at the host is received. If the received data and the data transmitted from the host are same, declare the test case as PASS, otherwise as FAIL.

###### Ethernet Test
The following test cases shall be performed to qualify the Ethernet. The following test cases are listed below

Requirement ID :
DP_VPX_0233_MANUAL_PS_ETH
###### Ethernet Ping Test
Requirement ID	DP_VPX_0233_MANUAL_PS_ETH_01
Description	This test shall be performed between 2 ports of different systems considering that both ports are connected with LAN cable. This shall be carried out by sending & receiving data through ping command to/from Target port IP address. If ping test is passed, declare the test case as PASS, otherwise as FAIL. / Note: Pre-loaded data will be transferred by Operating System as part of Ethernet Ping test

###### RTC Test
The following test cases shall be performed to qualify the RTC. The following test cases are listed below

Requirement ID :
DP_VPX_0233_MANUAL_PS_RTC
###### RTC Test

Requirement ID	DP_VPX_0233_MANUAL_PS_RTC_01
Description	The RTC parameters are configured with the user selected values and reading it after a predefined gap (EX. 8 secs). If the read time is updated with an addition of predefined gap then the test is considered as pass, else fail. / Note: The test result with tolerance of +/-1 second in addition to the expected seconds will be accepted.

###### Temperature Sensor Test

The following test cases shall be performed to qualify the Temperature Sensor. The following test cases are listed below

Requirement ID :
DP_VPX_0233_MANUAL_PS_TEMPSNSR
###### Temperature Sensor Test

Requirement ID	DP_VPX_0233_MANUAL_PS_TEMPSNSR_01
Description	This test shall be carried out by reading the Temperature Sensor value and checking whether the read value is within the low limit and high limit of Local temperature which is configured by the user. If the Temperature values are within the limits then the test case is declared as PASS, otherwise as FAIL. / Note: Temperature Sensor Limits are listed below. / Local Temperature ( -10 to 70) / External Temperature(-10 to 70)

###### Voltage Monitoring Test

The following test cases shall be performed to qualify the ADM. The following test cases are listed below

Requirement ID :
DP_VPX_0233_MANUAL_PS_ADM
###### Voltage Monitoring Test
Requirement ID	DP_VPX_0233_MANUAL_PS_ADM_01
Description	The Voltage limits will be provided in a file ("dpvpx0233_adm_limits.txt"). This file will be read in-order to compare the read voltages. This test shall be carried out by reading the ADM input channel voltages from the processor and verify the read value with expected voltage from the file. Also, read and display power good status. / Note : Application will load the predefined values from the ADM Limit file.

###### PCI Enumeration Test
The following test cases shall be performed to qualify the PCI Enumeration. The following test cases are listed below

Requirement ID :
DP_VPX_0233_MANUAL_PS_PCI
###### PCI Enumeration Test

Requirement ID	DP_VPX_0233_MANUAL_PS_PCI_01
Description	This test shall enumerate the PCI devices with Device ID and Vendor ID and compare the user expected PCI devices with the enumerated devices. / The test result will depend on the outcome of comparison of the enumerated and the expected PCI device.

##### Programmable Logic

Requirement ID :
DP_VPX_0233_MANUAL_PL

###### LMK PLL Test
The following test cases shall be performed to qualify the LMK PLL Interface. The following test cases are listed below.
Requirement ID :
DP_VPX_0233_MANUAL_PL_LMK_PLL
###### File Configuration
Requirement ID	DP_VPX_0233_MANUAL_PL_LMK_PLL_01
Description	This operation shall provide an option to configure PLL. This can be done through Reading and writing the Data in particular offset through SPI Interface. / Note: PLL_CONFIG.txt file will be used to configure the PLL.

###### File Dump
Requirement ID	DP_VPX_0233_MANUAL_PL_LMK_PLL_02
Description	This operation shall provide an option to Read the Data from PLL through SPI Interface.

###### Single Write
Requirement ID	DP_VPX_0233_MANUAL_PL_LMK_PLL_03
Description	This test shall provide an option to write single Data through SPI Interface.

###### Single Read
Requirement ID	DP_VPX_0233_MANUAL_PL_LMK_PLL_04
Description	This test shall provide an option to Read Back single data through SPI Interface.

###### PLL Lock Status
Requirement ID	DP_VPX_0233_MANUAL_PL_LMK_PLL_05
Description	This operation shall be performed to verify the Lock status of the LMK PLL.

###### Sysref Enable/Disable
###### Enable
Requirement ID	DP_VPX_0233_MANUAL_PL_LMK_PLL_06_01
Description	This operation provides an option to Enable Sysref.

###### Disable
Requirement ID	DP_VPX_0233_MANUAL_PL_LMK_PLL_06_02
Description	This operation provides an option to Disable Sysref.

###### AFE7906 ADC Test Cases
The following test cases shall be performed to qualify the AFE7906 ADC Interface. The following test cases are listed below.

Requirement ID :
DP_VPX_0233_MANUAL_PL_AFE7906_ADC
###### AFE Core Reset

Requirement ID	DP_VPX_0233_MANUAL_PL_AFE7906_ADC_01
Description	This operation provides an option to Reset the AFE chip. / Note: AFE chip is available for Resetting.

###### AFE Single Write

Requirement ID	DP_VPX_0233_MANUAL_PL_AFE7906_ADC_02
Description	This operation provides an option to perform the single write operation in AFE chip.

###### AFE Single Read

Requirement ID	DP_VPX_0233_MANUAL_PL_AFE7906_ADC_03
Description	This operation provides an option to perform the single read operation in AFE chip.

###### AFE Bring-up

Requirement ID	DP_VPX_0233_MANUAL_PL_AFE7906_ADC_04
Description	This operation shall be performed to configure the AFE7906 ADC. This can be done by loading Text file which was followed by Reset and Core Initialization. / Note: A separate utility Latte Software used to generate the Text file for AFE chip [AFE having 4 Rx and 2 Fb channels].

###### AFE Core Initialization
Requirement ID	DP_VPX_0233_MANUAL_PL_AFE7906_ADC_05
Description	This operation provides an option to check the Core Initialization for AFE Chip. / Note: AFE chip is available for Resetting.

###### JESD Bond Status
Requirement ID	DP_VPX_0233_MANUAL_PL_AFE7906_ADC_06
Description	This Operation shall be performed to synchronize the JESD and FPGA. It can be verified by reading the BOND STATUS REGISTER.

###### Data Logging
Requirement ID	DP_VPX_0233_MANUAL_PL_AFE7906_ADC_07
Description	This operation shall be performed to get the IQ Data From AFE chip. / Note: Data Plotting is done by a separate tool – HSDC Pro, 6 number of channels are available to get the IQ Data.

###### HD2 Correction Enable
The following test cases shall be performed to qualify the HD2 Correction enable. The following test cases are listed below.

Requirement ID :
DP_VPX_0233_MANUAL_PL_AFE7906_ADC_HD2
###### HD2 Coeff Write

Requirement ID	DP_VPX_0233_MANUAL_PL_AFE7906_ADC_HD2_08_01
Description	This Operation provides an option to write HD2 Coefficient Values in AFE.

###### HD2 Coeff Read

Requirement ID	DP_VPX_0233_MANUAL_PL_AFE7906_ADC_HD2_08_02
Description	This Operation provides an option to Read HD2 Coefficient Values from AFE.

###### ADC Dynamic Configuration

The following test cases shall be performed to qualify the ADC Dynamic configuration. The following test cases are listed below.

Requirement ID :
DP_VPX_0233_MANUAL_PL_AFE7906_ADC_DYNAMIC

###### Device Health Status

Requirement ID	DP_VPX_0233_MANUAL_PL_AFE7906_ADC_DYNAMIC_09_01
Description	This Operation shall Provide an option the Check the Device Health status

###### Update RxNco

Requirement ID	DP_VPX_0233_MANUAL_PL_AFE7906_ADC_DYNAMIC_09_02
Description	This Operation shall Provide an option to update the Rx NCO Frequency. / Note: 4 number of Rx channels are available to change the Nco Freqency.

###### Update FbNco

Requirement ID	DP_VPX_0233_MANUAL_PL_AFE7906_ADC_DYNAMIC_09_03
Description	This Operation shall Provide an option to update the Fb Nco Frequency. / Note: 2 number of Fb channels are available to change the Nco Freqency.

###### Set Rx DSA

Requirement ID	DP_VPX_0233_MANUAL_PL_AFE7906_ADC_DYNAMIC_09_04
Description	This Operation shall Provide an option to update the Rx DSA. / Note: 4 number of Rx channels are available to change the Rx DSA.

###### Set Fb DSA

Requirement ID	DP_VPX_0233_MANUAL_PL_AFE7906_ADC_DYNAMIC_09_05
Description	This Operation shall Provide an option to update the Fb DSA. / Note: 2 number of Fb channels are available to change the Fb DSA.

###### Read Rx Nco

Requirement ID	DP_VPX_0233_MANUAL_PL_AFE7906_ADC_DYNAMIC_09_06
Description	This Operation shall Provide an option to read the Rx Nco data. / Note: 4 number of Rx channels are available to read the Rx Nco data.

###### Read Fb Nco

Requirement ID	DP_VPX_0233_MANUAL_PL_AFE7906_ADC_DYNAMIC_09_07
Description	This Operation shall Provide an option to read the Fb Nco data. / Note: 2 number of Fb channels are available to read the Fb Nco data.

###### NCO Update
The following test cases shall be performed to qualify the NCO Update. The following test cases are listed below.

Requirement ID :
DP_VPX_0233_MANUAL_PL_AFE7906_NCO_UPDATE
###### All Channel Enable

Requirement ID	DP_VPX_0233_MANUAL_PL_AFE7906_NCO_UPDATE_10_01
Description	This Operation shall Provide an option to enable all the NCO channel to High.

###### Single Channel Enable

Requirement ID	DP_VPX_0233_MANUAL_PL_AFE7906_NCO_UPDATE_10_02
Description	This Operation shall Provide an option to enable single channel based on the channel number entered by the user.

###### All Channel Disable

Requirement ID	DP_VPX_0233_MANUAL_PL_AFE7906_NCO_UPDATE_10_03
Description	This Operation shall Provide an option to disable all the NCO pins to Low.

###### Single Channel Disable

Requirement ID	DP_VPX_0233_MANUAL_PL_AFE7906_NCO_UPDATE_10_04
Description	This Operation shall Provide an option to disable single channel based on the channel number entered by the user.

###### Band Selection
Requirement ID	DP_VPX_0233_MANUAL_PL_AFE7906_BAND_SEL_11
Description	This Operation shall provide an option to select the Band(Wide Band/ Narrow Band).

###### ADC Automation
The following test cases shall be performed to qualify the ADC Automation. The following test cases are listed below.

Requirement ID :
DP_VPX_0233_MANUAL_PL_AFE7906_ADC_AUTOMATION
###### Automation Data Logging

Requirement ID	DP_VPX_0233_MANUAL_PL_AFE7906_ADC_AUTOMATION_12_01
Description	This operation shall provide an option to get the IQ Data From AFE chip with different frequencies at a time and plot that data in HSDC Pro.

###### Automation Phase Matching

Requirement ID	DP_VPX_0233_MANUAL_PL_AFE7906_ADC_AUTOMATION_12_02
Description	This operation shall Provide an option to get the phase difference of all channels at a time.

###### PL DDR4 Test
The following test cases shall be performed to qualify the PL DDR4 Interface. The following test cases are listed below.

Requirement ID :
DP_VPX_0233_MANUAL_PL_DDR4

###### DDR4 Reset

Requirement ID	DP_VPX_0233_MANUAL_PL_DDR4_01
Description	This operation shall be performed to reset DDR4 control register.

###### Data Bus Test
Requirement ID	DP_VPX_0233_MANUAL_PL_DDR4_02
Description	Refer the Section 4.1.2.2.1.2.1

###### Address Bus Test
Requirement ID	DP_VPX_0233_MANUAL_PL_DDR4_03
Description	Refer the Section 4.1.2.2.1.2.2

###### Device Test
Requirement ID	DP_VPX_0233_MANUAL_PL_DDR4_04
Description	Refer the Section 4.1.2.2.1.2.3

###### Full Memory Test
Requirement ID	DP_VPX_0233_MANUAL_PL_DDR4_05
Description	This test shall be performed to determine whether each memory location of DDR4 is usable for read and write operations. Firstly, incremental counter is being written from the starting base address of the DDR4 upto its full size (8GB). / Secondly, the read operation is carried out for the full DDR4 (8GB) from the base address. If the read data is not same as written date, then the test is failed, else the test is passed.

###### 10G Ethernet Test

- This test shall be carried out to qualify the 10G Ethernet functionality and the RIO Lanes.
- This shall includes configuration of both the RIO Logic and Lane repeaters.

Requirement ID :
DP_VPX_0233_MANUAL_PL_10GETHERNET
###### Lane Repeater Configuration

Requirement ID	DP_VPX_0233_MANUAL_PL_10GETHERNET_01
Description	This operation shall be performed to write the data to I2C for Lane repeater configuration / Note:4 channels are available for 10G Configuration.

###### Core Reset

Requirement ID	DP_VPX_0233_MANUAL_PL_10GETHERNET_02
Description	This operation shall be performed to reset IP core

###### Ethernet Reset

Requirement ID	DP_VPX_0233_MANUAL_PL_10GETHERNET_03
Description	This operation shall be performed to reset Ethernet.

###### Network Configuration

Requirement ID	DP_VPX_0233_MANUAL_PL_10GETHERNET_04
Description	This operation shall be performed to Configure Network parameters MAC and IP address

###### Transmit Data

Requirement ID	DP_VPX_0233_MANUAL_PL_10GETHERNET_05
Description	This operation shall be performed to transmit data in packet format to host.

###### Receiver Packet summary

Requirement ID	DP_VPX_0233_MANUAL_PL_10GETHERNET_06
Description	This operation shall be performed to receive packets from host and to check the bandwidth

###### PL UART Test
The test shall be carried out to qualify the UART module in the PL section of the DP-VPX-0233.

Requirement ID :
DP_VPX_0233_MANUAL_PL_UART
###### Read

Requirement ID	DP_VPX_0233_MANUAL_PL_UART_01
Description	Refer the Section 4.1.2.2.1.9.2

###### Write
Requirement ID	DP_VPX_0233_MANUAL_PL_UART_02
Description	Refer the Section 4.1.2.2.1.9.1

###### LVTTL Test

The following tests shall be carried out to qualify the LVTTL interface.

Requirement ID :
DP_VPX_0233_MANUAL_PL_LVTTL
###### IO Mode Test

Requirement ID	DP_VPX_0233_MANUAL_PL_LVTTL_01
Description	This test shall be performed to qualify the LVTTL IO's. Waking 1's and 0's shall be done to validate the working of the LVTTL IO's. If the read value and written values are same then this test is declared as PASS otherwise FAIL. / Note: 4 sets are available to test the LVTTL Test cases.

###### Clock Mode Test

Requirement ID	DP_VPX_0233_MANUAL_PL_LVTTL_02
Description	This test shall be performed to qualify the LVTTL IO's. Clock pulse shall be sent to calculate the ON and OFF time of the IOs to validate the working of the LVTTL IO's. Frequency calculated from the ON time and OFF time of the IO is same as the frequency given as input then the test is declared as PASS otherwise FAIL. / Note: A Clock Frequency of 1MHz will be sent in each IO lines

###### Manual IO Mode Test

Requirement ID	DP_VPX_0233_MANUAL_PL_LVTTL_03
Description	This test shall be performed to qualify the LVTTL IO's Manually. Manual validation shall be done by writing either ONE of ZERO to individual IO’s and read back. if the values are same then the test is declared as PASS otherwise FAIL.

###### Manual Clock Mode Test

Requirement ID	DP_VPX_0233_MANUAL_PL_LVTTL_04
Description	This test shall be performed to qualify the LVTTL Clock Manually. This test case provides provision to turn ON and OFF the LVTLL clock manually.

###### LVDS Test

The following tests shall be carried out to qualify the LVDS interface.

Requirement ID :
DP_VPX_0233_MANUAL_PL_LVDS
###### IO Mode Test

Requirement ID	DP_VPX_0233_MANUAL_PL_LVDS_01
Description	This test shall be performed to qualify the LVDS IO's. Walking 1's and 0's shall be done to validate the working of the LVDS IO's. If the read value and written values are same then this test is declared as PASS otherwise FAIL. / Note: 3 sets are available to test LVDS Test cases.

###### Clock Mode Test

Requirement ID	DP_VPX_0233_MANUAL_PL_LVDS_02
Description	This test shall be performed to qualify the LVDS IO's. Clock pulse shall be sent to calculate the ON and OFF time of the IOs to validate the working of the LVDS IO's. Frequency calculated from the ON time and OFF time of the IO is same as the frequency given as input then the test is declared as PASS otherwise FAIL. / Note: A Clock Frequency of 1MHz will be sent in each IO lines

###### Manual Mode Test
Requirement ID	DP_VPX_0233_MANUAL_PL_LVDS_03
Description	This test shall be performed to qualify the LVDS IO's Manually. Manual validation shall be done by writing either ONE of ZERO to individual IO’s and read back. if the values are same then the test is declared as PASS otherwise FAIL.

###### GPI and GPO Test
The following tests shall be carried out to qualify the GPO interface.

Requirement ID :
DP_VPX_0233_MANUAL_PL_GPI_GPO
###### IO Mode Test

Requirement ID	DP_VPX_0233_MANUAL_PL_GPI_GPO_01
Description	This test shall be performed to qualify the GPI GPO IO's. Clock pulse shall be sent to calculate the ON and OFF time of the IOs to validate the working of the GPI GPO IO's. Frequency calculated from the ON time and OFF time of the IO is same as the frequency given as input then the test is declared as PASS otherwise FAIL. / Note: A Clock Frequency of 1MHz will be sent in each IO lines.

###### FPGA Junction Temperature Test
The following test cases shall be performed to qualify the FPGA Junction Temperature.

Requirement ID	DP_VPX_0233_MANUAL_PL_JUNC_TEMP
Description	This module provides the provision to read the FPGA Junction temperature from the device.

#### Auto Mode Test Cases
In auto mode test shall be performed auto mode test cases that are enable by user configure by ATP hardware to qualify in the board. The following inputs are allow the user to select the test to perform, number of cycles to perform, delay between each cycle and delay between each tests.
Requirement ID :
DP_VPX_0233_AUTO
##### Processor Test
Refer the section 4.2.2.1.1
##### DDR4 Test
Refer the section 4.2.2.1.2
##### EEPROM Test
Refer the section 4.2.2.1.3
##### MRAM Test
Refer the section 4.2.2.1.4
##### NOR Flash Test
Refer the section 4.2.2.1.5
##### NAND Flash Test
Refer the section 4.2.2.1.6
##### Ethernet Test
Refer the section 4.2.2.1.10
##### RTC Test
Refer the section 4.1.2.2.1.11
##### Temperature Sensor Test
Refer the section 4.2.2.1.12
##### Voltage Monitoring Test
Refer the section 4.2.2.1.13
## DPSPL1255 Module
### Manual Mode Test Performance
#### Programmable Logic

Requirement ID :
DP_VPX_0233_MANUAL_PL
##### LMK PLL Test

The following test cases shall be performed to qualify the LMK PLL Interface. The following test cases are listed below.
Requirement ID :
DP_VPX_0233_MANUAL_PL_LMK_PLL
###### File Configuration
Requirement ID	DP_VPX_0233_MANUAL_PL_LMK_PLL_01
Description	Refer the Section 4.1.2.2.2.1.1

###### File Dump
Requirement ID	DP_VPX_0233_MANUAL_PL_LMK_PLL_02
Description	Refer the Section 4.1.2.2.2.1.2

###### Single Write
Requirement ID	DP_VPX_0233_MANUAL_PL_LMK_PLL_03
Description	Refer the Section 4.1.2.2.2.1.3

###### Single Read
Requirement ID	DP_VPX_0233_MANUAL_PL_LMK_PLL_04
Description	Refer the Section 4.1.2.2.2.1.4

###### PLL Lock Status
Requirement ID	DP_VPX_0233_MANUAL_PL_LMK_PLL_05
Description	Refer the Section 4.1.2.2.2.1.5

##### RFDAC Test
The following test cases shall be performed to qualify the PL RFDAC interface. The following test cases are listed below.

Requirement ID :
DP_VPX_0233_MANUAL_PL_RFDAC
###### File Write
Requirement ID	DP_VPX_0233_MANUAL_PL_RFDAC_01
Description	This operation shall be performed to configure the RFDAC. This can be carried out by reading a configuration file and writing the RFDAC registers through SPI Interface.

###### File Read
Requirement ID	DP_VPX_0233_MANUAL_PL_RFDAC_02
Description	This operation shall be performed to read the RFDAC register data. This can be carried out by reading the RFDAC registers and printing it in a Log File.

###### Single Data Write

Requirement ID	DP_VPX_0233_MANUAL_PL_RFDAC_03
Description	This test shall be performed to qualify the Write operation of the RFDAC by writing a single register through SPI Interface.

###### Single Data Read
Requirement ID	DP_VPX_0233_MANUAL_PL_RFDAC_04
Description	This test shall be performed to qualify the Read operation of the RFDAC by Reading a single register through SPI interface.

###### Power Level Transmission
Requirement ID	DP_VPX_0233_MANUAL_PL_RFDAC_05
Description	This operation provides an option to Power on the Module.

###### RFDAC Data Transmission
Requirement ID	DP_VPX_0233_MANUAL_PL_RFDAC_06
Description	This operation shall be performed to qualify the DAC Data transmission. / Note: RFDAC Synchronize should be done before RFDAC Data Transmission.

###### RFDAC Reset

Requirement ID	DP_VPX_0233_MANUAL_PL_RFDAC_07
Description	This operation provides an option to reset RFDAC.

## DPSPL1276 Module
### Manual Mode Test Performance
#### Programmable Logic

Requirement ID :
DP_VPX_0233_MANUAL_PL
##### LMK PLL Test

The following test cases shall be performed to qualify the LMK PLL Interface. The following test cases are listed below.
Requirement ID :
DP_VPX_0233_MANUAL_PL_LMK_PLL
###### File Configuration
Requirement ID	DP_VPX_0233_MANUAL_PL_LMK_PLL_01
Description	Refer the Section 4.1.2.2.2.1.1

###### File Dump
Requirement ID	DP_VPX_0233_MANUAL_PL_LMK_PLL_02
Description	Refer the Section 4.1.2.2.2.1.2

###### Single Write
Requirement ID	DP_VPX_0233_MANUAL_PL_LMK_PLL_03
Description	Refer the Section 4.1.2.2.2.1.3

###### Single Read
Requirement ID	DP_VPX_0233_MANUAL_PL_LMK_PLL_04
Description	Refer the Section 4.1.2.2.2.1.4

###### PLL Lock Status
Requirement ID	DP_VPX_0233_MANUAL_PL_LMK_PLL_05
Description	Refer the Section 4.1.2.2.2.1.5

##### RFDAC Test
The following test cases shall be performed to qualify the PL RFDAC interface. The following test cases are listed below.

Requirement ID :
DP_VPX_0233_MANUAL_PL_RFDAC
###### File Write

Requirement ID	DP_VPX_0233_MANUAL_PL_RFDAC_01
Description	Refer the Section 4.2.1.1.2.1

###### File Read

Requirement ID	DP_VPX_0233_MANUAL_PL_RFDAC_02
Description	Refer the Section 4.2.1.1.2.2

###### Single Data Write

Requirement ID	DP_VPX_0233_MANUAL_PL_RFDAC_03
Description	Refer the Section 4.2.1.1.2.3

###### Single Data Read

Requirement ID	DP_VPX_0233_MANUAL_PL_RFDAC_04
Description	Refer the Section 4.2.1.1.2.4

###### Power Level Transmission

Requirement ID	DP_VPX_0233_MANUAL_PL_RFDAC_05
Description	Refer the Section 4.2.1.1.2.5

###### RFDAC Data Transmission

Requirement ID	DP_VPX_0233_MANUAL_PL_RFDAC_06
Description	Refer the Section 4.2.1.1.2.6

###### RFDAC Reset

Requirement ID	DP_VPX_0233_MANUAL_PL_RFDAC_07
Description	Refer the Section 4.2.1.1.2.7

# Software System Attributes
The other non-functional requirements, including the performance, safety and security requirements are described in this section.
## Performance Requirements
1. Instruments/Modules shall be brought to the default setting while quitting the application or after completing the test.
2. Test operation shall be carried out only if all the modules are detected.
## Safety Requirements
1. Instruments/Modules shall be brought to the default setting while quitting the application or after completing the test.
2. Functional operations shall be restricted when any of the hardware module is not detected.
3. Warning / Error messages shall be printed from the application to indicate the user about the failures / uncompounded actions.
## Security Requirements
1. The application will be protected from the anonymous users. The software will be provided with a log in feature, which will be password activated. Only developer and other users will be able to access the application.
2. The test setup shall be disconnected from public network to avoid unauthorized access to the board.
## Software Quality Attributes
The software shall be maintained by using the version details of application
  - The software shall be designed to run on the following platforms : Microsoft Windows, Linux.
  - Before Installing the setup, for instruments communication, NI Max, NI VISA, HSDC Pro and SIGGEN Driver shall be installed.
  - The software shall be maintained with version details and program checksum.
# Requirements Traceability

Requirement ID in SRS	Section / Requirement ID in HRS Document
DP_VPX_0233_MANUAL_PS_PRCS	DP-VPX-0233-HRS-002
DP_VPX_0233_MANUAL_PS_DDR4	DP-VPX-0233-HRS-0010
DP_VPX_0233_MANUAL_PS_EEPROM	DP-VPX-0233-HRS-0014
DP_VPX_0233_MANUAL_PS_MRAM	DP-VPX-0233-HRS-0013
DP_VPX_0233_MANUAL_PS_NORFLASH	DP-VPX-0233-HRS-0011
DP_VPX_0233_MANUAL_PS_NANDFLASH	DP-VPX-0233-HRS-0012
DP_VPX_0233_MANUAL_PS_USB	,DP-VPX-0233-HRS-0018
DP_VPX_0233_MANUAL_PS_SATA	DP-VPX-0233-HRS-0015
DP_VPX_0233_MANUAL_PS_UART	DP-VPX-0233-HRS-0017
DP_VPX_0233_MANUAL_PS_ETH	DP-VPX-0233-HRS-0015
DP_VPX_0233_MANUAL_PS_RTC	DP-VPX-0233-HRS-007
DP_VPX_0233_MANUAL_PS_TEMPSNSR	DP-VPX-0233-HRS-0021
DP_VPX_0233_MANUAL_PS_ADM	DP-VPX-0233-HRS-0024
DP_VPX_0233_MANUAL_PS_PCI	DP-VPX-0233-HRS-0015
DP_VPX_0233_MANUAL_PL_LMK_PLL	DP-VPX-0233-HRS-008
DP_VPX_0233_MANUAL_PL_AFE7906_ADC	DP-VPX-0233-HRS-003
DP_VPX_0233_MANUAL_PL_DDR4	DP-VPX-0233-HRS-0010
DP_VPX_0233_MANUAL_PL_RFDAC	DP-VPX-0233-HRS-004
DP_VPX_0233_MANUAL_PL_10GETHERNET	DP-VPX-0233-HRS-0018
DP_VPX_0233_MANUAL_PL_UART	DP-VPX-0233-HRS-0017
DP_VPX_0233_MANUAL_PL_LVTTL	DP-VPX-0233-HRS-006
DP_VPX_0233_MANUAL_PL_LVDS	DP-VPX-0233-HRS-006
DP_VPX_0233_MANUAL_PL_GPI_GPO	DP-VPX-0233-HRS-006
DP_VPX_0233_MANUAL_PL_JUNC_TEMP	DP-VPX-0233-HRS-0021