SOFTWARE REQUIREMENT SPECIFICATIONS
FOR
3U VPX SOSA Zynq Ultrascale+ MPSoC based 6 Channel 14-Bit 0.02 to 3GHZ I/P Digital Receiver Module
DP-VPX-0236

DOCUMENT TITLE	SOFTWARE REQUIREMENT SPECIFICATIONS FOR 3U VPX SOSA Zynq Ultrascale+ MPSoC based 6 Channel 14-Bit 0.02 to 3GHZ I/P Digital Receiver Module
DOCUMENT REFERENCE	DP-VPX-0236-V1-01-SRS-0V04
VERSION NUMBER	0.04
VERSION DATE	March 19 , 2026
PREPARED BY	Name: Magima V M / Sign:
DOCUMENT REVIEW BY	Name: Gowthami V / Sign:
TECHNICAL REVIEW BY	Name: Kingshuk Mitra / Sign:
PROCESS REVIEW BY	Name: Gowthami V / Sign:
APPROVED BY	Name: / Sign:

Copyright by Data Patterns
All right reserved. These materials are proprietary to Data Patterns and no part of these materials should be reproduced, published in any form by any means, electronic or mechanical including photocopy or any information storage or retrieval system nor should the materials be disclosed to third parties without the written authorization of Data Patterns.

Revision History
S. NO.	VER. NO.	VER. DATE	CHANGED BY	SECTION (S) CHANGED	DESCRIPTION / OF CHANGE
1	0V01	June 25 ,2025	Magima V M	-	Initial Version
2	0V02	September 03 ,2025	Magima V M	Section 4.2.2.2.3 , 4.2.2.2.4.3 , 4.2.2.2.9	Internal Comments closed with DP-VPX-0236-SDG-SRR-0V02
3	0V03	December 18 , 2025	Magima V M	Section 4.2.2.2.2.10 , 4.2.3.7 , 1.3	Internal Comments closed with DP-VPX-0236-SDG-SRR-0V03
4	0V04	March 19 , 2026	Magima V M	Section 4 , 4.2.2.1.11.1, 4.2.2.2.10, 4.2.2.2.4, 4.2.2.2.5	DRB Comments closed with DP-VPX-0236-SDG-SRR-0V04

# Introduction
This Software Requirement Specification document describes the requirements involved in the design and development of the test application software for DP-VPX-0236, that is used to qualify the hardware requirements.
## Purpose
The purpose of this document is to provide the software requirements for the development of software for DP-VPX-0236. It aids the designer to test & qualify the hardware through the test software.
The intended audience for this SRS is Design Review Board (DRB). The expected users of this document are the internal QAC (Quality Assurance and Control) department, HDD (Hardware Design and Development) department and SDG (Software Design Group) department. The various entities involved in the design and development of this SRS are listed in the below table.
## Scope
The scope of this document describes the aspects related to functional and performance tests of DP-VPX-0236 module through Linux ATP. The identification details are provided below:

Table 1: Entities Involved in ATP Development
Identification Number	DP-VPX-0236-V1-01-SRS-0V04
Title	SOFTWARE REQUIREMENT SPECIFICATIONS FOR 3U VPX SOSA Zynq Ultrascale+ MPSoC based 6 Channel 14-Bit 0.02 to 3GHZ I/P Digital Receiver Module DP-VPX-0236
Version Number	0.04
Abbreviation	SRS

## Definitions, Acronyms, and Abbreviations
The acronyms and abbreviations used in this document are listed in the below Table 2.

Table 2 : List of Acronyms and Abbreviations

ATP	Acceptance Test Plan
UART	Universal Asynchronous Receiver Transmitter
DDR	Double Data Rate
PCI	Peripheral Component Interconnect
SRS	Software Requirement Specification
HRS	Hardware Requirement Specification
RTC	Real Time Clock
MRAM	Magneto-resistive Random Access Memory
USB	Universal Synchronous Bus
SATA	Serial Advanced Technology Attachment
RAM	Random Access Memory
EEPROM	Electrically Erasable Programmable Read-Only Memory
JTAG	Joint Test Action Group
ADC	Analog to Digital Converter
SPI	Serial Peripheral Interface
PLL	Phase Locked Loop
RF	Radio Frequency
SOSA	Sensor Open System Architecture

## References
Table 3 : Reference Documents
S. No	Document Name	Document Reference

1	Hardware Requirement Specification - DP-VPX-0236	DP-VPX-0236-000-HRS-0V06
2	Software Requirement Specification - DP-VPX-0233	DP-VPX-0233-V1-01-SRS-1V00
3	Software Requirement Specification - DP-VPX-0227	DP-VPX-0227-V1-01-SRS-1V00
4	Common Software Requirement Specification	DP-COMMON-SDG-SRS(AsTP-ATE)-0V05-DRAFT

## Document Overview
Section 1: Introduction
Describes about the introduction of this document such as purpose, scope, and document overview. It also lists the acronyms and referenced documents.

Section 2: Overall Description
This section provides overall description covering the product perspective, product functions, user characteristics, operating environment, design and implementation constraints, user documentation and assumptions & dependencies.
Section 3: External Interface Requirements
This section describes the details of user interfaces, hardware interfaces, software interfaces and communication interfaces.
Section 4: Functional Requirements
This section lists out the details of functional requirements.
Section 5: Software System Attributes
This section specifies performance requirements, safety requirements, security requirements, software quality attributes and business rules.
Section 6: Other Requirements
This section describes other requirements.
Section 7: Requirements Traceability
This section lists out the requirement traceability matrix.

# Overall Description
## Product Perspective
DP-VPX-0236 shall be a 3U VPX digital receiver Module compliant with VITA 67.2 standard. This module shall have Zynq Ultrascale Plus reprogrammable (MPSoC) Dual / Quad core Arm Processor signal processing hardware in combination with AFE based RF Receiver.

The Processing section (PS) operates with Dual / Quad Arm core which performs the system management functionality of receiver. This Section shall have on board 4GB 32-bit DDR4 dynamic memories and dual QSPI NOR flash for boot configuration. It shall have an EEPROM memory of 4Kb via I2C interface to store the DDR4 memory configuration details. an eMMC NAND flash of 16GB for application and user storage and a 4MB MRAM for storing critical information.It shall provide 1000Base-T Ethernet for Communication and 2x RS422 (or) 2x RS232 UART port for debugging purpose. It offers a x1 PCIe gen2 link, two x1 SATA interfaces and One SGMII Interface. It shall have two RS232/ RS422 UART port for debugging purpose.

The Programmable Logics(PL) Section shall have x8 25 Gbps JESD204B receiver Core for AFE ADC and x4 10G Link to Field for transmitting the IQ data and x4 10G lanes for optical communication through piggy module. This Section shall have on board 4GB 32-bit DDR4 dynamic memories for easing IQ data logics. It provides SPI interface Logic for RFADC and PLL . It shall have two RS232 UART port for communication purpose.It also provides 95Nos of control IO’s to DDC module.

This module shall have 5Nos of 2.2GHz +/-300MHz ADC Input path with 3GSPS sampling rate. This module shall have low noise on board clock generation and distribution section to provide jitter free Sampling Clock to RFADC and FPGA JESD Cores. This section shall also have a option of choosing internal and external reference clock.

On board Power Generator & Sequencing section shall be used for generation of all the power supplies in the module from +12V,+5V & +3.3V. This module shall have VPX P0 Connector for Power Supply, VPX P1 for all communication links and debugging interfaces and VITA 67.2 RF connector for receiving x1LO, x1 Clock references,x1 Monitoring port of LO and x5 ADC inputs. It also has an XMC connector for DDC module interface with 95 nos of Control Io’s and Power supply of +12V . This module shall have a temperature sensor for monitoring the FPGA temperature. The module shall be of conduction cooled type with Ruggedizer and wedge lock arrangement.

  - Features
 The main features of DP-VPX-0236 module is given below:

- Zynq Ultra-scale Plus MPSoC from Xilinx
- 32Bit 4GB DDR4 Memory from PS & 32Bit 4GB DDR4 Memory from PL
- x5 14-bit 2.2GHz ADC input Channels with 3GSPS Sampling based on AFE7906 with JESD204B/C digital Interface.
- 16GB eMMC NAND flash for User storage and 64MB dual parallel QSPI for boot file storage.
- 512KB MRAM & 4Kb EEPROM memory interfaces for critical data storage.
- x1 1000 Base-T and x1 SGMII Ethernet Interface for communication.
- 2 x RS422 interface or 2xRS232, 1x RS422 for debugging.
- x4 10G interface to Filed for transmitting IQ Data and x4 10G lanes for Optical communication.
- x1 PCIe interface , x2 Sata interface from PS
- x95 TTL/LVTTL Control IO’s for DDC Module.
- On board clock generator section with Internal & External Reference
- On board Power supply generator & sequencer
  - Applications
The main applications of DP-VPX-0236 module is given below:

- V/U/SHF Search Receiver
- Digital Receiver for both RF & IF signals.
- Data Communications.
- Signal Processing.

### Block Diagram

Figure 1: Block diagram of DP_VPX_0236

## Product Functions
DP-VPX-0236 shall be a 3U VPX digital receiver Module compliant with VITA 67.2 standard. This module shall have Zynq Ultrascale Plus reprogrammable (MPSoC) Dual / Quad core Arm Processor signal processing hardware in combination with AFE based RF Receiver.

DP-VPX-0236 software requirements are categorized into 2 major requirements based on the MPSOC’s
- Processing Section
- Programmable Logic
## User Classes and Characteristics
The different users of DP-VPX-0236 test application area Data patterns – SDG, HDD,
production, QA team. The users are expected to test the product functionality of module.
## Operating Environment
The operating environment details of the software are given in the below table.
Table 4: Target Software Environment

S. No	Software	Description
1	Operating system	Linux 5.4
2	Architecture	AARCH64
3	Cross Compiler	aarch64-xilinx-linux-gcc
4	Build Tool	Petalinux 2021.2
5	Programming Language	C
6	GUI	Qt5.14.2

## Design and Implementation Constraints
COM1 / ttyPS0 of DP-VPX-0236 target board is used as the debug port and will not be tested separately as part of application software. It will be considered as working, if the boot up messages displayed on the console during board booting.

## User Documentation
The Following Documents should be prepared and submitted for DP_VPX_0236

       1. Software Requirement Specifications(SRS)
       2. Software Design Document(SDD)
## Assumptions and Dependencies
NA

# External Interface Requirements
## User Interfaces
The following main menu shall be displayed,

-------------------------------------------------------------------------------------------------
        MAIN MENU
        --------------------------------------------------------------------------------------------------
        1. Manual Mode Test
2. Auto Mode Test
3. About
        99. Exit
        --------------------------------------------------------------------------------------------------
Enter the option :

The console shall be cleared after getting input from user and the selected test case options will be displayed from the beginning of the console.

## Hardware Interfaces
Table 5 : Hardware Interfaces
S. No	Hardware Interfaces	Description
	RS232 or RS422 Serial Port	UART Serial port used for debugging and as the interface between the host and target.
	Ethernet	Ethernet is used to transfer data between host and the target.
	DDR4	One 32 Bit 8GB DDR4 Controller from PS Section with operating upto 2400MT/S. / One 32 Bit 8GB DDR4 Controller from PL Section with operating upto 2400MT/S.
	MRAM	4Mb MRAM via SPI Interface is used for critical storage during power off.
	NAND FLASH (User Flash)	16GB eMMC NAND Flash (8 bit) is used as the user flash for storage device.
	NOR FLASH (Boot Flash)	2 x 64MB Quad SPI NOR Flash is used as the boot flash.
	EEPROM	4Kb DDR4 SPD EEPROM is used to store the DDR4 configuration details.
	RTC	Real Time Clock is used to update the current time and date.
	Temperature Sensor	Temperature sensor is used to monitor the processor temperature.
	SATA	SATA device (SATA DOM) is used for SATA testing.
	Programmable Logic	Programmable logic is used to configure AFE7906 ADC and LMK PLL based on the board configuration.

## Software Interfaces
Table 6 : software interfaces
S. No	Software	Requirement Description
1.	Windows	Putty
2.	Linux	Minicom

## Communications Interfaces

UART
Serial cable (RS232 or RS422) is required to connect the Target to the serial port of the Host PC for target console.
The DP-VPX-0236 Consists of 4No’s of RS232 ports and 2No’s of RS422 ports.

Table 7: UART Communication Interface
S. No	Configuration	Range
1	Baud rate	RS232- 115200 / RS422- 115200
2	Parity	None
3	Stop Bits	1
4	Number of bits	8

Ethernet
Ethernet is required to connect the target to the LAN. It is used to transfer data between the target board and the host machine. It is also used for target console via ssh.

# Functional Requirements
Table 8: Functional Requirement Test
Requirement Identification Number	Requirement Description	Reference Requirement ID
PROCESSING SECTION
DP_VPX_0236_MANUAL_PS_PRCS	Processor Test	DP_SDG_COM_PERI_04_PROCS_01
DP_VPX_0236_MANUAL_PS_DDR4	DDR4 Test	DP_SDG_COM_MEM_01_DDR_07
DP_VPX_0236_MANUAL_PS_EEPROM	EEPROM Test	DP_SDG_COM_MEM_01_EEPROM_02
DP_VPX_0236_MANUAL_PS_MRAM	MRAM Test	DP_VPX_0206_MRAM_03_01_04
DP_VPX_0236_MANUAL_PS_NAND	NAND Flash Test	DP_SDG_COM_MEM_01_FLASH_04
DP_VPX_0236_MANUAL_PS_NOR	NOR Flash Test	DP_VPX_0206_NORFLASH_03_01_06
DP_VPX_0236_MANUAL_PS_SATA	SATA Test	DP_SDG_COM_MEM_01_SATA_06
DP_VPX_0236_MANUAL_PS_UART	UART Test	DP_SDG_COM_COMM_02_RS422RS232/RS485_01
DP_VPX_0236_MANUAL_PS_ETH	Ethernet Test	DP_SDG_COM_COMM_02_ETH_02
DP_VPX_0236_MANUAL_PS_RTC	RTC Test	DP_SDG_COM_PERI_04_RTC_04
DP_VPX_0236_MANUAL_PS_TEMPSNSR	Temperature Sensor Test	DP_SDG_COM_PERI_04_TEMPSNSR_13
DP_VPX_0236_MANUAL_PS_ADM	Voltage Monitoring Test	DP_SDG_COM_PERI_04_VOLTAGEMONIT_14
PROGRAMMABLE LOGIC
DP_VPX_0236_MANUAL_PL_LMK_PLL	LMK PLL Test	DP_VPX_0233_MANUAL_PL_LMK_PLL
DP_VPX_0236_MANUAL_PL_AFE7906_ADC	AFE7906 ADC Test	DP_VPX_0233_MANUAL_PL_AFE7906_ADC
DP_VPX_0236_MANUAL_PL_DDR4	DDR4 (PL) Test	DP_SDG_COM_MEM_01_DDR_07
DP_VPX_0236_MANUAL_PL_PCI	PCI Test	New
DP_VPX_0236_MANUAL_PL_UART	PL UART Test	DP_SDG_COM_COMM_02_RS422RS232/RS485_01
DP_VPX_0236_MANUAL_PL_LVTTL	LVTTL Test	DP_VPX_0233_MANUAL_PL_LVTTL
DP_VPX_0236_MANUAL_PL_LVDS	LVDS Test	DP_VPX_0233_MANUAL_PL_LVDS
DP_VPX_0236_MANUAL_PL_10G	10G Test	DP_VPX_0227_MANUAL_PL_10G
DP_VPX_0236_MANUAL_PL_JUNC_TEMP	FPGA Junction Temperature Test	DP_VPX_0233_MANUAL_PL_JUNC_TEMP
DP_VPX_0236_MANUAL_PL_I2C_READ_TEMP	I2C Temperature Read Test	New

## Test Configuration
Test configuration shall enable the user to configure each of the Auto/manual mode test cases. If the configuration file is already available (in a predefined path) then it shall be be read and stored in an appropriate data structures. If configuration file is unavailable (in a predefined path) then the following test cases shall be perform.
### Auto Mode Test Selection
This shall configure the Auto Mode test cases by getting the input from user to Enable/Disable the state of all the available test cases in Auto mode.
### Manual Mode Test Selection
This shall configures the Manual Mode test cases by getting the input from user to Enable/Disable the state of all the available test cases in Manual mode.
### Test Specific Details
This is to provide the configuration details specific to the enabled test cases in either or both of the auto and manual mode test case options.
## Test Performance
### Auto Mode Test Performance
The auto mode test performance shall perform the auto mode test cases that are enabled using the target configuration for qualifying the board. The selection of the auto mode test depends on the user (Refer 4.1 for Test Configuration). The following are the inputs for performing auto mode test :

- ENTER THE NO OF CYCLE [1-200]:
- ITERATION GAP (in Seconds) [1s - 10s]:
- INTER-ITERATION GAP (in Seconds) [1s – 10s]:

The user shall need to enter input first. The enabled auto mode test cases will then be performed for the specified number of cycles. The summary of the auto mode test results will be displayed as a consolidated report once the test process is over. The Test process shall be paused at any time (using Ctrl+C) to see the status report and can be continued further or stopped to get back to the main menu. A consolidated report shows the status of the auto mode Test cases that are executed shall be displayed in the console and the report shall be stored in a file.
### Manual Mode Test Performance
The manual mode test performance shall perform the manual mode test cases that are enabled using the target configuration for qualifying the board. The selection of the manual mode test depends on the user (Refer 4.1 for Test Configuration).

The following are the details regarding the test cases included in manual mode Test Performance.

#### Processing Section

Requirement ID :
DP_VPX_0236_MANUAL_PS

##### Processor Test

The following test cases shall be performed to qualify the processor ALU and FPU test cases. The following test cases are listed below.

Requirement ID :
DP_VPX_0236_MANUAL_PS_PRCS

###### ALU Test
Requirement ID	DP_VPX_0236_MANUAL_PS_PRCS_01
Description	This test shall be performed to qualify the processor (ALU). The following tests are to be carried out. / 1. Arithmetic operation Test (Addition, Subtraction, Division and Multiplication) / 2. Shift operation Test (Left shift and Right shift) / 3. Logical operation Test (AND, OR and NOT)

###### FPU Test
Requirement ID	DP_VPX_0236_MANUAL_PS_PRCS_02
Description	This test shall be performed to qualify the processor (FPU). The following tests are to be carried out. / 1. Floating point Arithmetic Test (Floating point Addition, Subtraction, Multiplication and Division).

##### DDR4 Test
The following test cases shall be performed to qualify the DDR4. The following test cases are listed below

Requirement ID :
DP_VPX_0236_MANUAL_PS_DDR4

###### Data Bus Test
Requirement ID	DP_VPX_0236_MANUAL_PS_DDR4_01
Description	This test shall be performed to qualify the data bus lines in the memory device. The Walking 1's and Walking 0's test shall be carried out. Perform memory walking ones test by left shifting the data, 1 bit at a time until it reaches the 32nd bit. Perform memory walking zero tests by left shifting the complement of data , 1 bit at a time until it reaches the 32nd bit. If both test cases are success, then the test shall be considered as PASS, otherwise FAIL.

###### Address Bus Test
Requirement ID	DP_VPX_0236_MANUAL_PS_DDR4_02
Description	This test shall be performed to qualify the address bus lines in the memory device. A base address shall be written with known Pattern and rest of the addresses are written with Anti pattern. Read the data from all these locations. If the read value and written value are not same, then return error else the base address shall be written with anti pattern and rest of the addresses are written with pattern. Read the data from all these locations. If the read value and written value are same, then test shall be considered as PASS, otherwise FAIL

###### Device Test
Requirement ID	DP_VPX_0236_MANUAL_PS_DDR4_03
Description	This test shall be performed to determine whether every bit in the device is capable of holding both 0 and 1. Write the incremental counter 32-bit data (0x00 00 00 00 , 0x00 00 00 01, 0x00 00 00 02,......,n) in the allocated memory of particular size (RAM size). Start reading the data from starting memory location and check for previously written data if both are not same then return error, else write inverted data to same location. Repeat this sequence for next memory location until maximum size (RAM size) is reached. Start reading the data from first memory location and check for previously written inverted data. If both are not same then return error else repeat this sequence for next memory location until maximum size (RAM size) is reached. If the written values and read back values are same, then test shall be considered as PASS, otherwise FAIL.

##### EEPROM Test
The following test cases shall be performed to qualify the EEPROM. The following test cases are listed below

Requirement ID :
DP_VPX_0236_MANUAL_PS_EEPROM
###### Upload Board Information
Requirement ID	DP_VPX_0236_MANUAL_PS_EEPROM_01
Description	This test shall be performed to validate the proper initialization of flash device. The device shall be initialized and a predefined data shall be loaded and read back to ensure proper initialization of the device. If both values are same, then test shall be declared as PASS, otherwise FAIL. / Note: Information shall be loaded only once for each board.

###### Data Retention Test
Requirement ID	DP_VPX_0236_MANUAL_PS_EEPROM_02
Description	This test shall be performed to qualify the authenticity of the memory device. A read operation shall be performed to get the Data stored in the memory. If the read data is the expected value, then test shall be declared PASS, otherwise FAIL.

###### Checksum Test
Requirement ID	DP_VPX_0236_MANUAL_PS_EEPROM_03
Description	This test shall performed to check the data integrity in the memory device. The data in the memory device shall be read from a fixed area/locations and checksum shall be computed. The computed checksum shall be compared against the pre-loaded/known checksum value.

###### Write / Read Test
Requirement ID	DP_VPX_0236_MANUAL_PS_EEPROM_04
Description	This test shall be performed by getting offset address and data from the user as an input and write the input data in the input address and read the data from the user given input address, If both write and read data are same then shall be considered as PASS else FAIL.

##### MRAM Test
The following test cases shall be performed to qualify the MRAM. The following test cases are listed below
Requirement ID :
DP_VPX_0236_MANUAL_PS_MRAM
###### Upload Board Information
Requirement ID	DP_VPX_0236_MANUAL_PS_MRAM_01
Description	Refer the Section 4.2.2.1.3.1

###### Data Retention Test
Requirement ID	DP_VPX_0236_MANUAL_PS_MRAM_02
Description	Refer the Section 4.2.2.1.3.2

###### Checksum Test
Requirement ID	DP_VPX_0236_MANUAL_PS_MRAM_03
Description	Refer the Section 4.2.2.1.3.3

###### Full Memory Test
Requirement ID	DP_VPX_0236_MANUAL_PS_MRAM_04
Description	This test shall be performed by getting offset address and data from the user as an input and write the input data in the input address and read the data from the user given input address, If both write and read data are same then shall be considered as PASS else FAIL.

##### NOR Flash Test
The following test cases shall be performed to qualify the NOR Flash. The following test cases are listed below
Requirement ID :
DP_VPX_0236_MANUAL_PS_NORFLASH
###### Upload Board Information
Requirement ID	DP_VPX_0236_MANUAL_PS_NORFLASH_01
Description	Refer the Section 4.2.2.1.3.1

###### Data Retention Test
Requirement ID	DP_VPX_0236_MANUAL_PS_NORFLASH_02
Description	Refer the Section 4.2.2.1.3.2

###### Checksum Test
Requirement ID	DP_VPX_0236_MANUAL_PS_NORFLASH_03
Description	Refer the Section 4.2.2.1.3.3

##### NAND Flash Test
The following test cases shall be performed to qualify the NAND Flash. The following test cases are listed below
Requirement ID :
DP_VPX_0236_MANUAL_PS_NANDFLASH
###### Upload Board Information
Requirement ID	DP_VPX_0236_MANUAL_PS_NANDFLASH_01
Description	Refer the Section 4.2.2.1.3.1

###### Data Retention Test
Requirement ID	DP_VPX_0236_MANUAL_PS_NANDFLASH_02
Description	Refer the Section 4.2.2.1.3.2

###### Checksum Test
Requirement ID	DP_VPX_0236_MANUAL_PS_NANDFLASH_03
Description	Refer the Section 4.2.2.1.3.3

##### SATA Test
The following test cases shall be performed to qualify the SATA. The following test cases are listed below

Requirement ID :

DP_VPX_0236_MANUAL_PS_SATA
###### Read/Write Test

Requirement ID	DP_VPX_0236_MANUAL_PS_SATA_01
Description	This test shall mount the SATA device in the specified mount point and will create and write sample data in a file in the mounted partition. This test shall read the file content from the device and compare with the written file. If both written and read data is same, it will return success, otherwise failure. / Note: Make sure that the SATA device is connected with the board and formatted as linux Partition.

##### UART Test
The test cases shall be performed to qualify the UART. The following test cases are listed below
Requirement ID :
DP_VPX_0236_MANUAL_PS_UART
###### Write Test
Requirement ID	DP_VPX_0236_MANUAL_PS_UART_01
Description	This test shall be performed to qualify the UART Write Functionality. A user entered data or a predefined data is transmitted. If the transmitted data and the data received at the host are same, declare the test case as PASS, otherwise as FAIL.

###### Read Test
Requirement ID	DP_VPX_0236_MANUAL_PS_UART_02
Description	This test shall be performed to qualify the UART Read Functionality. The data entered at the host is received. If the received data and the data transmitted from the host are same, declare the test case as PASS, otherwise as FAIL.

##### Ethernet Test
The following test cases shall be performed to qualify the Ethernet. The following test cases are listed below

Requirement ID :
DP_VPX_0236_MANUAL_PS_ETH

###### Ethernet Ping Test
Requirement ID	DP_VPX_0236_MANUAL_PS_ETH_01
Description	This test shall be performed between 2 ports of different systems considering that both ports are connected with LAN cable. This shall be carried out by sending & receiving data through ping command to/from Target port IP address. If ping test is passed, declare the test case as PASS, otherwise as FAIL. / Note: Pre-loaded data will be transferred by Operating System as part of Ethernet Ping test

###### Ethernet Socket Test

Requirement ID	DP_VPX_0236_MANUAL_PS_ETH_02
Description	This test shall be performed between 2 ports of same or different systems considering that both ports are connected with LAN cable. Socket communication shall be established between these 2 systems and data shall be transmitted from client system to server system. The server system transmits the received data to client. If the transmitted and received data are same, declare the test case as PASS, otherwise as FAIL. / Note : Board Ethernet(RGMII & SGMII) are need to connect in the hub and set the unique IP address to validate the Ethernet Socket test.

##### RTC Test
The following test cases shall be performed to qualify the RTC. The following test cases are listed below

Requirement ID :
DP_VPX_0236_MANUAL_PS_RTC
###### RTC Test
Requirement ID	DP_VPX_0236_MANUAL_PS_RTC_01
Description	The RTC parameters are configured with the user selected values and reading it after a predefined gap (EX. 8 secs). If the read time is updated with an addition of predefined gap then the test is considered as pass, else fail. / Note: The test result with tolerance of +/-1 second in addition to the expected seconds will be accepted.

##### Temperature Sensor Test

The following test cases shall be performed to qualify the Temperature Sensor. The following test cases are listed below.

Requirement ID :
DP_VPX_0236_MANUAL_PS_TEMPSNSR

###### Temperature Sensor Test
Requirement ID	DP_VPX_0236_MANUAL_PS_TEMPSNSR_01
Description	This test shall be carried out by reading the Temperature Sensor value and checking whether the read value is within the low limit and high limit of Local temperature which is configured by the user. If the Temperature values are within the limits then the test case is declared as PASS, otherwise as FAIL. / Note: Temperature Sensor Limits are listed below. / Local Temperature ( -40 to 80) / External Temperature(-40 to 80)

##### Voltage Monitoring Test

The following test cases shall be performed to qualify the ADM. The following test cases are listed below

Requirement ID :
DP_VPX_0236_MANUAL_PS_ADM
###### Voltage Monitoring Test
Requirement ID	DP_VPX_0236_MANUAL_PS_ADM_01
Description	The Voltage limits will be provided in a file ("dpvpx0236_adm_limits.txt"). This file will be read in-order to compare the read voltages. This test shall be carried out by reading the ADM input channel voltages from the processor and verify the read value with expected voltage from the file. Also, read and display power good status. / Note : Application will load the predefined values from the ADM Limit file.

#### Programmable Logic

Requirement ID :
DP_VPX_0236_MANUAL_PL

##### LMK PLL Test
The following test cases shall be performed to qualify the LMK PLL Interface. The following test cases are listed below.
Requirement ID :
DP_VPX_0236_MANUAL_PL_LMK_PLL
###### File Configuration
Requirement ID	DP_VPX_0236_MANUAL_PL_LMK_PLL_01
Description	This operation shall provide an option to configure PLL. This can be done through Reading and writing the Data in particular offset through SPI Interface. / Note: PLL_CONFIG.txt file will be used to configure the PLL.

###### File Dump
Requirement ID	DP_VPX_0236_MANUAL_PL_LMK_PLL_02
Description	This operation shall provide an option to Read the Data from PLL through SPI Interface.

###### Single Write

Requirement ID	DP_VPX_0236_MANUAL_PL_LMK_PLL_03
Description	This test shall provide an option to write single Data through SPI Interface.

###### Single Read
Requirement ID	DP_VPX_0236_MANUAL_PL_LMK_PLL_04
Description	This test shall provide an option to Read Back single data through SPI Interface.

###### PLL Lock Status
Requirement ID	DP_VPX_0236_MANUAL_PL_LMK_PLL_05
Description	This operation shall be performed to verify the Lock status of the LMK PLL.

###### Sysref Enable/Disable
###### Enable
Requirement ID	DP_VPX_0236_MANUAL_PL_LMK_PLL_06_01
Description	This operation provides an option to Enable Sysref.

###### Disable
Requirement ID	DP_VPX_0236_MANUAL_PL_LMK_PLL_06_02
Description	This operation provides an option to Disable Sysref.

##### AFE7906 ADC Test Cases
The following test cases shall be performed to qualify the AFE7906 ADC Interface. The following test cases are listed below.

Requirement ID :
DP_VPX_0236_MANUAL_PL_AFE7906_ADC

###### AFE Core Reset

Requirement ID	DP_VPX_0236_MANUAL_PL_AFE7906_ADC_01
Description	This operation provides an option to Reset the AFE chip. / Note: 1 AFE chip is available for Resetting.

###### AFE Single Write

Requirement ID	DP_VPX_0236_MANUAL_PL_AFE7906_ADC_02
Description	This operation provides an option to perform the single write operation in AFE chip.

###### AFE Single Read

Requirement ID	DP_VPX_0236_MANUAL_PL_AFE7906_ADC_03
Description	This operation provides an option to perform the single read operation in AFE chip.

###### AFE Bring-up

Requirement ID	DP_VPX_0236_MANUAL_PL_AFE7906_ADC_04
Description	This operation shall be performed to configure the AFE7906 ADC. This can be done by loading Text file which was followed by Reset and Core Initialization.

###### AFE Core Initialization
Requirement ID	DP_VPX_0236_MANUAL_PL_AFE7906_ADC_05
Description	This operation provides an option to check the Core Initialization for AFE Chip. / Note: AFE chip is available for Resetting.

###### JESD Bond Status
Requirement ID	DP_VPX_0236_MANUAL_PL_AFE7906_ADC_06
Description	This Operation shall be performed to synchronize the JESD and FPGA. It can be verified by reading the BOND STATUS REGISTER.

###### Data Logging
Requirement ID	DP_VPX_0236_MANUAL_PL_AFE7906_ADC_07
Description	This operation shall be performed to get the IQ Data From AFE chip. / Note: Data Plotting is done by a separate tool – HSDC Pro, 4 number of Rx and 1 Fb channels are available to get the IQ Data.

###### Band Selection
Requirement ID	DP_VPX_0236_MANUAL_PL_AFE7906_ADC_08
Description	This operation shall be performed to select Wide band and Narrow band to log ADC and DDC data.

###### ADC Digital Attenuation
Requirement ID	DP_VPX_0236_MANUAL_PL_AFE7906_ADC_09
Description	This module shall write / read the Digital Attenuator Settings through SPI interface. / Note: AGC, MSTC, CAL settings are available for Attenuation Settings.

###### AGC Digital Attenuation
Requirement ID	DP_VPX_0236_MANUAL_PL_AFE7906_ADC_09_01
Description	This module shall write / read AGC attenuation value through corresponding FPGA register.

###### MSTC Digital Attenuation

Requirement ID	DP_VPX_0236_MANUAL_PL_AFE7906_ADC_09_02
Description	This module shall write / read MSTC attenuation value through corresponding FPGA register.

###### CAL Digital Attenuation

Requirement ID	DP_VPX_0236_MANUAL_PL_AFE7906_09_03
Description	This module shall write / read CAL attenuation value through corresponding FPGA register.

###### HD2 Correction Enable
The following test cases shall be performed to qualify the HD2 Correction enable. The following test cases are listed below.

Requirement ID :
DP_VPX_0236_MANUAL_PL_AFE7906_ADC_HD2
###### HD2 Coeff Write

Requirement ID	DP_VPX_0236_MANUAL_PL_AFE7906_ADC_10_01
Description	This Operation provides an option to write HD2 Coefficient Values in AFE.

###### HD2 Coeff Read

Requirement ID	DP_VPX_0236_MANUAL_PL_AFE7906_ADC_10_02
Description	This Operation provides an option to Read HD2 Coefficient Values from AFE.

###### ADC Dynamic Configuration

The following test cases shall be performed to qualify the ADC Dynamic configuration. The following test cases are listed below.

Requirement ID :
DP_VPX_0236_MANUAL_PL_AFE7906_ADC_DYNAMIC

###### Device Health Status

Requirement ID	DP_VPX_0236_MANUAL_PL_AFE7906_ADC_11_01
Description	This Operation shall Provide an option the Check the Device Health status.

###### Update RxNco

Requirement ID	DP_VPX_0236_MANUAL_PL_AFE7906_ADC_11_02
Description	This Operation shall Provide an option to update the Rx NCO Frequency.

###### Update FbNco

Requirement ID	DP_VPX_0236_MANUAL_PL_AFE7906_ADC_11_03
Description	This Operation shall Provide an option to update the Fb Nco Frequency.

###### Set Rx DSA

Requirement ID	DP_VPX_0236_MANUAL_PL_AFE7906_ADC_11_04
Description	This Operation shall Provide an option to update the Rx DSA.

###### Set Fb DSA

Requirement ID	DP_VPX_0236_MANUAL_PL_AFE7906_ADC_11_05
Description	This Operation shall Provide an option to update the Fb DSA.

###### ADC Automation
The following test cases shall be performed to qualify the ADC Automation. The following test cases are listed below.

Requirement ID :
DP_VPX_0236_MANUAL_PL_AFE7906_ADC_AUTOMATION
###### Automation Data Logging

Requirement ID	DP_VPX_0236_MANUAL_PL_AFE7906_ADC_AUTOMATION_01
Description	This operation shall provide an option to get the IQ Data From AFE chip with different frequencies at a time and plot that data in HSDC Pro.

###### Automation Phase Matching

Requirement ID	DP_VPX_0236_MANUAL_PL_AFE7906_ADC_AUTOMATION_02
Description	This operation shall Provide an option to get the phase difference of all channels at a time.

##### PL DDR4 Test
The following test cases shall be performed to qualify the PL DDR4 Interface. The following test cases are listed below.

Requirement ID :
DP_VPX_0236_MANUAL_PL_DDR4
###### Data Bus Test
Requirement ID	DP_VPX_0236_MANUAL_PL_DDR4_01
Description	Refer the Section 4.2.2.1.2.1

###### Address Bus Test
Requirement ID	DP_VPX_0236_MANUAL_PL_DDR4_02
Description	Refer the Section 4.2.2.1.2.2

###### Device Test
Requirement ID	DP_VPX_0236_MANUAL_PL_DDR4_03
Description	Refer the Section 4.2.2.1.2.3

###### Full Memory Test
Requirement ID	DP_VPX_0236_MANUAL_PL_DDR4_04
Description	This test shall be performed to determine whether each memory location of DDR4 is usable for read and write operations. Firstly, incremental counter is being written from the starting base address of the DDR4 upto its full size (4GB). / Secondly, the read operation is carried out for the full DDR4 (4GB) from the base address. If the read data is not same as written date, then the test is failed, else the test is passed.

###### Single Write / Read
Requirement ID	DP_VPX_0236_MANUAL_PL_DDR4_05
Description	This test shall be performed by getting offset address and data from the user as an input and write the input data in the input address and read the data from the user given input address, If both write and read data are same then shall be considered as PASS else FAIL.

##### PCIe Test
The following test cases shall be performed to qualify the PCIe. The following test cases are listed below.
Requirement ID:
DP_VPX_0236_MANUAL_PL_PCIe
###### PCIe Write
Requirement ID	DP_VPX_0236_MANUAL_PL_PCIe_1
Description	This module shall provide option to write single Data into user specified pcie offset. If the write process done then PASS otherwise FAIL.

###### PCIe Read
Requirement ID	DP_VPX_0236_MANUAL_PL_PCIe_2
Description	This module shall provide option to read single Data into user specified pcie offset. If the read process done then PASS otherwise FAIL.

###### PCIe Full Memory Test
Requirement ID	DP_VPX_0236_MANUAL_PL_PCIe_3
Description	This test shall be performed to compare the write and read data are same in all possible address of PCIe up to the total size. If the verification process done then PASS otherwise FAIL. / Note: Total size of PCIe is 8192 bytes.

##### 10G Test
The following test cases shall be performed to qualify the 10G Interface. The following test cases are listed below.

Requirement ID :
DP_VPX_0236_MANUAL_PL_10G
###### IP Configuration

Requirement ID	DP_VPX_0236_MANUAL_PL_10G_01
Description	This test shall be done to configure the 10G Ethernet through a file which contains IP address for source and destination, MAC address, Subnet Mask, Gateway IP, and Port number for source and destination.

###### Core Status

Requirement ID	DP_VPX_0236_MANUAL_PL_10G_02
Description	This Module provides a provision to check the Core status of 10G Ethernet. / Note: 2 no.of channels are available to check the Lane status.

###### BandWidth Test

Requirement ID	DP_VPX_0236_MANUAL_PL_10G_03
Description	This test shall be used to validate the bandwidth of the 10G ethernet by calculating the speed of transmission through transmitting and receiving of data.

##### PL UART Test
The test shall be carried out to qualify the UART module in the PL section of the DP-VPX-0236.

Requirement ID :
DP_VPX_0236_MANUAL_PL_UART
###### Read

Requirement ID	DP_VPX_0236_MANUAL_PL_UART_01
Description	Refer the Section 4.2.2.1.8.2

###### Write
Requirement ID	DP_VPX_0236_MANUAL_PL_UART_02
Description	Refer the Section 4.2.2.1.8.1

##### LVTTL Test

The following tests shall be carried out to qualify the LVTTL interface.

Requirement ID :
DP_VPX_0236_MANUAL_PL_LVTTL
###### IO Mode Test

Requirement ID	DP_VPX_0236_MANUAL_PL_LVTTL_01
Description	This test shall be performed to qualify the LVTTL IO's. Waking 1's and 0's shall be done to validate the working of the LVTTL IO's. If the read value and written values are same then this test is declared as PASS otherwise FAIL.

###### Clock Mode Test

Requirement ID	DP_VPX_0236_MANUAL_PL_LVTTL_02
Description	This test shall be performed to qualify the LVTTL IO's. Clock pulse shall be sent to calculate the ON and OFF time of the IOs to validate the working of the LVTTL IO's. Frequency calculated from the ON time and OFF time of the IO is same as the frequency given as input then the test is declared as PASS otherwise FAIL. / Note: A Clock Frequency of 1MHz will be sent in each IO lines

##### LVDS Test
The following tests shall be carried out to qualify the LVDS interface.

Requirement ID :
DP_VPX_0236_MANUAL_PL_LVDS

###### Clock Mode Test

Requirement ID	DP_VPX_0236_MANUAL_PL_LVDS_02
Description	This test shall be performed to qualify the LVDS IO's. Clock pulse shall be sent to calculate the ON and OFF time of the IOs to validate the working of the LVDS IO's. Frequency calculated from the ON time and OFF time of the IO is same as the frequency given as input then the test is declared as PASS otherwise FAIL. / Note: A Clock Frequency of 1MHz will be sent in each IO lines.

##### FPGA Junction Temperature Test
The following test cases shall be performed to qualify the FPGA Junction Temperature.

Requirement ID	DP_VPX_0236_MANUAL_PL_JUNC_TEMP
Description	This module provides the provision to read the FPGA Junction temperature from the device.

##### I2C Temperature Read Test
The following test cases shall be performed to qualify the I2C Temperature.

Requirement ID	DP_VPX_0236_MANUAL_PL_I2C_READ_TEMP
Description	This module provides the provision to read temperature using I2C Device.

### Auto Mode Test Cases
In auto mode test shall be performed auto mode test cases that are enable by user configure by ATP hardware to qualify in the board. The following inputs are allow the user to select the test to perform, number of cycles to perform, delay between each cycle and delay between each tests.
Requirement ID :
DP_VPX_0236_AUTO
#### Processor Test
Refer the section 4.2.2.1.1
#### DDR4 Test
Refer the section 4.2.2.1.2
#### EEPROM Test
Refer the section 4.2.2.1.3
#### MRAM Test
Refer the section 4.2.2.1.4
#### NOR Flash Test
Refer the section 4.2.2.1.5
#### NAND Flash Test
Refer the section 4.2.2.1.6
#### Ethernet Test
Refer the section 4.2.2.1.9
#### RTC Test
Refer the section 4.2.2.1.10
#### Temperature Sensor Test
Refer the section 4.2.2.1.12
#### Voltage Monitoring Test
Refer the section 4.2.2.1.13
# Software System Attributes
## Performance Requirements
The Ethernet data transfer rate shall be minimum of 100mbps.
## Safety Requirements
NA
## Security Requirements
NA
## Software Quality Attributes
NA
## Business Rules
NA

# Other Requirements
NA

# Requirements Traceability

Requirement ID in SRS	Section / Requirement ID in HRS Document
DP_VPX_0236_MANUAL_PS_PRCS	DP-VPX-0236-HRS-002
DP_VPX_0236_MANUAL_PS_DDR4	DP-VPX-0236-HRS-008
DP_VPX_0236_MANUAL_PS_EEPROM	DP-VPX-0236-HRS-0012
DP_VPX_0236_MANUAL_PS_MRAM	DP-VPX-0236-HRS-0011
DP_VPX_0236_MANUAL_PS_NORFLASH	DP-VPX-0236-HRS-009
DP_VPX_0236_MANUAL_PS_NANDFLASH	DP-VPX-0236-HRS-0010
DP_VPX_0236_MANUAL_PS_SATA	DP-VPX-0236-HRS-0013
DP_VPX_0236_MANUAL_PS_UART	DP-VPX-0236-HRS-0015
DP_VPX_0236_MANUAL_PS_ETH	DP-VPX-0236-HRS-0013
DP_VPX_0236_MANUAL_PS_RTC	DP-VPX-0236-HRS-005
DP_VPX_0236_MANUAL_PS_TEMPSNSR	DP-VPX-0236-HRS-0017
DP_VPX_0236_MANUAL_PS_ADM	DP-VPX-0236-HRS-0023
DP_VPX_0236_MANUAL_PL_LMK_PLL	DP-VPX-0236-HRS-007
DP_VPX_0236_MANUAL_PL_AFE7906_ADC	DP-VPX-0236-HRS-003
DP_VPX_0236_MANUAL_PL_DDR4	DP-VPX-0236-HRS-008
DP_VPX_0236_MANUAL_PL_UART	DP-VPX-0236-HRS-0015
DP_VPX_0236_MANUAL_PL_LVTTL	DP-VPX-0236-HRS-004
DP_VPX_0236_MANUAL_PL_LVDS	DP-VPX-0236-HRS-004
DP_VPX_0236_MANUAL_PL_JUNC_TEMP	DP-VPX-0236-HRS-0017
DP_VPX_0236_MANUAL_PL_I2C_READ_TEMP	DP-VPX-0236-HRS-004
DP_VPX_0236_MANUAL_PL_PCI	DP-VPX-0236-HRS-0013
DP_VPX_0236_MANUAL_PL_10G	DP-VPX-0236-HRS-0014