## HARDWARE REQUIREMENTS SPECIFICATION (HRS)
Project: AUDS
Document ID: AUDS-HRS-001
Revision: 1.0

### 1. Module Overview
The AUDS hardware module integrates sensing, compute, flight control, and communication into a single ruggedized payload for UAV integration.

### 2. Features & Applications
- Real-time YOLOv8n inference at 30 fps
- Dual-IMU redundancy with voting logic
- RTK GPS for cm-level positioning
- FHSS anti-jam telemetry
- IP54 environmental protection

### 3. Block Diagram (Text Explanation)
Power from 6S Li-Ion battery → TI LM51231 PMIC → distributes 5V/12V/3.3V to:
- Jetson Orin NX (main compute)
- STM32H753 flight controller
- FLIR Boson 640 (thermal)
- Sony IMX477 (EO)
- Microhard pDDL modem
- Here+ RTK GPS
Dual IMU (BMI088 + ADIS16470) feed into STM32 with voting logic. All peripherals communicate via PCIe, UART, SPI, or GMSL2.

### 4. Specifications Table
Category	Component	Spec
Processor	Jetson Orin NX 16GB	100 TOPS, 15W
MCU	STM32H753	Cortex-M7, 2MB Flash
EO Camera	Sony IMX477	12MP, Global Shutter
Thermal	FLIR Boson 640	640x512, 60Hz
IMU (Primary)	BMI088	24g, 6-axis
IMU (Redundant)	ADIS16470	Tactical grade, 2000°/s
GPS	Here+ RTK	cm-level, dual band
Telemetry	Microhard pDDL	900MHz, 37dBm, FHSS
Battery	Tattu 22000mAh	6S, 12C, 45 min flight

### 5. Detailed Specification Statements
ID	Requirement
AUDS-HRS-001	The Jetson Orin NX shall operate at 15W TDP and provide 100 TOPS (INT8).
AUDS-HRS-002	The STM32H753 shall run PX4 flight stack with triple-redundancy IMU voting.
AUDS-HRS-003	The Sony IMX477 shall support global shutter to avoid motion artifacts.
AUDS-HRS-004	The FLIR Boson 640 shall output 14-bit raw thermal data over USB3.
AUDS-HRS-005	The Microhard pDDL shall operate at 900 MHz with 50 channels FHSS.
AUDS-HRS-006	The TI LM51231 PMIC shall provide 92% efficiency at 5A load.
AUDS-HRS-007	The system shall include an NVMe M.2 2280 (≥ 256GB) for fallback storage.

### 6. FPGA Section
N/A – All vision acceleration is handled by Jetson Orin NX’s dedicated NVDLA engine.

### 7. Development Platform
- SDK: JetPack 6.0
- Flight Stack: PX4 v1.15
- Debug: JTAG (STM32) + GDB (Jetson)
- Simulation: Gazebo + PX4-HIL

### 8. FAT & Demo Validation
Test	Criteria
Power-on self-test	All sensors enumerated within 5 sec
Thermal soak	-20°C to +50°C, 2 hrs each
Vibration	MIL-STD-810H, no physical damage
RF sensitivity	-110 dBm @ 900 MHz, BER < 1e-5
Endurance	45 min continuous detection