## SOFTWARE REQUIREMENTS SPECIFICATION (SRS)
Project: AUDS
Document ID: AUDS-SRS-001
Revision: 1.0

### 1. Product Perspective
AUDS software is a real-time embedded application running on Linux (Jetson) and NuttX RTOS (STM32). It performs sensor capture, AI inference, tracking, and MAVLink telemetry.

### 2. Functional Requirements
ID	Requirement
AUDS-SRS-001	Software shall capture 12MP EO frames at 30 fps via MIPI CSI-2.
AUDS-SRS-002	Software shall capture thermal frames at 60 Hz via GMSL2.
AUDS-SRS-003	Software shall run YOLOv8n INT8 quantized model at ≥ 30 fps.
AUDS-SRS-004	Software shall distinguish combatant vs. civilian by detecting weapon/uniform patterns.
AUDS-SRS-005	Software shall track up to 32 objects simultaneously using Kalman filters.
AUDS-SRS-006	Software shall output MAVLink 2 OBSTACLE_DISTANCE messages at 10 Hz.

### 3. External Interfaces
Interface	Protocol	Data Rate	Requirement ID
EO Camera	MIPI CSI-2	40 Gbps	AUDS-SRS-001
Thermal	GMSL2	6 Gbps	AUDS-SRS-002
Telemetry	MAVLink 2 over UART	345 kbps	AUDS-SRS-006
Video Downlink	V-Nova Perseus over Ethernet	10 Mbps	AUDS-SRS-007
NVMe Storage	PCIe Gen4	8 GB/s	AUDS-SRS-008

### 4. Performance Requirements
ID	Requirement
AUDS-SRS-009	Inference latency (camera → TensorRT output) < 40 ms.
AUDS-SRS-010	Tracking update latency < 10 ms.
AUDS-SRS-011	Total sensor-to-GCS latency < 150 ms.
AUDS-SRS-012	CPU load on Jetson ≤ 70% during max detection.

### 5. Safety Requirements
ID	Requirement
AUDS-SRS-013	On loss of RF link for > 1 sec, software shall write tracks to NVMe and initiate RTB.
AUDS-SRS-014	Dual IMU voting: if Δ > 5 deg/sec, discard outlier and flag fault.
AUDS-SRS-015	Software shall detect thermal sensor failure and fallback to EO-only mode.

### 6. Security Requirements
ID	Requirement
AUDS-SRS-016	All MAVLink 2 messages shall be signed and encrypted with AES-256-GCM.
AUDS-SRS-017	The Jetson root filesystem shall be encrypted with dm-crypt (LUKS).
AUDS-SRS-018	Secure boot shall be enabled on STM32 with signed firmware.

### 7. Real-Time Constraints
ID	Requirement
AUDS-SRS-019	The object detection thread shall use SCHED_DEADLINE with period = 33 ms, runtime = 15 ms.
AUDS-SRS-020	The flight control loop (PX4) shall run at 1 kHz on STM32.
AUDS-SRS-021	The MAVLink telemetry thread shall have priority 98 (Linux real-time).

### 8. AI/ML Module Requirements
ID	Requirement
AUDS-SRS-022	Model shall be pruned from YOLOv8n to ≤ 2.5 MB.
AUDS-SRS-023	Calibration shall use INT8 with TensorRT, mAP ≥ 0.85 @ IoU=0.5.
AUDS-SRS-024	Re-identification (Re-ID) embedding size ≤ 128 bytes per track.