## SYSTEM REQUIREMENTS SPECIFICATION (SyRS)
Project: Autonomous Urban Detection System (AUDS)
Document ID: AUDS-SyRS-001
Revision: 1.0
Classification: Unclassified – Controlled Distribution

### 1. Introduction
#### 1.1 Purpose
This document specifies the system-level requirements for the Autonomous Urban Detection System (AUDS), a UAV-borne payload designed for intruder detection in GPS-denied and EMI-contested environments.
#### 1.2 Scope
AUDS provides real-time detection, classification, and tracking of human combatants, civilians, small UAS, and ground vehicles. It operates in urban canyons, dense foliage, and nighttime border surveillance scenarios.
#### 1.3 Definitions
- EO: Electro-Optical
- IR: Infrared
- EMI: Electromagnetic Interference
- RTB: Return to Base

### 2. System Overview
AUDS is an edge-AI system mounted on a medium-lift UAV. It combines gimbaled EO/IR sensors, an NVIDIA Jetson Orin NX for deep learning, and a redundant flight controller. The system outputs MAVLink 2 telemetry to a Ground Control Station (GCS) and operates autonomously under RF jamming.

### 3. System Block Diagram (Text Description)
text
[EO/IR Sensor Suite] --> [Jetson Orin NX (ISP + TensorRT)] --> [MAVLink 2 Encapsulation] --> [RF Transceiver (900MHz/2.4GHz)] --> [GCS Display]
        |
        v
        [STM32H753 Flight Controller]
        |
        v
        [Dual IMU + RTK GPS + Optical Flow]
Fallback path: RF jam → onboard storage (NVMe) → visual odometry → RTB.

### 4. System Specifications
Parameter	Value
Detection Range (slant)	500 m (human), 1000 m (vehicle)
Classification Range	200 m
Latency (sensor → alert)	< 150 ms
Operating Temperature	-20°C to +50°C
EMI Resilience	FHSS + AES-256-GCM
Endurance	45 min (hover), 90 min (loiter)

### 5. System Level Requirements
ID	Requirement
AUDS-SyRS-001	System shall detect human-sized targets at 500 m slant range under urban canyon conditions.
AUDS-SyRS-002	System shall classify combatant vs. civilian via uniform/weapon detection at 200 m.
AUDS-SyRS-003	System shall maintain end-to-end latency < 150 ms from image capture to operator alert.
AUDS-SyRS-004	System shall continue autonomous operation for ≥ 3 minutes after RF link loss.
AUDS-SyRS-005	System shall execute return-to-home using visual odometry when GPS is denied.

### 6. Hardware Requirements
ID	Requirement
AUDS-SyRS-006	System shall include a global shutter EO camera with ≥ 12 MP resolution.
AUDS-SyRS-007	System shall include a thermal camera with ≥ 640x512 resolution and 60 Hz refresh.
AUDS-SyRS-008	System shall provide 100 TOPS of INT8 inference performance onboard.

### 7. Software Requirements
ID	Requirement
AUDS-SyRS-009	System shall run YOLOv8n-based detection at ≥ 30 fps.
AUDS-SyRS-010	System shall implement Kalman filter-based multi-object tracking.
AUDS-SyRS-011	System shall support OTA firmware updates over MAVLink.

### 8. External Interfaces
Interface	Protocol	Bandwidth
EO Camera	MIPI CSI-2	40 Gbps
Thermal Camera	GMSL2	6 Gbps
C2 Link	Microhard pDDL (900 MHz, FHSS)	345 kbps
Video Downlink	V-Nova Perseus (2.4 GHz)	10 Mbps

### 9. Mechanical Requirements
ID	Requirement
AUDS-SyRS-012	Total payload mass ≤ 1.5 kg.
AUDS-SyRS-013	Enclosure shall be IP54 rated.
AUDS-SyRS-014	System shall withstand MIL-STD-810H vibration (helicopter profile).

### 10. Environmental Requirements
ID	Requirement
AUDS-SyRS-015	Operate in 95% relative humidity (non-condensing).
AUDS-SyRS-016	Survive 30-minute rain at 10 mm/hr.
AUDS-SyRS-017	Reject false positives due to high ambient heat via EO/IR fusion.