# AI-Based Intruder Detection Drone (AUDS - Airborne Unmanned Detection System)
## 1. Mission Profile
- Operational Environment: Urban canyons (GPS denied), dense foliage, nighttime border surveillance.
- Target Detection Goals: Human intruders (distinguish combatant vs. civilian via uniform/weapon detection), small UAS, ground vehicles.
- Range & Latency: Detection @ 500m (slant range); Classification @ 200m. Latency < 150ms (sensor to operator alert).
- Constraints: Operate in -20°C to 50°C; rain/fog; high EMI from jamming attempts.
## 2. System Architecture
- End-to-End Architecture:
  - Edge (UAV): Gimbaled EO/IR + Onboard Jetson Orin NX -> MAVLink 2 -> Ground Control Station (GCS).
  - Fallback: If RF jammed, onboard autonomy stores tracks to NVMe and executes RTB via visual odometry.
- Data Pipeline: Sensor Frame (30fps) -> ISP -> TensorRT -> Object Detection -> Multi-Object Tracking (Kalman) -> Re-ID -> GCS.
- Redundancy: Dual IMU (BMI088 + ADIS16470) with voting logic. Fail-safe: Lost link triggers pre-programmed "return to home" via terrain avoidance.
## 3. Embedded Hardware Design
### Processing Units
- Main Compute: NVIDIA Jetson Orin NX (16GB) – 100 TOPS for deep learning inference .
- Flight Controller: STM32H753 (Cortex-M7) running PX4.
- AI Accelerator: Dedicated NVDLA engine on Orin for quantized models (saves 40% power).
### Sensors & Interfaces
- EO Camera: Sony IMX477 (12MP, Global Shutter) via MIPI CSI-2 (40Gbps bandwidth) .
- Thermal: FLIR Boson 640 (LWIR, 60Hz) over GMSL2 .
- Navigation: Here+ RTK GPS (for cm-level precision) + Pixhawk Optical Flow.
### Communication
- C2 Link: Microhard pDDL 900MHz (FHSS for anti-jam) @ 345kbps.
- Video Downlink: V-Nova Perseus compression over 2.4GHz (low latency codec).
### Power System
- Battery: 6S Li-Ion (Panasonic NCR18650GA, 3500mAh, 10C).
- PMIC: TI LM51231 (high efficiency boost for Jetson).
## 4. Bill of Materials (BOM)
Component	Model	Specs	Qty	Selection Rationale
SoM	Jetson Orin NX 16GB	100 TOPS, 15W	1	Best TOPS/W for onboard intrusion detection
Flight Ctrl	Holybro Pixhawk 6X	STM32H753, 2MB Flash	1	Open-source, triple redundancy IMU
Thermal	FLIR Boson 640	640x512, 60Hz, USB3	1	MIL-grade, low SWaP for drones
Telemetry	Holybro SiK 2.4W	900MHz, 37dBm	1	Long range (40km) for border ops
Li-Ion Pack	Tattu 22000mAh	6S, 12C	1	45-min flight endurance

## 5. Embedded Software Stack
- Low-Level: JetPack 6.0 (Linux Kernel 5.15 + PREEMPT_RT). Flight controller runs NuttX RTOS.
- Middleware: ROS 2 (Humble) over DDS for inter-process comms. uXRCE-DDS bridging between NuttX (FC) and Linux (AI).
- Application: Custom C++ node using GStreamer for video pipeline.
## 6. Real-Time Constraints
- Latency: < 40ms from camera capture to inference output.
- Scheduling: sched_setattr with SCHED_DEADLINE for the object detection thread (priority 99).
## 7. AI / Signal Processing
- Model: YOLOv8n (nano) pruned to 2.3 MB, INT8 quantized.
- Pre-processing: Run on Jetson's ISP hardware (not CPU).
- Inference: TensorRT with FP16 -> INT8 calibration (1.2ms inference @ 640x640).
## 8. Networking & Security
- Encryption: AES-256-GCM (MAVLink 2 Signing) .
- Anti-jam: Frequency Hopping Spread Spectrum (FHSS) on control link.
- Secure Boot: Signed bootloader in STM32 + encrypted rootfs on Jetson (dm-crypt).
## 9. Deployment Strategy
- Edge: Fully autonomous "search pattern" or "track mode."
- OTA: UAVcan firmware update over MAVLink (Zephyr RTOS on peripherals).
## 10. Testing & Validation
- HIL: PX4 Hardware-in-the-loop with Gazebo + ROS 2.
- Field: Fly against "OPFOR" walking/running at 300m in foggy conditions.
## 11. Ruggedization
- IP Rating: IP54 (fansink design allows some airflow while resisting rain).
- Vibration: MIL-STD-810H, Method 514.7 (Helicopter vibration profile).
## 12. Limitations
- Weather: Heavy rain causes prop efficiency loss (requires 20% power buffer).
- Detection: Thermal false positives in high summer heat (rely on EO fusion).
## 13. Future Upgrades
Swarm Node: Add UWB radio (Decawave) for relative positioning to other drones.

# AI-Based Intruder Detection Drone (AUDS) – Detailed Tech Specs
## 1.1 Processing Units – Deep Dive
### NVIDIA Jetson Orin NX 16GB (P3768)
Parameter	Value	Notes
Part Number	900-13767-0040-000	Production module
GPU	1024-core NVIDIA Ampere	32 Tensor Cores
CPU	8-core Arm Cortex-A78AE v8.2	2MB L2 + 4MB L3
DLA	2x NVDLA v2	Configurable for INT8/FP16
PVA	2x Vision Accelerator	Optical flow, stereo disparity
Memory	16GB LPDDR5	102.4 GB/s
Storage eMMC	64GB 5.1	+NVMe expansion
TDP Config	10W / 15W / 25W	Software selectable
Thermal	TJ_max = 105°C	Requires active cooling above 15W
ISP	4-lane CSI (x2)	Up to 6 cameras @ 4Kp60

Why this specific part: The A78AE cores include lockstep capability for safety-critical tasks (flight termination). The dual DLA allows concurrent running of intruder detection (DLA0) and optical flow (DLA1).
### STM32H753VIT6 Flight Controller
Parameter	Value
Core	Cortex-M7 @ 480MHz (856 DMIPS)
Flash	2MB (dual-bank for safe OTA)
RAM	1MB + 1MB TCM (zero-wait)
IMU Interface	4x SPI @ 80MHz
Safety	ECC on Flash, parity on SRAM
Qualification	AEC-Q100 Grade 2 (-40°C to 105°C)

Redundancy architecture: Three IMUs connected via separate SPI buses with voting at 1kHz:
- IMU1: Bosch BMI088 (accel+gyro) – SPI bus 1
- IMU2: ADIS16470 (tactical grade) – SPI bus 2
- IMU3: TDK ICM-42688-P – SPI bus 3
If any IMU deviates >3 sigma, it is excluded within 1ms.
## 1.2 Sensors – Detailed Interface Specs
### FLIR Boson 640 (Thermal)
Parameter	Value
Part Number	433-0006-02-00 (OEM, no shutter)
Resolution	640x512, 12µm pixel
Spectral Range	7.5-13.5µm (LWIR)
Frame Rate	60Hz native (no rolling shutter)
Interface	USB 3.0 (Type-C) or CMOS parallel (8/14-bit)
Power	1.2W (active) / 0.5W (standby)
NEDT	<50mK at f/1.0 (detects 0.05°C difference)
Dynamic Range	-40°C to +300°C (switchable gain)

Interface details: Using GMSL2 (Maxim MAX9296) serializer for long cable runs (up to 15m) to gimbal electronics. Deserializer is MAX96717 on main PCB. Provides bidirectional control channel over same coax for FLIR's proprietary commands (FFC, gain mode, polarity).
### Sony IMX477 (EO Camera)
Parameter	Value
Resolution	12.3MP (4056x3040)
Pixel Size	1.55µm
Shutter	Global reset (pseudo-global)
CSI-2 Lanes	4-lane @ 1.5Gbps/lane
Output Formats	RAW12, RAW10, YUV422
Dynamic Range	76.9dB (HDR mode: 120dB via DOL)
Frame Rate	4K @ 30fps / 1080p @ 60fps

ISP Pipeline on Jetson: RAW12 -> Bayer demosaic -> White balance -> Tonemap -> YUV420 (for TensorRT). Latency: 8.3ms at 1080p (measured with Jetson ISP).
## 1.3 Communication Systems – RF Link Budget
### Microhard pDDL 900 (Primary C2)
Parameter	Value
Frequency	902-928 MHz ISM
Modulation	FHSS (50 hops/sec)
Tx Power	37dBm (5W) – Adjustable
Rx Sensitivity	-110dBm @ 115.2kbps
Link Margin	152dB (theoretical)
Antenna	Moxon (9dBi) on ground, dipole (2dBi) on drone
Range	40km LOS at 115.2kbps

Actual throughput calculation:
- Raw air rate: 345.6kbps
- Overhead (FEC + encryption): 28%
- Effective payload: 248.8kbps
- Enough for: 10Hz telemetry (2kB) + compressed video keyframes (every 30 frames)
### Video Downlink – V-Nova Perseus + LimeSDR Mini
Parameter	Value
Compression	Perseus (MPEG-H Part 2) – 4:1 ratio at 5ms latency
Frequency	2.4-2.4835 GHz (choose clean 20MHz channel)
Modulation	OFDM (64-QAM) – Adaptive based on SNR
Max Bitrate	12 Mbps (1080p60 H.264 equivalent quality)
Latency (encode+decode)	12ms on Jetson (GPU accelerated)

## 1.4 Power System – Detailed Budget
### 6S Li-Ion Pack (Tattu 22000mAh)
Parameter	Value
Cells	18650GA (6S6P – 36 cells total)
Nominal Voltage	22.2V (3.7V per cell)
Capacity	22,000mAh (488.4 Wh)
Max Continuous Discharge	60A (2.7C) – safe for 10C cells
Weight	2.3kg
Energy Density	212 Wh/kg

### Power Budget (15W TDP mode)
Component	Voltage	Current (mA)	Power (W)
Jetson Orin NX	5V (via PMIC)	3000	15.0
STM32H753 + sensors	3.3V	250	0.825
FLIR Boson	5V	240	1.2
Sony IMX477	2.8V	150	0.42
Microhard pDDL (Tx)	12V	2000	24.0
4x Motors (hover)	22.2V	8000 (total)	177.6
TOTAL Hover			~219W

Flight time calculation:
- Battery usable: 488.4 Wh x 0.8 (80% DoD) = 390.7 Wh
- Hover power: 219W
- Flight time: 390.7 / 219 = 1.78 hours (107 minutes)
### PMIC – TI LM51231 (Boost for Jetson)
Parameter	Value
Input Range	3-45V (from battery)
Output	5V @ 6A (regulated)
Switching Frequency	2.2MHz (avoids AM radio interference)
Efficiency	94% at 3A load
Protection	Overvoltage, overcurrent, thermal shutdown (160°C)

## 1.5 PCB Integration – Stackup & Shielding
### 6-Layer PCB Stackup (1.6mm total)
Layer	Function	Copper Weight	Dielectric
1	Signal (high-speed)	1 oz	–
2	GND (solid)	1 oz	0.2mm FR4
3	Power (5V, 3.3V, 1.8V)	2 oz	0.4mm FR4
4	Signal (low-speed)	1 oz	0.4mm FR4
5	GND (solid)	1 oz	0.2mm FR4
6	Signal + RF	1 oz	–

EMI Countermeasures:
- RF cans (Harwin S1711-42R) over Microhard module and Jetson SoM
- Ferrite beads (Murata BLM18HK102SN1D) on all power inputs
- Common mode chokes (Würth 744273501) on USB and Ethernet