# Passive RF Signal Detector (ESM Pod)
## 1. Mission Profile
- Environment: Battlefield EW screen (mounted on mast or MRZR vehicle).
- Target Goals: Detect and geolocate enemy drones (DJI, Mavic), squad radios (PRC-152), and man-in-the-middle attacks.
- Range: 5km (handheld radio), 15km (drone video link).
- Constraints: Must be passive (no emissions). EMI hardened against 50V/m.
## 2. System Architecture
Architecture: Antenna array -> Tuner -> FPGA -> ARM CPU -> Ethernet -> GCS.

Data Pipeline: I/Q samples -> FFT -> Signal Detection -> CNN Classifier -> TDOA Geolocation.

Redundancy: Dual-channel LNAs to prevent saturation if near friendly transmitter.
## 3. Hardware Design
- RF Frontend: Ettus Research B205mini (70MHz – 6GHz) or Analog Devices AD9363.
- FPGA: Xilinx Zynq 7020 (FFT acceleration).
- CPU: i.MX 8M Plus (Cortex-A53) for classification.
- Antenna: 4x Crossed-loop Magnetic (H-field) for direction finding.
## 4. BOM
Component	Model	Specs	Qty	Rationale
SDR	ADALM-PLUTO Rev C	325 MHz to 3.8 GHz	1	Low cost, 2x2 MIMO
FPGA	Artix-7 A100T	100k logic cells	1	Real-time FFT
LNA	Mini-Circuits ZX60-P105LN+	0.4dB NF	4	Boost weak drone signals

## 5. Software Stack
- OS: Yocto Project (Poky) for minimal attack surface.
- Signal: GNU Radio 3.10 with custom OOT module for de-hopping.
- AI: TFLite Micro for "Drone/Not Drone" classifier on waterfall images.
## 6. Real-Time
- Sampling: 61.44 MSPS.
- Latency: < 10ms from signal arrival to frequency ID.
## 7. AI Model
- Architecture: 1D-CNN on I/Q samples (MobileNetV1 style depthwise conv).
- Optimization: CMSIS-NN on Cortex-M7 core inside Zynq.
## 8. Security
Anti-tamper: Voltage glitch detection (TI TPS3808) wipes encryption keys if chassis opened.
## 9. Deployment
Field Cal: Automated noise floor calibration at power-up.
## 10. Validation
Test: Anritsu MS2720B signal generator simulating frequency-hopping drones.
## 11. Ruggedization
Enclosure: IP67, milled aluminum acting as heat sink for the AD9363.
## 12. Limitations
Scan speed: Full 6GHz scan takes 2 seconds (misses short burst transmissions).
## 13. Upgrades
Add AI: Correlate RF signature with acoustic drone sound for confirmation.

## 14. AI Model Details – Production Implementation
### 14.1 Model Architecture