# Embedded Tactical Display & Radio System
## 1. System Architecture (Heterogeneous by Design)
### End-to-End Block Diagram
text
┌─────────────────────────────────────────────────────────────────────────────────────┐
│ TACTICAL GROUND STATION (Ruggedized) │
├─────────────────────────────────────────────────────────────────────────────────────┤
│ │
│ ┌──────────────┐ ┌──────────────┐ ┌──────────────┐ ┌──────────────┐ │
│ │ SENSOR LAYER │ │ CONTROL LAYER│ │ DISPLAY LAYER│ │ RADIO LAYER │ │
│ ├──────────────┤ ├──────────────┤ ├──────────────┤ ├──────────────┤ │
│ │ GPS UART │───▶│ STM32H7 │───▶│ i.MX 8M Plus │───▶│ SX1278 SPI │ │
│ │ IMU I2C │ │ Real-time │ │ Qt Render │ │ LoRa 915MHz │ │
│ │ RF Detector │ │ Safety │ │ Map Overlay │ │ │ │
│ └──────────────┘ └──────┬───────┘ └──────┬───────┘ └──────┬───────┘ │
│ │ │ │ │
│ ▼ ▼ ▼ │
│ ┌──────────────────────────────────────────────────┐ │
│ │ BACKPLANE (CAN / Ethernet) │ │
│ └──────────────────────────────────────────────────┘ │
│ │ │
│ ▼ │
│ ┌─────────────────────────────┐ │
│ │ Optional AI Accelerator │ │
│ │ (Jetson Orin Nano Super) │ │
│ │ - Target classification │ │
│ │ - Drone detection │ │
│ └─────────────────────────────┘ │
└─────────────────────────────────────────────────────────────────────────────────────┘
### Data Pipeline with Latency
text
GPS (1Hz) ─────────────────────────────────────────┐
        │
IMU (100Hz) ──▶ STM32 (Kalman) ──▶ 5ms ──▶ Position
        │
Radio Rx (50Hz) ────────────────────────────────────┼──▶ i.MX 8M ──▶ Display @ 30fps
        │ (UI)
Camera (30fps) ──▶ Jetson (YOLO) ──▶ 45ms ──────────┘

Total UI latency: < 100ms (fighter jet requirement)
Rafale MDPU inspiration: The Rafale’s Modular Data Processing Unit fuses data from radar, optronics, EW, IFF, and data links . Your system does the same at ground-station scale.
## 2. Core Module Deep Dives
### 2.1 Embedded Processing Unit – Three-Tier Strategy
#### Tier 1: Real-Time Control (STM32H753) – Non-negotiable
Parameter	Value	Why This Matters
Part Number	STM32H753VIT6	Production-available
Core	Cortex-M7 @ 480MHz	856 DMIPS for control loops
Safety	ECC Flash, dual-core lockstep	Detects single-bit failures
Peripherals	4x SPI @ 80MHz, 4x UART, CAN-FD	Radio + GPS + IMU simultaneously
Power	300mW active	Runs for days on battery

This handles:
- Radio protocol stack (LoRa MAC, error correction)
- GPS NMEA parsing and IMU fusion (complementary filter, <1ms)
- Health monitoring (battery, link quality, temperature)
- Fail-safe watchdog (if main CPU crashes, STM32 keeps radio alive)
#### Tier 2: User Interface (NXP i.MX 8M Plus) – The Workhorse
Parameter	Value	Why This Matters
Part Number	MCIMX8M-Plus-DB	Production-grade
CPU	4x Cortex-A53 @ 1.8GHz + Cortex-M7	Application + real-time co-processor
GPU	GC7000L (3D) + 2D compositor	Smooth map panning, 60fps UI
NPU	2.3 TOPS (optional)	Lightweight ML without Jetson
Display	Dual LVDS, MIPI-DSI	10" sunlight-readable support
Power	2-6W (configurable)	Battery-friendly
Temp Range	-40°C to +105°C	Field deployable

Why not Raspberry Pi 5? The i.MX 8M Plus offers:
- Industrial temperature range (Pi: 0-50°C)
- 10+ year longevity (Pi: 2-3 years before revision change)
- Built-in NPU for 2.3 TOPS (Pi: 0 TOPS without HAT)
- CAN-FD for vehicle integration (Pi: none)
Raspberry Pi 5 is for prototyping only. Production tactical systems use NXP, TI, or ST industrial-grade .
#### Tier 3: AI Acceleration (NVIDIA Jetson Orin Nano Super) – Optional
Parameter	Value
Part Number	900-13767-0040-000
AI Performance	67 TOPS (INT8)
Power	7-25W configurable
Use Case	Drone detection, target classification

Add this ONLY if you need:
- Real-time object detection (<100ms inference)
- Multi-sensor AI fusion (camera + RF + acoustic)
- Running YOLOv8 or similar at >30fps
Otherwise, the i.MX 8M Plus NPU handles basic classification (person/vehicle/no-person) at 2.3 TOPS, enough for 90% of tactical UI needs .
### 2.2 Display Unit – Sunlight-Readable Tactical
Component	Model	Specs	Selection Rationale
Display	Newhaven NHD-10.1-HDMI-RSXP	10.1" IPS, 1000 nit, 1280x800	Sunlight-readable (critical outdoors)
Touch	PCAP (projected capacitive)	10-point, glove-compatible	Works with tactical gloves
Backlight Driver	Microchip MIC2841	PWM dimming, 10-100%	Night vision compatible (low red mode)
Interface	LVDS (via i.MX 8M)	4-lane, 60fps	Long cable run (2m) tolerant

Key spec: 1000 nits minimum. Consumer displays are 300-500 nits – unusable in direct sunlight. Tactical ops require 800-1200 nits .
### 2.3 Radio Communication System – Fighter Jet Equivalent
The Rafale uses Link 16 (secure, jam-resistant datalink). Your ground system uses a tiered approach:
#### Primary Radio: LoRa SX1278 (Long Range Telemetry)
Parameter	Value	Source
Frequency	915 MHz (Americas) / 868 MHz (EU)	ISM band
Range	5-10km (urban), 20km (LOS)
Data Rate	300 bps – 50 kbps	Adaptive spreading factor
Sensitivity	-148 dBm (lowest)	Can hear drones from 15km
Power	20dBm (100mW) transmit	10mA @ 3.3V
Modulation	LoRa (chirp spread spectrum)	Interference-resistant

Why LoRa over Wi-Fi/Bluetooth? Range. Wi-Fi dies at 300m. LoRa talks at 20km .
#### Secondary: Telemetry Radio (MAVLink for Drones)
Component	Model	Specs
Radio	Holybro 900X (SiK v2)	900MHz, 1W, 250kbps
Range	40km (LOS with directional antenna)
Protocol	MAVLink 2	Drone command/control

Use case: Direct drone integration. When a drone is within 5km, switch from LoRa (slow, long range) to 900X (fast, shorter range).
#### Optional: SDR for RF Detection (RTL-SDR v3)
Parameter	Value
Frequency	24MHz – 1.7GHz
Bandwidth	2.4MHz (real-time)
Interface	USB 2.0

Detects: Enemy drone video links, unauthorized radios, signal direction finding (with directional antenna).
### 2.4 Sensor Inputs – GPS and IMU
#### GPS: u-blox NEO-M9N (Not NEO-6M)
Parameter	NEO-6M (Old)	NEO-M9N (Current)
Channels	50	72
Constellations	GPS only	GPS + Galileo + GLONASS + BeiDou
Accuracy	2.5m	1.5m
Update Rate	5Hz	25Hz
Sensitivity	-161dBm	-167dBm
Jamming	None	RF interference detection

Why upgrade: In electronic warfare environments, single-constellation GPS fails. Multi-constellation gives 4x more satellites, works through jamming .
#### IMU: BNO055 (Absolute Orientation) – Sensor Fusion Done
Parameter	Value
Part Number	BNO055 (Bosch)
Sensors	3-axis accel + gyro + mag + fusion
Output	Quaternion / Euler angles
Internal Fusion	Runs on-chip (no CPU load)
Update Rate	100Hz
Interface	I2C or UART

Alternative: MPU6050 (raw only) requires 50% of your STM32 CPU for fusion. BNO055 offloads this – critical for real-time response.
#### Camera (Optional for AI)
Component	Model	Specs
CSI Camera	Arducam IMX477	12MP, MIPI CSI-2, 60fps
USB Camera	Logitech C920 (budget)	1080p, UVC compliant

## 3. Complete Bill of Materials (Production-Ready)
Tier	Component	Model	Specs	Qty	Cost (USD)
Must-Have	STM32	STM32H753VIT6	480MHz, ECC	1	$18
Must-Have	NXP i.MX 8M Plus	MCIMX8M-Plus	4xA53 @ 1.8GHz + NPU	1	$89
Must-Have	GPS	u-blox NEO-M9N	Multi-constellation	1	$45
Must-Have	IMU	BNO055	Absolute orientation	1	$28
Must-Have	Radio (Long)	SX1278 (915MHz)	LoRa, 20km range	1	$12
Must-Have	Radio (Fast)	Holybro 900X	250kbps, 40km	1	$65
Must-Have	Display	Newhaven 10.1"	1000 nit, LVDS	1	$320
Must-Have	Power	3S LiPo + DC-DC	12V, 5000mAh	1	$45
Optional	Jetson	Orin Nano Super	67 TOPS, 7-25W	1	$249
Optional	SDR	RTL-SDR v3	RF detection	1	$35
Optional	Camera	Arducam IMX477	12MP, CSI	1	$75

Base system (no AI): ~$622
Full system (with Jetson + SDR + Camera): ~$981
Prototype with Raspberry Pi 5: $150 board + $45 GPS + $28 IMU + $12 LoRa = $235
(But not field-deployable)
## 4. Embedded Software Stack
### OS Selection by Processor
Processor	OS	Rationale
STM32H7	FreeRTOS	Real-time, <1ms task switching
i.MX 8M Plus	Yocto Project (Linux)	Customizable, minimal attack surface, 10-year support
Jetson (if used)	Ubuntu 20.04/22.04 LTS + JetPack	NVIDIA SDK support

Why not Raspberry Pi OS on production? Consumer OS lacks security hardening, real-time patches, and long-term support .
### Middleware: ROS2 (Optional but Recommended)
Component	Package	Purpose
ROS2 Humble	Ubuntu 22.04	Message passing between STM32, i.MX, Jetson
MAVLink	mavros	Drone telemetry integration
QT 6.5	qtbase	UI framework for tactical display

### UI Framework: Qt for Embedded
Why Qt over React/Electron?
- Runs on bare Linux (no browser overhead)
- Hardware-accelerated (OpenGL)
- 60fps guaranteed (not "best effort")
- Touch-optimized for tactical gloves
- Memory footprint <100MB (Electron: 300MB+)
Features to implement:
- QML for declarative UI (faster iteration than C++)
- Map widget (OpenStreetMap or offline MBTiles)
- Custom widgets for compass, signal strength, target markers
### Communication Protocol Stack
text
┌─────────────────────────────────────────────────────────────┐
│ APPLICATION LAYER │
├─────────────────────────────────────────────────────────────┤
│ MAVLink (Drone) │ Custom Binary (Radio) │ NMEA (GPS) │
├─────────────────────────────────────────────────────────────┤
│ TRANSPORT LAYER │
├─────────────────────────────────────────────────────────────┤
│ UDP (Ethernet) │ UART (STM32 ↔ i.MX) │ SPI (LoRa) │
├─────────────────────────────────────────────────────────────┤
│ PHYSICAL LAYER │
├─────────────────────────────────────────────────────────────┤
│ LoRa (915MHz) │ 900MHz Telemetry │ Ethernet │
└─────────────────────────────────────────────────────────────┘
## 5. Real-Time Constraints
Task	Processor	Deadline	Consequence of Miss
Radio packet decode	STM32	10ms	Lost telemetry
IMU fusion	STM32	1ms	Drift in position
GPS parsing	STM32	100ms	Position lag
UI frame render	i.MX 8M	16.6ms (60fps)	Stuttering map
AI inference (optional)	Jetson	50ms	Delayed detection

Scheduling: STM32 runs FreeRTOS with rate-monotonic scheduling. i.MX runs Linux with PREEMPT_RT patch for UI tasks.
## 6. AI Integration (Optional but Powerful)
If you add the Jetson Orin Nano Super, implement:
Model	Task	Performance
YOLOv8n (quantized)	Drone detection in camera feed	45ms @ 640x640
1D-CNN	RF signal classification	4ms on STM32
ResNet-18	Target identification (vehicle vs person)	25ms

Without Jetson: The i.MX 8M Plus NPU runs MobileNetV2 at 15fps – enough for basic person detection, not drone tracking .
## 7. Networking & Security
Layer	Mechanism	Implementation
Link	AES-128 (LoRa)	SX1278 hardware crypto
Transport	TLS 1.3 (Ethernet)	mbedTLS on i.MX
Application	MAVLink signing	SHA-256
Boot	Secure boot (i.MX HAB)	Prevents firmware tampering
Anti-jam	Frequency hopping (LoRa)	Channel agility

For production: Add an Infineon OPTIGA TPM for key storage.
## 8. Deployment Strategy
Phase	Hardware	Purpose
Prototype	Raspberry Pi 5 + peripherals	Prove concept, iterate UI
Field Test	i.MX 8M Plus + STM32 + LoRa	Validate range, battery life
Production	Custom PCB (i.MX + STM32 on same board)	Ruggedize, reduce cost

OTA Updates:
- i.MX: SWUpdate (dual-copy)
- STM32: UART bootloader (via i.MX)
- Jetson: NVIDIA OTA (if used)
## 9. Testing & Validation
Test	Method	Pass Criteria
Range	LoRa 20km LOS test	Packet loss <5%
GPS jamming	Inject 1575MHz noise	Re-acquire <10s
Temperature	Thermal chamber (-20°C to +50°C)	No frame drops
Vibration	MIL-STD-810H (Method 514.7)	No connector loosening
UI responsiveness	Touch latency measurement	<50ms from touch to action

## 10. Limitations & Risk Analysis
Risk	Probability	Mitigation
LoRa congestion in urban areas	High	Implement adaptive data rate, listen-before-talk
GPS denied (jamming)	Medium	Fallback to IMU dead reckoning (drifts 1m/s)
i.MX 8M Plus overheating	Low	Passive heatsink + thermal throttle
Jetson power spike >25W	Medium	Supercapacitor bank + current limiting
Display glare	Medium	Anti-glare film + hood design

## 11. When to Choose Each Processor (Decision Matrix)
Your Priority	Primary Processor	Secondary
Lowest cost prototype ($250)	Raspberry Pi 5	STM32 for radio
Field deployable, no AI ($650)	i.MX 8M Plus	STM32
Drone detection + AI ($1000)	Jetson Orin Nano Super	i.MX 8M (UI) + STM32 (safety)
Ultra-low power (battery days)	STM32H7 (only)	None (no UI)
Ruggedized production	i.MX 8M Plus + STM32	Custom PCB